## Slide 1
Scope of AI/ML for NG-RAN in Rel-19
Agenda: 9.1.3.1
Source: Samsung
Document for : Discussion and decision

## Slide 2
Baseline Objectives from RAN Chair
RAN chair recently shared his summary for RAN Rel-19 Package in RP-232745.
In general, we are supportive on the summary, and observe there are several discussion points, especially the yellow-highlighted parts.
  6 months SI + 12 months WI
  Rel-18 leftovers (depends on Rel-18 outcome), e.g.:
    Mobility optimization
      - NR-DC
      - UE Trajectory prediction
    Energy saving
      - Prediction for energy cost
    Continuous MDT
  At least 1 At most 2 potential new use case/scenario which benefits from inference-based techniques
    Coverage and Capacity Optimization
    Potential Rel-18 use case enhancements (e.g. new scenarios for ES)
    QoE
    Slicing
    Note: Model training/inference at the DU and/or F1 enhancements must be justified by the use case
  Study: Consider available functionality specified in 5GC (NWDAF, MDAS) in order to align AI/ML framework between RAN and CN

## Slide 3
Potential new use cases
We support to study the new use cases of slicing and QoE.
Slicing
QoE
Slicing: network uncertainty and delayed reconfiguration may deteriorate the performance.
  Resource allocation: proper remapping policy to improve efficiency and satisfy QoS of UEs
QoE: relationship between QoE parameters and network related parameters is implicit.
  QoE prediction: varying-trend prediction of QoE for maintaining user experience
CCO:
With the AI/ML, the main enhancement is to support predicted CCO decision. The existing signaling can support predicted CCO policy exchange. Other part e.g. the model design is implementation. So there is no strong requirement for CCO.
Potential Rel-18 use case enhancements:
The new scenario for NES is mainly within the scope of RAN1 and RAN2. It is better to study the use case with impact mainly in RAN3.
  Proposal 1: Study new use cases of slicing and QoE in Rel-19.

## Slide 4
Coordination with CN
  For use cases i.e. mobility optimization, energy saving and load balancing, no coordination requirement is identified in Rel-18 (RAN3 reply LS in R3-237745).
  For R19, whether available functionality specified in 5GC is useful in RAN need to be discussed case by case. It’s not possible to evaluate this without considering use cases.
  The aim of AI/ML for NG-RAN is to optimize the policy in RAN in order to adapt to network variations (e.g. the dynamic change of radio quality), so the policy should be timely-optimized. The information from CN is non-real-time, which can not match with RAN requirement.
  The benefit of the coordination with CN is not solid.
  The requirement for the coordination with CN can be discussed case by case. There is no need to have a separate objective.
  Proposal 2: Remove the last highlighted bullet on the alignment between RAN and CN.

## Slide 5
Rel-18 Leftovers
Mobility enhancement:
  Support to study the NR-DC cases.
Multi-dimensionality HO brings high complexity and heavy overhead.
  Important parameters prediction: e.g. traffic, QoS performance to assist HO policy setting
  HO decision prediction: HO decision for DC to improve robustness
Continuous MDT:
  This topic was studied in the R17 SI, and there is no requirement identified.
  In R18, there is no identified parameter that must be collected from MDT. Several solutions were proposed to solve different issues, which are controversial and cannot be concluded.
  MDT is mainly beneficial for the case that training is located in OAM. In such case, OAM can get the training data from gNB directly.
  Proposal 3: Study Rel-18 leftover on Mobility enhancement.

## Slide 6
Proposal
Potential objectives:
  6 months SI + 12 months WI
  Rel-18 leftovers (depends on Rel-18 outcome), e.g.:
    Mobility optimization
      - NR-DC
      - UE Trajectory prediction
    Energy saving
      - Prediction for energy cost
    Continuous MDT
  At least 1 At most 2 potential Study following new use case/scenario which benefits from inference-based techniques
    Coverage and Capacity Optimization
    Potential Rel-18 use case enhancements (e.g. new scenarios for ES)
    QoE
    Slicing
    Note: Model training/inference at the DU and/or F1 enhancements must be justified by the use case
  Study: Consider available functionality specified in 5GC (NWDAF, MDAS) in order to align AI/ML framework between RAN and CN

## Slide 7
Thank you!