## Slide 1: Views on LP WUS for R19 WI
Xiaomi
3GPP TSG RAN Meeting #102 RP-233137
Edinburgh, Scotland, December 11-15, 2023

## Slide 2: Brief introductions for R18 SI
    The study on LP WUS and its receiver is summarized in TR 38.869
      LP WUS can be applied for eMBB/IoT and wearable cases, mainly for stationary and low/medium speed scenarios.
      Evaluations on power consumption/coverage have been done. LP WUS shows large power saving gain and its coverage performance is similar as PUSCH msg3 but worse than PDCCH.
      Waveform comparisons across OOK/FSK/OFDMA signals are completed. Based on discussion in RAN #101, OOK-1/4 and Harmonized design that accommodates OOK-1/OOK-4 and OFDM waveform got the most support.
      Receiver architectures for envelop detection/FSK and OFDMA based receiver are studied.
      Procedures for synchronization, RRM measurement, LP-WUS monitoring for RRC idle/inactive and RRC connected UE, (de)activation procedures of LP-WUS are studied.

## Slide 3: Essential topics for R19 WI- RAN1
Waveform
    Harmonized design that accommodates OOK-1/OOK-4 and OFDM waveform can be supported
      Based on discussion in RAN #101, Direction 1 and 2 got the most support. Direction 2, the harmonized design to accommodate OFDM and OOK-1/OOK-4, should be adopted since it will support both OOK-based and OFDM- based LP WUR without extra signals.
      OOK-1 is more robust to timing error, and of lower complexity compared to OOK-4, but with lower bit rate.
      If relatively small bitrate carried in LP WUS/LP-SS, OOK-1 is preferred compared with OOK-4.
Coverage
    For OFDM-based signal/receiver, the coverage performance is similar as other NR DL channels, and needs no coverage enhancement
    For OOK-based signal/receiver, simulation shows the coverage is similar as PUSCH msg 3, and worse than PDCCH. And coverage enhancement should be supported
      Robust coding, e.g., Manchester coding.
      Time domain repetition
      Power boosting
    For OOK-based receiver, if coverage imbalance exists between LP WUS and legacy NR channels, how to avoid ping-pang effect for UE switching between MR awake-Ultra sleep should be considered.

## Slide 4: Essential topics for R19 WI- RAN1
Synchronization
    For OFDM-based receiver, PSS/SSS can be reused. For OOK-based receiver, periodical LP-SS, is recommended.
        The periodicity of LP-SS can refer to the RSS in MTC, which is configurable to 160, 320, 640 and 1280 ms.
        With PSS/SSS or periodical LP-SS, LP WUR can stay sync with gNB and monitor LP WUS by duty cycle manner.
        LP-SS is cell specific, e.g. cell ID is carried, if supporting neighboring cell RRM measurement.
RRM measurement
    Serving cell RRM measurement based on PSS/SSS for OFDM-LP WUR receiver and LP –SS by OOK-LP WUR receiver should be supported.
    For OFDM-LP WUR receiver, neighboring cell RRM measurement should be supported.
    For OOK-LP WUR receiver, if after coverage enhancement, the LP-SS coverage is whole cell, neighboring cell RRM measurement can also be supported.
    Serving/neighbor cell RRM measurement by main radio can be relaxed, including partially/fully offloaded to LP WUR, for RRC idle/inactive UE.

## Slide 5: Essential topics for R19 WI- RAN1
LP WUS monitoring
    Duty cycle monitoring is preferred compared to always on monitoring, since it is more power saving and provide another dimension for UE subgrouping.
    LP WUS is transmitted by duty cycle manner, multiple LP WUS time occasions corresponding to different UE sub-group can be configured within a cycle.
Coexistence with other NR channels/signals
    LP-SS/WUS should be able to be multiplexed with other NR channels/signals of main radio in the same OFDM symbols.

## Slide 6: Essential topics for R19 WI- RAN1
Information carried
    For LP-WUS for RRC idle/inactive UE
      Different LP WUS monitoring occasions correspond to different UE groups, similar as PO.
      Within each MO, at least wake up indication for Paging DCI monitoring is indicated.
      At least UE sub-group ID is indicated, similar as PEI.
        Different or the same UE subgrouping method can be applied for LP WUS and PEI
    For LP-WUS for RRC connected UE
      UE specific configured monitoring occasions.
      A single LP WUS occasion can correspond to one or multiple UEs, with separate indication for each UE/UE subgroup
        UE subgroup is subject to gNB configuration
      UE will monitor LP WUS when MR is sleeping. At least wake up indication for PDCCH monitoring is indicated.

## Slide 7: Essential topics for R19 WI- RAN2
    For LP-WUS for RRC idle/inactive UE
      Procedures for UE entering/exiting of LP-WUS monitoring should be specified.
      Procedures for UE MR paging monitoring triggered by LP-WUS should be specified
Main receiver on
RRC IDLE/Inactive
Main receiver off
Operation on LP-WUS
Entry of using LP-WUS
Exit of using LP-WUS
UE behavior(s) during the ultra-deep sleep, FFS
AS layer procedures is not required to perform? E.g.,
how to receive SI change notification and/or ETWS/CMAS.
UE behavior(s) out of the ultra-deep sleep
Paging monitoring
RRM measurement

## Slide 8: Essential topics for R19 WI- RAN2
    For LP-WUS for RRC connected UE:
      Procedures for UE entering/exiting of the LP-WUS monitoring should be specified.
      Procedures for LP-WUS monitoring by LP-WUR and PDCCH monitoring triggered by LP-WUS, e.g., how LP-WUS works with C-DRX/PDCCH skipping/SSSG switching, should be specified.
      No impact on existing RRM/RLM/BFD/CSI measurements for MR.
PDCCH monitoring
RRC Connected
LP-WUS monitoring
Entry of using LP-WUS
Exit of using LP-WUS
UE behavior(s) by LP-WUS monitoring :
Stops PDCCH monitoring of MR
No impact on existing RRM/RLM/BFD/CSI measurements
FFS: LP-WUS impact on running timers, e.g., BWP IAT timer
FFS: LP-WUS impact on SPS and CG
UE behavior(s) out of LP-WUS monitoring
LP-WUS works with C-DRX, PDCCH skipping
e.g., LP-WUS co-exist with R16 DCP, LP-WUS triggers IAT timer directly

## Slide 9: Summary
  Proposal 1: RAN is suggested to consider the following objectives for Rel-19 LP-WUS WI:
Specify LP-SS and LP-WUS(RAN1): Specify harmonized design that accommodates OOK-1/OOK-4 and OFDM waveform for LP-WUS/LP-SS, including the information carried, occupied resources and multiplexing with legacy channels, that can be detected by LP-WUR. Specify coverage enhancement schemes for LP-WUS/LP-SS. For LP-WUS for RRC idle/inactive UE (RAN2, RAN1): Specify necessary procedures to allow UE enter/exit of the LP-WUS monitoring (RAN2, RAN1) Specify necessary procedures to allow UE MR (Main receiver) paging monitoring triggered by LP-WUS (RAN1, RAN2) For LP-WUS for RRC connected UE(RAN1, RAN2): Specify necessary procedures to allow UE enter/exit of the LP-WUS monitoring (RAN2, RAN1) Specify necessary procedures to allow LP-WUS monitoring by LP-WUR and PDCCH monitoring triggered by LP-WUS, e.g., how LP-WUS works with C-DRX, PDCCH skipping, SSSG switching(RAN1, RAN2) Specify necessary impact on configured resources in connected mode with LP-WUS (e.g. SPS CG); Note: No impact on existing RRM/RLM/BFD/CSI measurements for MR. For RRM measurement(RAN4, RAN2, RAN1): Specify further RRM relaxation of UE MR for both serving and neighbor cell measurements, including partially/fully offloading serving cell/neighbor measurements to LP-WUR, for RRC idle/inactive UE (RAN4, RAN2, RAN1) Specify UE RF and RRM core requirements (RAN4) Specify UE Rx RF requirement for the new features introduced in this WI Specify RRM core requirements for the new features introduced in this WI

## Slide 10: Thanks