## Slide 1: Proposal on network energy saving in Rel-19
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
Agenda Item: 9.1.1.5
RP-233155

## Slide 2: Potential Scope in RP-232745
RAN chair suggests the following as potential scope:
  On-demand SSB transmission for Scell for connected UEs
    Possible triggering methods (e.g., UE uplink wake-up-signal using an existing signal/channel, cell on/off indication via backhaul, Scell activation/deactivation signaling, etc.)
  On-demand SIB1transmission for idle UEs
    Possible triggering methods (e.g., UE uplink wake-up-signal using an existing signal/channel, cell on/off indication via backhaul, Scell activation/deactivation signaling, etc.)
  Others
    [SSB]/SIB1-less operation in multi-carrier scenario for (documented in TR38.864)
      [SSB]/SIB1-less for non-anchor NES cell for UEs in IDLE/INACTIVE state, where it is assumed that another carrier (an anchor cell) is available for the UE
    Adaptation of common signal/channel transmissions (documented in TR38.864)
    Specify Cell DRX/DTX for UEs in idle/inactive modes (as an extension of Rel-18 cell DRX/DTX)
    Multi-TRP adaptation mechanisms
    UE group-common or cell-specific BWP configuration, adaptation and/or switching.
    Group cell switch
    Power domains studied in R18 (techniques D-2 ~ D-5)
    Low-power SSB/SIB1/Paging
    Extension of spatial and power domain techniques in 1) high load scenarios 2) Type-II codebook types
    Semi-static beam-specific broadcast channel configuration
    Scenario 2a for SSB-less
    It was also mentioned that some proposals for multi-carrier enhancements may be beneficial for network energy savings (e.g. cross-carrier HARQ, fast DL carrier switch, multi-carrier CSI)
    Extensions to network-controlled repeaters (NCR), e.g. backhaul/control link behavior for efficient interaction between NES-capable gNB and associated NCR, to consider the case where the gNB would operate with S/P-domain adaptation or cell DTX/DRX adaptation for NW energy saving
We provide our view on objectives that are RAN1/RAN2-centric or involves non-trivial RAN1/RAN2 work

## Slide 3: Background
During Rel-18 NW Energy Saving (NES) SI phase, various T/F/S/P-domain NES techniques were studied, as enumerated below.
Considering impacts on legacy NR UEs and performance analysis, some NES techniques (i.e., B-1-1, A-4, C-1, and D-1 techniques) out of studied ones are included in Rel-18 NES WID.
Domain | Technique
Time | A-1: Adapting transmission/reception of common channels/signals A-1-1: Simplified SSB without PBCH or with partial PBCH A-1-2: Skipping of SSB/SIB1 transmission occasion A-1-3: Configuration/adaptation of longer periodicity of SSB/SIB1 and/or uplink random access opportunities A-1-4: Adapting paging or SSB transmission patterns A-1-5: Dynamically adapting PRACH periodicity and occasions A-1-6: Scheduling of SIB1 without PDCCH
 | A-2: Adaptation of UE specific signals and channels
 | A-3: UE wake up signal (WUS) for gNB A-3-1: UE WUS triggering gNB for SSB/SIB/RACH A-3-2: UE WUS triggering gNB to wake up in case of uplink traffic arrival
 | A-4: Adaptation of DTX/DRX
 | A-5: Adaptation of SSB/SIB1 A-5-1: SSB- and/or SIB1-less operation for non-CA A-5-2: On-demand SSB/SIB1
Domain | Technique
Frequency | B-1: Multi-carrier energy savings enhancements B-1-1: SSB- and/or SIB1-less operation for inter-band CA B-1-2: Dynamic UE-group PCell switching
 | B-2: Adaptation of bandwidth part of UE(s) within a carrier
 | B-3: Adaptation of bandwidth of UE(s) within a BWP
Spatial | C-1: Adaptation of spatial elements
 | C-2: Adaptation of TRPs in mTRP operation
Power | D-1: Adaptation of transmission power of signals and channels
 | D-2: Over the air digital pre-distortion
 | D-3: Tone reservation
 | D-4: PA power bias adaptation
 | D-5: UE post-distortion

## Slide 4: LGE view on potential scope
Potential objective in RP-232745
  On-demand SSB transmission for SCell for connected UEs
    Possible triggering methods (e.g., UE uplink wake-up-signal using an existing signal/channel, cell on/off indication via backhaul, Scell activation/deactivation signaling, etc.)
  On-demand SIB1 transmission for idle UEs
    Possible triggering methods (e.g., UE uplink wake-up-signal using an existing signal/channel, cell on/off indication via backhaul, Scell activation/deactivation signaling, etc.)
Based on Tdocs submitted to RAN#101, SSB/SIB1-less or on-demand SSB/SIB1 operations (i.e., A-1, A-3, and A-5 techniques) can be categorized as follows:
Category | SSB and/or SIB1-less | On-demand SSB/SIB1 | UE status
Cat-1 | SSB-less operation limited to SCell | With on-demand SSB | RRC_CONNECTED
Cat-2 | SSB-less operation limited to SCell (e.g., for fast SCell activation) | Not needed | RRC_CONNECTED
Cat-3 | SSB/SIB1-less operation with single-carrier scenario | With on-demand SSB/SIB1 | IDLE (or INACTIVE)
Cat-4 | SSB/SIB1-less operation with multi-carrier scenario (e.g., SSB/SIB1-less operation for non-anchor carrier) | With on-demand SSB/SIB1, if needed | IDLE (or INACTIVE)
Cat-5 | SSB/SIB1-less operation with multi-carrier scenario (e.g., SIB1 for non-anchor carrier to be transmitted on anchor carrier and NOT on non-anchor carrier) | Not needed | IDLE (or INACTIVE)

## Slide 5: LGE view on potential scope
LGE view
  Among five categories, Cat-1 can be considered in Rel-19, taking account of:
    Design/configuration of UL signal/channel to request on-demand SSB
    Procedure for on-demand SSB operation
  For other categories,
    Justification for the relevant scenarios should be further identified
    Impacts on legacy UEs should be carefully investigated.
  Particularly, for on-demand SIB1 transmissions (i.e., Cat-3 to Cat-5),
    On-demand SIB1 transmission for idle mode requires huge discussion on cell selection, cell reselection, essential SIB, other SIB as assistance info, etc. in RAN2 as SIB1 is quite essential. Corresponding specification impacts would be quite big.
    It is not clear if achievable NES gain with on-demand SIB1 transmission can be justified.
  Those presented as possible triggering methods (marked as green in previous slide) are too unclear to be specified in objective unless they are further clarified and reworded.
    It is ambiguous how cell on/off indication is related and how Scell act/deac signaling is related.
    Unless the objective indeed intends to limit solution candidates already, the detailed signaling should be discussed and decided in normative phase.

## Slide 6: LGE view on “Others”
Rel-18 NES WI introduces spatial domain techniques focusing on single TRP operation.
For adaptation of TRPs in multi-TRP operation (C-2 technique),
  Substantial network energy saving gain has been shown during NES SI phase.
  As captured in TR 38.864, no impact for legacy UEs is foreseen if the adaptation technique is used on a UE-specific basis.
LGE view
  To enable efficient adaptation of TRPs, the enhancements of CSI, TCI, beam management and repetition related procedures can be considered in Rel-19.
Multi-TRP operation with enhanced NES

## Slide 7: LGE view on “Others”
LGE view
  We do not support introducing “group cell switch” via common signaling
    NES gain of the group cell switch is questionable. R18 NES CHO condition and R19 NES CHO enhancements as we propose is more generic and useful.
    Group cell switch via common signaling has large specification impact and serious consideration including security aspect.
  We do not support introducing anchor cell concept for multi-carrier operation
    The concept of anchor cell unnecessarily complicates UE behaviors to very high extents but its exclusive benefit/ necessity is quite unclear.
  We do not support specifying Cell DRX/DTX for UEs in idle/inactive modes
    For UE in idle/inactive modes,
      if network wants to bar legacy UEs while admitting Cell DTX/DRX capable UEs, it is sufficient to set cellBarred in MIB as barred while setting R18 NES specific access barring bit as notBarred.
      Else if network admits legacy UEs as well, it should react as legacy gNB for any UE in idle/inactive, regardless of whether the UE is Cell DTRX capable or not (paging, RACH, etc). No further optimization is useful for NES gain.

## Slide 8: Additional RAN1 centric objective
In addition, the following Rel-18 leftover items can be considered in Rel-19.
  CSI overhead/complexity reduction
  TCI configuration enhancement
  Beam management enhancement
  PUCCH resource adaptation based on activated sub-configurations

## Slide 9: Additional RAN2 centric objective
R18 Mobility enhancement for NES
  In Rel-18, RAN2 enhanced CHO for Cell DTX/DRX NES use case.
    CHO condition specific to Cell DTX/DRX can be configured to UE. UE can execute the CHO condition, if satisfied, only after it receives NES CHO activation indication included in DCI 2-9 indicated for Cell DTX/DRX activation.
  During Rel-18, RAN2 acknowledged that Cell-Off use case is considered important for maximizing NES gain. However, the R18 CHO enhancement cannot cover Cell-Off use case, due to the limitation:
    DCI 2-9 have a single bit indication of NES CHO activation, rather then two bit indications covering both Cell DTX/DRX and Cell-Off.
    NES CHO condition has a flag of a single code-point to indicate that the condition is Cell DTX/DRX-specific, rather than having two separate flags covering both Cell DTX/DRX and Cell-Off.
To better support Cell-Off with CHO, we propose
    To include objective “enhance CHO to support Cell-Off-specific CHO condition”
    Potential specification impact to support Cell-Off-specific CHO condition is straightforward and small;
      The minimum would be to introduce variant of DCI 2-9 indicating two CHO activation bits and to introduce a flag in CHO condition to indicate that the condition is Cell-Off-specific.
    Failure recovery due to no CHO

## Slide 10: Proposal on network energy saving in Rel-19
SSB-less operation with on-demand SSB for SCell of RRC-connected UEs
  Design/configuration of UL signal/channel to request on-demand SSB
  Procedure for on-demand SSB operation
CHO enhancement for Cell-Off use case
  CHO condition specific to Cell-Off, DCI 2-9 extension
Dynamic TRP adaptation (on/off) mechanism for NW energy savings in multi-TRP operation
  Enhancements of CSI, TCI, beam management and repetition related procedures to enable efficient adaptation of TRPs
Leftover issues of Rel-18 NES
  CSI overhead/complexity reduction
  TCI configuration enhancement
  Beam management enhancement
  PUCCH resource adaptation based on activated sub-configurations