## Slide 1: Views on Rel-19 Mobility Enhancements
RP-233239
Agenda Item: 9.1.2.1 Mobility enhancements
Source: Xiaomi
Document for: Discussion
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
1

## Slide 2: Introduction
In Chair’s summary for RAN Rel-19 Package[1], the following potential objectives are provided:
In the contribution, I will provide our views for these potential objectives.
[1] RP-232745 Summary for RAN Rel-19 Package: RAN1/2/3-led

## Slide 3: Inter-CU Layer 2 Mobility (LTM)
Motivation
  LTM has been supported to achieve fast inter-cell mobility with low interruption. And the sequential L1/L2 cell change between candidates without RRC reconfiguration has been supported in Rel-18 LTM.
  In Rel-18, only intra-DU LTM and intra-CU inter-DU LTM are supported.
  In Rel-18, LTM for simultaneous PCell and PSCell change is not supported in Rel-18.
Potential working scope
  To specify support for inter-CU Layer 2 Mobility (LTM):
    Rel-18 intra-CU LTM is used as the baseline;
    The procedure of inter-CU LTM are applicable to the following scenarios:
      Non-DC case (standalone and CA): inter-CU LTM for MCG change;
      NR-DC case: inter-CU LTM for SCG change; inter-CU LTM for simultaneous MCG and SCG change;
    CU-CU interface signalling to support inter-CU LTM;
    To avoid key reuse for the subsequent inter-CU LTM, including LTM for MCG change and LTM for SCG change.

## Slide 4: Measurements related enhancements for LTM
Motivation
  In Rel-18 L1 measurement report, periodic report on PUCCH, semi-persistent report on PUCCH and PUSCH and aperiodic report on PUSCH are supported. But event triggered report for L1 measurement is not supported.
  In Rel-17 ICBM, CSI measurement for candidate cell(s) is supported. But, only SSB-based measurement and reporting for candidate cell is allowed before LTM in Rel-18.
  In Rel-18, only L1-RSRP as the measurement quantity is supported for L1 measurement.
  In Rel-18, UE-based filtering to the L1 measurement results is not supported.
  In Rel-18, s-Measure does not apply to L1 LTM related measurements.
Potential working scope
  To specify measurements related enhancements for purpose of supporting LTM：
    To specify event triggered L1 measurement reporting for triggering LTM:
      To specify events for L1 measurement reporting;
      To specify the reporting resource for event triggered L1 measurement reporting;
      To specify the reporting format for event triggered L1 measurement reporting ;
    To specify CSI-RS measurements for LTM procedures and enable CSI-RS based beam management;
    To support L1-SINR as the Measurement quantity for L1 measurement reporting;
    To specify UE-based filtering to the L1 measurement results;
    To specify the conditions for the controlling of L1 measurements on LTM candidate cells:
      To define the threshold based on L1/L3 measurement results, e.g. similar to s-Measure.

## Slide 5: Subsequent conditional mobility
Motivation
  In Rel-16 and Rel-17, CHO and CPAC have been introduced to improve the robustness and UE should release stored all conditional configurations after successful completion of SpCell change procedure.
  In Rel-18, to reduce signalling overhead and interrupting time, the selective activation of the cell groups has been discussed. In selective activation of the cell groups, UE should keep conditional configurations after SpCell change for subsequent mobility without RRC reconfiguration. In Rel-18, the selective activation of the cell groups focuses on SCG and there‘s no time for MCG. And the terminology of the selective activation of SCG is “subsequent CPAC”.
  Rel-18 LTM can only be triggered by network command and conditional based LTM is not supported.
  In Rel-18, the LTM candidate configuration is not able to be used for CHO/CPAC, and the CHO/CPAC candidate configuration is not able to be used for LTM. However, both the CHO/CPAC candidate configuration and the LTM candidate configuration can be described by the RRCReconfiguration message
Potential working scope
  To specify mechanism and procedures of subsequent conditional mobility:
    Conditional LTM:
      To specify execution conditions based on L1/L3 measurement;
      Early TA acquisition enhancements for the RACH-less based LTM;
    Subsequent CHO in non-DC and NR-DC and the procedure of subsequent CHO is applicable to the following scenarios:
      Subsequent CHO with/without SCG change;
      Subsequent CHO with candidate SCGs for subsequent CPAC;
    A harmonized RRC modelling approach for LTM and conditional L3 mobility with the ability for subsequent mobility can be considered:
      To allow LTM candidate configurations used for CHO/CPAC procedure;
      To allow CHO/CPAC candidate configurations used for LTM procedure.

## Slide 6: Conclusion
Proposal: The following objectives can be considered for Mobility Enhancements in Rel-19
  To specify support for inter-CU Layer 2 Mobility (LTM):
    Rel-18 intra-CU LTM is used as the baseline;
    The procedure of inter-CU LTM are applicable to the following scenarios:
      Non-DC case (standalone and CA): inter-CU LTM for MCG change;
      NR-DC case: inter-CU LTM for SCG change; inter-CU LTM for simultaneous MCG and SCG change;
    CU-CU interface signalling to support inter-CU LTM;
    To avoid key reuse for the subsequent inter-CU LTM, including LTM for MCG change and LTM for SCG change.
  To specify measurements related enhancements for purpose of supporting LTM：
    To specify event triggered L1 measurement reporting for triggering LTM:
      To specify events for L1 measurement reporting;
      To specify the reporting resource for event triggered L1 measurement reporting;
      To specify the reporting format for event triggered L1 measurement reporting ;
    To specify CSI-RS measurements for LTM procedures and enable CSI-RS based beam management;
    To support L1-SINR as the Measurement quantity for L1 measurement reporting;
    To specify UE-based filtering to the L1 measurement results;
    To specify the conditions for the controlling of L1 measurements on LTM candidate cells:
      To define the threshold based on L1/L3 measurement results, e.g. similar to s-Measure.
  To specify mechanism and procedures of subsequent conditional mobility:
    Conditional LTM:
      To specify execution conditions based on L1/L3 measurement;
      Early TA acquisition enhancements for the RACH-less based LTM;
    Subsequent CHO in non-DC and NR-DC and the procedure of subsequent CHO is applicable to the following scenarios:
      Subsequent CHO with/without SCG change;
      Subsequent CHO with candidate SCGs for subsequent CPAC;
    A harmonized RRC modelling approach for LTM and conditional L3 mobility with the ability for subsequent mobility can be considered:
      To allow LTM candidate configurations used for CHO/CPAC procedure;
      To allow CHO/CPAC candidate configurations used for LTM procedure.

## Slide 7: Thanks
Xiaomi