## Slide 1
0
Views on Rel-19 Ambient IoT
December 2023
3GPP TSG RAN #102 RP-233420
Edinburgh, GB, December 11-15, 2023
Agenda Item: 9.1.1.4
Source: CMCC
Type: Discussion

## Slide 2
Motivation and use cases for Ambient IoT
Motivation and high value use cases
Huge demands for industries on tracking and monitoring which current RFID still cannot meet.
Ambient IoT is expected to enable billions of cellular new connections, by solving the bottleneck of conventional RFID, including limited coverage, high cost of deployment and maintenance, not supporting positioning and wide-area deployment.
As a competitive technology, IEEE 802.11 WG is now working on Ambient Power Communication to support battery-less and maintenance-free devices and will finish WI in Mar 2026. Once we miss the opportunity window, we will never have a second chance in 5G-A or 6G.
Therefore, let’s seize the opportunity promptly and unlock 5G-A new capability and value for billions connections.
Observation 1: We should deliver Ambient IoT as 5G-A key technology ASAP (i.e., specified in R19).
Inventory in factory
Scenario：Low-cost indoor factory inventory and positioning for large amount of materials
Requirement：Indoor NLOS coverage 20m, positioning accuracy ~2m, 0.02$ per tag
Wide area logistics tracking
Scenario：110.58 billion packets delivered in 2022, China. Requiring low-cost outdoor logistics tracking and positioning
Requirement：outdoor coverage 200m, positioning accuracy ~2m
Medicine & vaccine monitoring
Scenario: Temperature monitoring for medicine & vaccine
Requirement: indoor NLOS coverage 20m, supporting temperature sensing
Retailer
Scenario: 40 billion shoes and clothes sold in 2022, China. Requiring life-cycle management for production and retailer
Requirement：Outdoor coverage 200m, indoor coverage 20m，positioning accuracy~2m
Livestock management
Scenario: 10 billion livestock consumed in 2022, China. Requiring livestock access inventory, temperature monitoring
Requirement: Ourdoor coverage 200m, indoor 20m, support temperature sensing
High voltage substation monitoring
Scenario: Temperature monitoring, replacement of currently handheld infrared thermometer
Requirement: Outdoor coverage 200m, support temperature sensing

## Slide 3
Formulate a proper scope (1/2)
The workload for Device A/B/C are analyzed as follows:
Device A
  Aim at the device with ~1μW power consumption, backscattering transmission
  Study and specify necessary physical layer aspects, include waveform/numerology/modulation/frame structure/coding, basic DL/UL physical channels, necessary L1 procedures
  Study and specify necessary L2/L3 control plane and user plane, include access procedures, paging, security, UP protocol stack and packet structure
Device B
  Aim at the device with ~100uW power consumption, backscattering transmission. Comparing with Device A, only introduce higher capacity and amplifier
  Study additional aspects on top of Device A
Device C
  Aim at the device to achieve much higher link budget than Device A, with 1~10mW power consumption, active RF device. The physical design and L2/L3 design for Device C would be different with Device A
  Device C should be analyzed to verify that the cost and power consumption is much lower than the existing NB-IoT (~100mW) and eMTC technologies, and thus is not to be a replacement for them.
  The SI objectives for Device C are similar with Device A, but the design targets are different.
Observation 2: Device A & B can share the same design, while Device C may have different design with Device A. It is real mission impossible to study them all in one release, even without considering normative work for any kind of device in Rel-19. So, down-scoping in Rel-19 is needed, e.g., study Device A&B only and further check if it is feasible to have corresponding normative work in Rel-19, while have a separate SI for Device C in future release.
Device type

## Slide 4
Formulate a proper scope (2/2)
Both options are able to fit into R19 SI + WI
  Option 1: Only focus on Device A&B
  Option 2: Only focus on Device C
Considering the strong interests from industrial for Device A&B, we propose to focus on Device A&B for Rel-19
Proposal 1: Focus on Device A and B for Rel-19.
Device type
Topology 1 has the basic function among all others. It is common interests from all companies.
Topology 2 can compensate the coverage limitation for device A&B in topology 1, with additional work for relay related CP/UP design.
The scope for topology 2 may focus on the following aspects for layer-2 relay and layer-3 relay [RAN2]:
  Impact on CP procedure, e.g., connection control, paging, ambient link resource allocation and scheduling
  Impact on UP protocol stack, e.g., relay node protocol stack, packet formats
  The study on authorization and security may have dependency on SA2 and SA3 progress
Topology 3 can support wide area asset tracking for the ambient IoT devices by proximity intermediate node, while with additional work:
  Coordination among A-IoT Reader’s Tx and Rx over the air for topology 3
Observation 3: Device A&B + topology 2 can meet some of the scenarios that the Device C designed for, while Device C is not suitable for scenarios that Device A&B designed for.
Topology

## Slide 5
Highlight
Good business and deployment prospects
Timeline: Strong interests from industrial, to meet the demands of vertical customers more expeditiously, by the end of 2025 Q4.
SI/WI: A follow up WG SI/WI is expected to start in Rel-19 with 12 month SI (2024) + 6 month WI (2025 H1)
Target: The new IoT technology shall provide cost and power consumption much lower than the existing NB-IoT and eMTC technologies, and thus is not to be a replacement for them.
Deployment
  All standalone, in-band and guard-band operation can be considered. (Annex 1)
  Prioritize FR1 FDD
Device type
  Device A/B will be checked in Dec’24 for potential WI
Use cases: for Rel-19, inventory can be considered as basic use case, while it can also work for sensor and activator/command. Study of positioning is of interests.
Proposal 2: Check point in Dec’24 for conversion to Rel-19 Ambient IoT WI for Device A&B. Other device type can be further addressed in future release.
Highlight points for R19 SI/WI

## Slide 6
Work plan
6
SA1
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Rel-18
R18 L1 Start
R18 R1
Func. Freeze
R18 R2/3/4
Func. Freeze
R18 ASN.1
Freeze
Rel-19
Q1
Q2
Q3
R19 R2/3/4
Func. Freeze
R19 R1
Func. Freeze
2023.9 R19 L1 Start
SA1 R19 SI: Study on Ambient power-enabled Internet of Things
Start@SA1#97
R18 A-IoT RAN level SI
R19 A-IoT SA2 SI or SI+WI
RAN
SA2
R19 A-IoT RAN1/2/3/4 SI
RAN WG
Complete before Jun 2023
A-IoT RAN1/2/3/4 WI
2022
2023
2024
Approved@RAN#97
TBD
TBD
2025
12 month SI + 6 month WI in Rel-19. Focus only on the common and basic functions for passive device. The benefit is to meet the urgent market requirement in 2025.
  Proposal 3: We propose to have 12 month SI + 6 month WI in Rel-19, focusing on the basic and common design for inventory use case, passive device (A & B) and common ambient-link air interface for topology 1&2 first.
Check point

## Slide 7
Ambient IoT SI/WI Objectives
7
Identify evaluation methodology and KPIs based on RAN design target (SI only, RAN1)
  Target power/coverage/sensitivity/battery life for each device type
  Evaluation methodologies and results to be provided, including performance and coverage evaluation by considering appropriate scenarios/topology, impairment model and to analysis whether the AIoT can satisfy the coverage target.
Device hardware architecture(SI only, RAN1/RAN4)
  Device architecture for each device type
Study and specify necessary physical layer aspects, focusing on the basic and common design for inventory use case, passive device and common ambient-link air interface, including (RAN1/RAN2)
  Waveform/numerology/modulation/frame structure/coding
  Basic DL/UL physical channels
  Necessary L1 procedures
Study and specify necessary L2/L3 control plane and user plane for passive device, including (RAN2)
  minimum CP functions, e.g., access control, paging, security, mobility management
  minimum UP protocol layer and procedures, e.g., protocol stack, random access, packet structure
  mechanism(s) to support topology 2 (BS ↔ intermediate node ↔ AIoT device), focusing on the CP procedures and UP protocol stack for layer-2 relay and layer-3 relay
Study on the RAN architecture, including either gNB or UE act as reader, with/without CN connection (RAN3)
Coexistence with UEs and infrastructure with existing 3GPP technologies, e.g., LTE, NR, NB-IoT (RAN4/RAN1)
Study and specify necessary enhancement to support A-IoT device measurement based on LP-SS, at least for serving-cell (RAN4/1/2)
  Measurement accuracy and criteria (RAN4)
  Necessary procedures to support measurement (RAN2)
Note: the followings are considered in the study item,
  Device type A&B
  Topology 1&2
  FDD spectrum is prioritized for study
  Both spectrum in-band to NR, in guard-band to LTE/NR, and in standalone band(s) are considered

## Slide 8
Thank you!

## Slide 9
Annex 1: Spectrum and deployment
Spectrum and deployment
The following operations flexible deployment are to be considered,
  Mode A (in-band operation): Frequency bands in licensed spectrum, coexistence with UEs and infrastructure in frequency bands for NR
  Mode B (standalone operation) : Frequency bands in licensed spectrum, standalone operation in a narrow BW outside the NR carrier.
    Mode B-1: no additional GB needed among A-IoT CCs
    Mode B-2: additional GB needed among A-IoT CCs
  Mode C (guard-band operation): Frequency bands in licensed spectrum, standalone operation in a narrow BW in the guard-band of NR.
Proposal： Both standalone (with/without additional GB among CCs), in-band and guard-band operation in licensed spectrum is supported. FDD is prioritized for the study.

## Slide 10
Annex 2: Specification impact for topology 2
Motivation for common ambient-link design for topology 1&2
  The main benefit for topology 2 is to compensate the coverage limitation for topology 1.
  Ambient IoT devices are complexity, power and cost sensitive.
  It is device complexity, power and cost friendly if one type of device can be compatible to both topology 1 and 2
  Proposal: Topology 1 and 2 should share common Ambient-link design as much as possible, especially for layer 1 design. Whether the topology 1 and 2 can be totally agnostic to AIoT devices is FFS.
  In addition, for both topology 1&2, whether to introduce a separate CW node to support FDD transmission for device A can be studied in SI phase
Topology 2 specific study scope
  Study mechanism(s) to support topology 2 (BS ↔ intermediate node ↔ AIoT device), focusing on the following aspects for layer-2 relay and layer-3 relay [RAN2]:
    Impact on CP procedure, e.g., connection control, paging, ambient link resource allocation and scheduling
    Impact on UP protocol stack, e.g., relay node protocol stack, packet formats
    The study on authorization and security may have dependency on SA2 and SA3 progress
Device Types and Topologies
Topology 1
Topology 2
Intermediate node
AIoT R2T
CW
Backscatter or active signal for T2R
Uu interface
AIoT devices
AIoT devices

## Slide 11
Annex 3: Proximity assisted A-IoT communication to extend coverage
11
UE / Relay involvement (i.e., topology 3) is of interests for the following considerations,
Wide area asset tracking for the ambient IoT devices by proximity intermediate node (e.g., UEs/Relays)
Requires less complexity/UE power consumptions of the ambient IoT devices, such as the energy harvesting from proximity UEs/Relays.
Topologie 3 and scenarios
 | Energy harvesting | Downlink data | Uplink data | 
 |  |  | Incident signal | Backscatter signal
Topology 3a | Proximity UEs/Relays send CW1 in UL spectrum for ambient IoT device energy harvesting purpose | IM->AIoT@UL, need gNB->IM@DL for controlling/triggering | IM->AIoT@UL | A-IoT->gNB@UL
Topology 3b |  | gNB->AIoT@DL | gNB->AIoT@DL | AIoT->IM@DL, Need IM->gNB@UL for reporting
Note: IM: intermediate node, AIoT: Ambient IoT device

## Slide 12
Annex 4: New features for A-IoT in mobile network
12
Coverage improvement - Power pooling and multiple site
The following coverage target can be considered
Device B/C, target for comparable coverage to the current NR bottleneck. Tradeoff between coverage and complexity/power consumption is necessary.
Device A, strive for good coverage for topology 1 as much as possible and good proximity coverage for topology 2 (30~50 meter)
Multiple site (gNB/TRP)
Mainly used for RF energy harvesting coverage improvement purpose when there is not lots of site coordination/backhauling
Can be used for data coverage boosting if sufficient site coordination exists.
Power pooling
Study the gNB power pooling techniques to boost the coverage of the both RF energy harvesting and data receiving coverage
  Note: the data rate and latency may be degraded due to longer time to harvesting energy and Tx/Rx data.
Energy harvesting
Optimize energy harvesting procedure to enable communication protocol matching with A-IoT device energy storage/discharge
Assistant information of tag status reporting, e.g., state of charge,…
Mobility
Necessary enhancement to support A-IoT device measurement based on LP-SS, at least for serving-cell
  Evaluate LP-RSRP/RSRQ accuracy
  Necessary procedures to support measurement
Proposal: Study and specify the following aspects for A-IoT at least for device A/B
  Study the gNB power pooling techniques to boost the coverage of the both RF energy harvesting and data receiving coverage
  Energy harvesting procedure to enable communication protocol matching with A-IoT device energy storage/discharge and related assistant information.
  Necessary enhancement to support A-IoT device measurement based on LP-SS at least for serving-cell
  Single site operation is baseline, and multiple site (gNB/TRP) operation can be considered.

## Slide 13
Annex 5: Link Budget estimation
 |  | RFID | Device A | Device B | B类 半无源标签 | Device C
 | Energy storage | ~nF capacity | ~nF capacity | ~uF capacity | 100uF~mF capacity | Capacity
 | Energy source and RF capability | RF powered+ backscatter | RF powered+backscatter | RF powered+backscatter | Ambient powered+backscatter+sensor | active RF+ sensor
 | Cost | 0.03~0.06$ | 0.03~0.06$ | 0.06$ | 0.3~0.5$ | 1~4$
 | Power consumption | 1uW | [≤ 1 μW] or [≤ 10 μW] | 1~100uW | 100~200uW | ≤ 1 mW to ≤ 10 mW
 | Data rate |  | 0.1kbps < AIoT lowest data rate << 5kbps < eIoT highest data rate |  |  | 
 | Scenario | Indoor | Indoor | Indoor factory | Indoor factory / outdoor | Indoor/outdoor
DL | BS TX power | 33dBm | 33dBm | 33dBm | 33dBm indoor / 43dBm outdoor | 43dBm (BS 2T)
 | BS antenna gain |  | 2 |  | 2 | 16dB
 | Multi-BS joint transmission gain | 6 | 6 | 3 | 3 | 
 | BS EIRP | 39 | 44 | 38 | 38 | 
 | Device activation or detection threshold | -24dBm | -24dBm | -30dBm | -45dBm | -80dBm (SNR=20dB)
 | DL link budget | 63dB | 65dB | 71dB | Indoor 89dB / outdoor104dB | 139dB
UL | Reflected power for A/B UL TX power for C | -22dBm | -30dBm | -36dBm | -45dBm | -10dBm@15kHz
 | Device reflection loss | -8dB | -8dB |  | 10dB (amplified) | 
 | BS receiver sensitivity (2R) | -92dBm | -116dBm | -116 | -116dBm | -133dBm
 | BS antenna gain |  | 2 |  | 2 | 16
 | UL link budget | 62dB | 80dB | 74dB | InF 89dB / outdoor 97dB | 139dB
 | LOS coverage | 17m | 24m | 46m | InF 315m / outdoor 418m | -
 | NLOS coverage | 14m | 20m | 37m | InF 244m / outdoor 101m | Outdoor 500m+

## Slide 14
Annex 6: Device AB coexists with legacy NR
Background
Device AB has lower power consumption and complexity requirements according to TR38.848
For Device A, the power consumption target during transmitting/receiving is ≤ 1 μW or ≤ 10 μW,
For Device B, the target during transmitting/receiving is such that:
  Device A power consumption ≪ Device B power consumption < Device C power consumption; or
  Device A power consumption ≤ Device B power consumption < Device C power consumption.
The device power consumption during transmitting/receiving for Device C is ≤ 1 mW to ≤ 10 mW.
Thus, RF ED (envelope detector) receiver would be more practical for device A & B.
Typically, RF domain filter (Matching Network) is larger than 10MHz or more for RF ED depending on carrier frequency
time
Legacy NR DL
A-IoT DL
time
Legacy NR UL
A-IoT UL
A-IoT DL occupied a wideband (e.g., RF filter size)
A-IoT UL backscatters a narrow BW signal (e.g., CW signal) by simple OOK. (the A-IoT occupied a narrow BW)
Interference scenarios:
Ambient IoT in FDD spectrum
aggressor | victim | OK to survive?
NR DL | A-IoT DL | Need to study
A-IoT DL | NR DL | OK
NR UL | A-IoT UL | Proximity UE UL Tx may impact A-IoT UL
A-IoT UL | NR UL | Device A OK Device B ?
Observation: RF ED is more practical for device A & B. Device A & B and NR coexistence in FDD spectrum needed FFS.