## Slide 1
0
CMCC views on Rel-19 RAN4 RRM topics
3GPP TSG RAN Meeting #102 RP-233431
Edinburgh, GB, December 11-15, 2023
Agenda Item: 9.1.4.3
Source: CMCC
Document for: Discussion

## Slide 2
General consideration
Enhancement WIs for RRM and measurement gap have been conducted for 3 releases, only essential enhancements that has clear benefits and potential deployment demand should be prioritized in Rel-19.
Based on above consideration, following topics are proposed for Rel-19 RAN4 RRM
  Enhancement for measurement gap
    Parallel measurement for NCSG
    L1 inter-frequency measurement
  Enhancement for RRM
    FR2 measurement delay reduction

## Slide 3
Measurement gap - parallel measurement for NCSG
Specify RRM requirements to support parallel measurements upon NCSGs collision
UE capability and/or network indication, if needed
Potential Objectives
In Rel-18 MG Enhancements WI, for case 2: NCSG and concurrent MGs (i.e., the network has provided UE with multiple measurement gap patterns where at least one gap pattern is a NCSG), parallel measurements upon NCSGs collision is not supported due to limited timeline
From deployment point of view, parallel measurements upon NCSGs collision could help to reduce the impact on throughput while maintaining the benifit of concurrent MGs. It is benificial to consider parallel measurements upon NCSGs collision
Motivations

## Slide 4
Measurement gap - L1 inter-frequency measurement
Specify RRM requirements to support L1 inter-frequency measurement with NCSG and L1 inter-frequency measurement with NeedforGap
Potential Objectives
In Rel-18 further NR mobility enhancements WI, L1 inter-frequency measurement with NCSG and L1 inter-frequency measurement with NeedforGap are not considered in R18 L1/L2 based inter-cell mobility
L3 and L1 measurement are coupled. NCSG and NeedforGap, which reduce the impact on throughput from measurement gap, are already supported for L3 measurement. Without supporting NCSG and NeedforGap for L1 measurement results in different type of MG for L3 and L1 measurement, which is not efficient. It is benificial to support L1 inter-frequency with NCSG and L1 inter-frequency with NeedforGap
Motivations

## Slide 5
RRM enhancement-FR2 measurement delay reduction
Define reduced delay requirements for FR2
  Reducing RX beam sweeping factor based on AI/ML based beam prediction, including:
      RRC_IDLE state and RRC_inacticve state
        Cell re-selection requirements
      RRC_Connected state
        handover delay
        Radio link monitoring, BFD, CBD,e.g. evaluation period
        SCell activation delay
        Cell identification requirements for inntra-frequency and inter-frequency measurements
Potential Objectives
It is observed that some of the FR2 RRM requirements allow excessively long delay with RX beam sweeping factor (e.g. for cell re-selection, the scaling factor (N1) could be up to 8 for FR2-1)
In Rel-18, for the use case of AI/ML based beam management, UE could predict beams in time/frequency domain. This approach is also helpful for UE to perform RX beam sweeping, the RX beam sweeping factor could be reduced or eliminated with AI/ML, the FR2 RRM long delay requirements could be reduced
Motivation

## Slide 6
Simulation results: RX beam sweeping factor reduction based on AI/ML solution
Observation
  With AI/ML, the Rx beam can be predicted by a subset of beams. For 8Tx/2RX to predict 32Tx/8RX, with top-3/1, the predict accuracy is above 90%. The RX beam sweeping factor (i.e. 8) could be reduced.
Set B is a subset of Set A
  Set A: 32Tx/8RX
  Set B:
    case 1: 8Tx/4RX
    case 2: 8Tx/2RX
Top-K/1: the percentage of “the Top-1 strongest beam is one of the Top-K predicted beams”

## Slide 7
THANK YOU！