## Slide 1: RAN4-led topics in Rel-19: RF & OTA
RP-233459
3GPP TSG RAN Meeting #102
Edinburgh, UK, 11th – 15th December, 2023
Agenda Item 9.1.4.2
Source: Nokia, Nokia Shanghai Bell

## Slide 2
Overview
UE RF
Priority topics for UE RF:
  MPR reduction for contiguous UL CA in FR1
  High-power UE Bands
  High-power UE CA/DC combinations
  Simplification of band combinations
BS RF
Priority topics for BS RF:
  Mask of “Expected EIRP” for upper-6GHz band
  OTA conformance testing enhancements
  BS RF specification simplification
Overall, the RAN4 RF package should be limited to a small number of essential, commercially relevant items

## Slide 3
MPR reduction for contiguous UL CA in FR1
A large margin exists between current MPR requirement values for contiguous intraband UL CA and what can be simulated or measured  Rel-19 offers an opportunity to revisit and improve MPR definition which can improve UL coverage
Expected outcome and benefits:
More efficient and frequent use of intra-band CA facilitates high UL data rates
How to get there:
Review the specified MPR values for intra-band uplink CA in the light of practical implementation
Determine reasonable MPR values for contiguous RB allocations in contiguous uplink intra-band CA
Enable enhancement with modified MPR signalling
The difference between
simulated MPR and specified MPR

## Slide 4
High-power UE Bands
High-power UE classes are useful for uplink coverage. Rel-18 had a basket for enabling additional high-power NR bands, but no basket existed for LTE.
 Priority areas for Rel-19 should be enabling High-power UEs
Expected outcome and benefits:
PC2 support for additional LTE and NR bands is beneficial for wide area deployments. Also, it is needed to enable PC1.5 CA/DC functionality.
How to get there:
Introduce a basket for PC2 LTE bands (RP-233183).
Additional areas to consider:
HPUE (PC1/PC2) for NTN is beneficial to compensate challenging link budget.
Single band PC2 support for RedCap small data transmissions (e.g. utilities).
38.101-1 Table 6.2.1-1: UE Power Class
36.101 Table 6.2.2-1: UE Power Class

## Slide 5
High-power UE CA/DC combinations
At RAN4#109, PC1.5 NR UL inter-band CA was introduced to the specification. This is achieved with 1+2 Tx (3 Tx work-item) which means the bands need either UL MIMO support and/or Tx diversity support. i.e. has to be a TDD band.
SAR/MPR issues for PC1.5 seems already addressed with the introduction of this UL configuration. PC2 is already in specification since beginning of Rel-18. Meaning there should not be additional work for 2 Tx.
 In Rel-19 an evolution of this is to add additional CA support, not excluding FDD
Expected outcome and benefits:
PC1.5 and PC2 support for additional LTE and NR band combinations is beneficial for higher data rate coverage in wide area deployments.
How to get there:
To achieve PC1.5 NR UL CA both bands or CCs (inter/intra-band) needs to be PC2.
To achieve PC1.5 UL EN-DC both LTE band and NR band needs to be PC2.
  Adding more LTE PC2 bands is discussed in previous slide.
Introduce a basket for PC1.5 UL NR CA and EN-DC (Maybe split into separate WIs)

## Slide 6
Simplification of band combinations
The number of band combinations is growing exponentially (now over 10,000) and are getting more and more complex with both the evolution of the UEs and addition of new spectrum.
In Rel-19 it is essential to formulate a more efficient way of handling band combinations in preparation for 6G
Expected outcome and benefits:
Some unnecessary workload has already been eliminated in RAN4 when defining band combinations by giving clear guidelines/rules on what needs to be studied and what can be simplified.
But there are still multiple areas/aspects to simplify:
  Currently there is a large number of band combinations with high MSD allowance. The UE is only tested according to test-points for the issues (IMD / receiver harmonic mixing) and normal operation is not verified. The operators could utilize the non-problematic part of the spectrum better, but this is currently not tested. RAN4 can investigate if the current MSD framework can be enhanced or modified to address this problem.
  How to get there:
  Start a Rel-19 WI building on the Rel-18 SI, keeping same TR 38.846.

## Slide 7
BS RF – Mask of “Expected EIRP” above horizon in the 6425-7125 MHz band
Regulatory requirement for a single BS for protecting co-channel FSS space receivers from aggregate interference
Coexistence with Fixed Satellite Service (FSS) space receivers
Limits take into account that BSs within the satellite footprint have different:
  Orientations in azimuth
  Elevation angles
  Beamforming directions
Technical conditions to be finalized at the ITU 2023 World Radiocommunication Conference (WRC-23) – 20 November to 15 December 2023
Vertical angle measurement window (vertical angle above horizon) | Expected EIRP (dBm/MHz)
0 5 | P1
5 10 | P2
10 15 | P3
15 20 | P4
20 30 | P5
30 60 | P6
60 90 | P7
 | Expected EIRP (dBm/MHz)
 | P1
 | P2
 | P3
 | P4
 | P5
 | P6
 | P7
“Expected EIRP” for a vertical angle window is the averaging of EIRP over these 3 domains

## Slide 8
BS RF – Mask of “Expected EIRP” above horizon
Need for reflecting the new metric and the resulting regulatory technical conditions in the BS RF core specifications
Need for developing a methodology for measuring the expected EIRP for conformance test purposes
  Define which aspects will be subject of manufacturer declarations
    Beam modes/configurations/characteristics
  Measurement setup
    Beam modes/configurations/characteristics (e.g. quantity, directions)
    Resolution of measurement points in azimuth and elevation
  Post-processing of measurements
    Weighting of different beam modes
    Averaging over azimuth, elevation and beam modes
BS RF core requirements and conformance testing

## Slide 9
BS RF – OTA conformance testing enhancements
3GPP OTA conformance tests take significant time and need to be improved for at least a number of test requirements:
  Transmitter Intermodulation
    For Radiated Conformance Testing, consideration of reduction of interferer offset from 6 (3 on each side of carrier) to TBD, which significantly reduce testing effort
  Out-of-band Blocking
    Consideration of increasement of interferer step size, to reduce measurement points and thus testing effort is reduced proportionally
  TRP measurements
    Introduction of new optimized TRP method or modification of some of existing ones
  Co-location
    For CLTA characteristics, consideration of modification of CLTA characteristics to allow wider range of antennas e.g. wider bandwidth, in order to reduce number of needed CLTAs for testing and hence reducing testing effort

## Slide 10
BS RF - BS specifications simplification
Any introduction of new 3GPP band requires changes in large number of BS specifications:
  36.104/141 (LTE)
  37.104/141 (MSR)
  37.105/145-1/145-2 (AAS)
  38.104/141-1/141-2 (NR)
  38.106/115-1/115-2 (Repeater)
  38.174/176-1/176-2 (IAB)
For most of specifications above, the change due to introduction of new band is related to co-existence and co-location requirements only
Simplification of specifications above would significantly reduce number of CRs due to introduction of new band as well as reduce RAN4 workload overall

## Slide 11
Summary
UE RF priority topics:
  MPR reduction for contiguous UL CA in FR1
  High-power UE Bands
  High-power UE CA/DC combinations
  Simplification of band combinations
BS RF priority topics:
  Mask of “Expected EIRP” for upper-6GHz band
  OTA conformance testing enhancements
  BS RF specification simplification
Overall, the RAN4 RF package should be limited to a small number of commercially relevant items