## Slide 1: Use cases for ISAC channel modeling
3GPP TSG RAN#102 RP-233487
Edinburgh, Scotland, December 11 – 15, 2023
Xiaomi, CAICT, China Unicom, Deutsche Telekom, Bell Mobility, TELUS, Spark NZ Ltd, ABS, Rakuten Mobile, LG Uplus, KT Corp., Reliance Jio, KPN, TCL, Inspur, Google, Nvidia, Denso, ITRI, Spreadtrum, Fraunhofer IIS, CEWiT, New H3C, ETRI, Meta, Toyota ITC, Sharp, Lenovo, UESTC, Rohde & Schwarz

## Slide 2: Moderator's summary on ISAC in RAN#101
Regarding ISAC, the following way forward seems agreeable:
    If not already done in SID, a RAN-led study objective to select a small number of ISAC use cases from TR 22.837, and to identify appropriate corresponding information needed for point 2 below, i.e. scenarios, frequency ranges and sensing modes.
    A RAN1-led study objective to define channel modelling details for sensing using 38.901 (if applicable to the selected use cases) as a starting point, and taking into account relevant measurements, including:
          modelling of sensing targets, including, for example (if needed by the selected use cases), radar cross-section (RCS), mobility and clutter/scattering patterns;
          spatial consistency.
          This objective to start after completion of the first (RAN-led) objective if not already done in SID

## Slide 3: Use case grouping from SA1
32 use cases are identified in SA1 TR 22.837, which covers a wide range of applications
  Object and intruder detection for smart home, on a highway, for railways, for factory, for predefined secure areas around critical infrastructure
  Collision avoidance and trajectory tracking of UAVs, vehicles, AGVs
  Public safety search and rescue
  Automotive maneuvering and navigation
  Rainfall monitoring and flooding
  Health and sports monitoring
In SA1 TS 22.137, the use cases in TR 22.837 are further grouped into 3 scenarios
  Object detection and tracking
    4 categories depending on the value range of different metrics
  Environment monitoring
  Motion monitoring

## Slide 4: Use case grouping from SA1
The mapping between TS 22.137 and TR 22.837 is given below:
Scenario | Sensing service category | Sensing service description in a target sensing service area | Related use cases (referring to TR 22.837)
Object detection and tracking | 1 | Indoor/outdoor (e.g., detection of human, UAV) | 5.1, 5.13 – level1
 | 2 | Outdoor (e.g., detection of human, UAV) | 5.13 – level2, 5.6, 5.14
 | 3 | Indoor/outdoor (e.g., detection and tracking of human, animal, UAV) | 5.2, 5.7, 5.10, 5.11, 5.12, 5.23
 | 4 | Indoor/outdoor (e.g., detection and tracking of human, animal, UAV, AGV, vehicle) requiring higher performance than category 3 | 5.20, 5.22, 5.25, 5.32
Environment monitoring | 5 | Nature of environments monitored by sensing (e.g. rainfall, flooding monitoring) | 5.3, 5.5
Motion monitoring | 6 | Human motions and activities obtained by sensing (NOTE 5) | 5.15, 5.24
 | 7 | Human hand gestures obtained by sensing (NOTE 6) | 5.29
TR 22.837: 7.2 Consolidated potential KPIs of sensing results
TS 22.137: Table 6.2-1: Performance requirements for 5G Wireless sensing

## Slide 5: Use case selection for channel modeling
The use case categorization in TS 22.137 can be used for the use case selection of the ISAC channel modeling, due to the commonality of the sensing use cases within the same category/scenario.
The ‘Object detection and tracking’ scenario can be used as a starting point for channel modeling, due to the commercial use and the potential commonality of channel modelling.
  Further down selection may/may not be needed among the 4 categories of the ‘Object detection and tracking’ scenario. The outdoor UAV scenario may have a simplified modeling for the environment. The modeling methodology (e.g. environment interference modeling) for other use cases of the following categories can be similar.
    Category 1: Indoor/outdoor (e.g., detection of human, UAV)
    Category 2: Outdoor (e.g., detection of human, UAV)
    Category 3: Indoor/outdoor (e.g., detection and tracking of human, animal, UAV)
    Category 4: Indoor/outdoor (e.g., detection and tracking of human, animal, UAV, AGV, vehicle)
The characteristics of ‘Environment monitoring’ scenario and ‘Motion monitoring’ scenario may/may not introduce extra complexities for channel modeling, depending on how to model the weather/motion (e.g. rainy weather or breathing motion). Given the increasing occurrence of weather related disasters, it is important to consider these use cases.
Proposal 1: The scenario ‘Object detection and tracking’ from TS 22.137 is used as a starting point for ISAC channel modeling.
Proposal 2: The ISAC channel model attempts to cover more use cases other than ‘Object detection and tracking’ as defined in TS 22.137.

## Slide 6: Frequency range, Sensing mode
Sensing modes
The channel modeling methodology for gNB mono-static and UE mono-static can be common.
The channel modelling methodology for gNB-to-gNB, UE-to-UE, gNB-to-UE and UE-to-gNB bi-static can be common.
The “Object detection and tracking” scenario in TS 22.137 can make use of both mono-static sensing and bi-static sensing.
The mono-static sensing and the bi-static sensing would require different implementation complexities, and lead to different commercial interests.
Further evaluation (e.g. on sensing accuracy) for both mono-static sensing and bi-static sensing is required based on the ISAC channel model.
Proposal 3: Study ISAC channel modeling for 0.5–100 GHz.
Proposal 4: Study ISAC channel modeling for both mono-static sensing and bi-static sensing.
Frequency range
0.5–100 GHz can be considered for sensing, depending on the use cases targeting at different coverage and accuracy by using different frequencies (e.g. wider coverage via FR1).
The ISAC channel modeling methodology (i.e. how to concatenate transmission link and reflection link) can be common for 0.5–100 GHz.
  The channel modeling study of near field and spatial non-stationarity (e.g. for 7–24 GHz) is separate, following moderator's summary RP-232617 in RAN#101.

## Slide 7: Conclusion
Proposal 1: The scenario ‘Object detection and tracking’ from TS 22.137 is used as a starting point for ISAC channel modeling.
Proposal 2: The ISAC channel model attempts to cover more use cases other than ‘Object detection and tracking’ as defined in TS 22.137.
Proposal 3: Study ISAC channel modeling for 0.5-100 GHz.
Proposal 4: Study ISAC channel modeling for both mono-static sensing and bi-static sensing.

## Slide 8: Annex
Potential objectives:
    The ISAC channel model attempts to cover the use cases in TS 22.137. The ‘Object detection and tracking’ use cases in TS 22.137 including the deployment scenarios of indoor/outdoor, 0.5-100 GHz and monostatic/bistatic sensing are selected as the starting point for the ISAC channel modeling.
    If not already done in SID, a RAN-led study objective to select a small number of ISAC use cases from TR22.837, and to identify appropriate corresponding information needed for point 2 below, i.e. scenarios, frequency ranges and sensing modes.
    Define channel modelling details for sensing using 38.901 as a starting point, and taking into account relevant measurements, including: [RAN1]
          modelling of sensing targets and background environments, including, for example (if needed by the selected use cases), radar cross-section (RCS), mobility and clutter/scattering patterns;
          spatial consistency.
          This objective to start after completion of the first (RAN-led) objective if not already done in SID

## Slide 9: Thank you