## Slide 1: Motivation on Scell with uplink only transmission
Source: KDDI, ZTE, Sanechips
Agenda: 9.1.4.4
RP-240058
3GPP TSG RAN Meeting #103
Maastricht , NL, Mar 18th-21th, 2024
RP-24xxxx

## Slide 2: Background
Scell with uplink only transmission has been discussed in the previous release, lots of merits and applicable use case as listed in following have been identified and well discussed. However, due to the workload and limited TU restrictions, RRM requirement for Scell with uplink only transmission has not been specified yet until Rel-18. In order to enable this feature with full set of requirements in RAN4, it’s proposed to define the corresponding RRM requirement for it in Rel-19.

## Slide 3: UE RRM related evolution in Rel-19
Justification:
In Japan, MIC had allocated the 700MHz band to the use of IMT systems and migrated the use of FPU systems to 1.2GHz and 2.3GHz bands.
MIC assigned the band 2330-2370MHz for the use of IMT system in 2022 and the operation of the IMT system in the band has started in 2023.
It's essential to protect the incumbent service FPU from the foreseen IMT deployment, otherwise IMT BS DL CLI towards to FPU receiver would be significant.
Scell with UL only transmission at 2.3GHz could mitigate the gNB to gNB CLI issue to enable the good coexistence performance with FPU.
Former FPU
Current spectrum for FPU
(1.2GHz band)
Current spectrum for FPU
(2.3GHz band)

## Slide 4: UE RRM related evolution in Rel-19
Justification:
In USA, there are long discussion on coexistence issue between IMT deployment at C-band and aircraft radio altimeter at 4.2-4.4GHz.
The FAA determined that radio altimeters cannot be relied upon to perform their intended function if they experience interference from wireless broadband operations in the 3.7-3.98 GHz frequency band (5G C-Band).
Scell with UL only transmission at 5G C-band could provide good solution to enable the good coexistence performance with aircraft radio altimeter if there are no additional filtering implemented for the protection of interference from IMT network at the aircraft.

## Slide 5: UE RRM related evolution in Rel-19
Justification:
With the deployment of NR network, operators may refarm some of the LTE bands to NR to improve UL coverage and throughput.
Re-farm bands for UL transmission might be possible given NR coverage is UL limited. An operator may use other higher NR bands for capacity and the re-farming LTE band for coverage.
Scell with UL only transmission can address such re-farming demands from operators.
Serving cell using the re-farming band from LTE
Serving cell using the existing NR band

## Slide 6: UE RRM related evolution in Rel-19
Justification:
Based on the study in Rel-18, UL only scell by shutting down the NW DL transmitter could achieve significant power saving. For BS Category 1, 65.5% to 71.7% of network power saving gain could be achieved and for BS Category 2, 80.7% to 83.3% of power saving gain could be achieved.
Scell with UL only transmission could provide further network energy saving enhancement.

## Slide 7: UE RRM related evolution in Rel-19
Justification:
In Rel-18, for the band combination of CA_n5-n8, options 2 & 3 are dropped and only option 1 will be considered.
Option 1: DL CA_n5-n8 with single UL in n5 only
Option 2: UL/DL CA_n5-n8 with non-simultaneous Rx/Tx between n5 DL and n8 UL
Option 3: UL/DL CA_n5-n8 with additional dedicated filter for the restricted frequency ranges for specific operator
Scell with UL only transmission could enable the operators to utilize the uplink spectrum in band n8 in addition to Rel-18 Option 1 solution.
Rel-18 solution for CA_n5-n8
Rel-19 complementary solution for CA_n5-n8

## Slide 8: UE RRM related evolution in Rel-19
To consider the Scell with UL only transmission in Rel-19 RAN4 RRM WID:
Objective:
To define the RRM requirement for Scell with UL only transmission [RAN4].
Potential RAN1/2 impact if any could be triggered by LS.