## Slide 1: Proposals on UE RF Topics for Rel-19
NTT DOCOMO, INC.
3GPP TSG RAN #103
Maastricht, Netherlands, March 18-21, 2024
Agenda Item: 9.1.4.1
Document for: Discussion
RP-240067

## Slide 2: Overview
During RAN#102, candidate RF&OTA topics were discussed and several topics were recommended for further discussions and down-selection
Based on the summary, we propose UE RF topics for Rel-19 RAN4 package as follows:
  FR1 3Tx requirements for handheld UE
    Can be discussed under HPUE related topic
  FR1 6Rx requirements for handheld UE
  FR2 MPR requirements improvement for intra band CA
    Our main motivation is “MPR reduction for FR2 independent from DL CBW”
  FR2 Intra+Inter UL CA with different frequency bands for PC1/2/3/5
    This topic was not discussed in RAN#102 due to time limitation

## Slide 3: FR1 3Tx requirements for handheld UE
Motivation
  For 3Tx, in Rel-18, 1Tx+2Tx requirements for FWA were introduced in Rel-18 WI (4Rx_low_NR_band_handheld_3Tx_NR_CA_ENDC). Study for 1Tx+2Tx for handheld UE is also the scope of the WI, but no normative work for handheld UE in Rel-18.
  Without 1Tx+2Tx feature, even if a UE supports UL MIMO in single carrier and NR UL CA, the UE can not enable UL MIMO and NR UL CA simultaneously due to the 2Tx limitation.

## Slide 4: FR1 3Tx requirements for handheld UE
Possible objectives
  Specify UE RF requirements to enable 3Tx for NR CA/EN-DC with two bands for handheld UE
    In each band only 1CC included. The Tx capability considered is 1Tx in one band, and 2Tx in the other band
    The following power capabilities will be considered
      CA power class or EN-DC power class is PC2
        Case 1: PC3 FDD band 1Tx + PC2 TDD band 2Tx (UL MIMO and TxD)
        Case 2: PC3 FDD band 1Tx + PC3 TDD band 2Tx (UL MIMO)
        Case 3: PC3 TDD band 1Tx + PC2 TDD band 2Tx (UL MIMO)
      CA power class or EN-DC power class is PC1.5
        Case 4: PC3 FDD band 1Tx + PC1.5 TDD band 2Tx (UL MIMO and TxD)
    Consider whether 3Tx requirements for FWA introduced in Rel-18 can be reused or not.
    Study and specify increase UE power high limit feature for CA power class PC2 and PC1.5
    Frequency band combinations considered in this WI are in the table below:
      #Example band combinations for case 3 and 4 can be discussed.
Band combination | UL configuration | Max Power capabilities
CA_n28A-n78A | CA_n28A-n78A | PC3@n28A 1Tx; PC3/2@n78A 2Tx; CA power class PC2
DC_3A_n78A | DC_3A_n78A | PC3@3A 1Tx; PC2@n78A 2Tx; EN-DC power class PC2

## Slide 5: FR1 6Rx requirements for handheld UE
Motivation
  For 6Rx, 4Rx for handheld UE has been introduced from initial release of NR specification (Rel-15). In Rel-18, 8Rx for FWA/CPE/Vehicle/Industrial devices was introduced in Rel-18 WI (NR_ENDC_ RF_FR1_enh2). 6Rx for handheld UE would be a reasonable extension.
Possible objectives
  Specify 6Rx requirements for handheld UE.
    Example bands: n77/n78/n79.
    Specify the UE RF requirements to support 6Rx for both single carrier and CA/DC
    Study and if needed, specify the requirements to support SRS antenna switching for t1r6, t2r6, t4r6
    6 DL MIMO layers is considered.

## Slide 6: FR2 MPR requirements improvement for intra band CA
Motivation
  Until Rel-18, MPR for intra-band CA is large and hence it is difficult to keep intra-band CA in practice (e.g., switching to single cell operation around cell edge).
  Moreover, FR2 CA MPR is currently defined based on not only UL CBW but also DL CBW (i.e., cumulative aggregated channel bandwidth), and thus 1UL/xDL CA operation needs large MPR. To avoid the large MPR, switching from 1UL/xDL CA to 1UL/1DL may be required.
  Due to such switching between intra-band CA and single cell operation, it is difficult to use joint scheduler for multi-cell scheduling instead of per-cell scheduler in practice.
Possible objectives
  Study and specify improved MPR for FR2 intra-band CA.
    Study, as one of the improved MPR solution, whether MPR for FR2 intra band CA can be defined based on only UL CBW (i.e., independent from DL CBW). Other solutions are not precluded.
    Target band combination is CA n257I.
UL
DL
UL CBW
DL aggregated CBW
Cumulative aggregated CBW(CABW)
→ MPR is defined based on CABW

## Slide 7: FR2 Intra+Inter UL CA with different frequency bands for PC1/2/3/5
Motivation
  FR2 Intra-band UL CA had been introduced from Rel-15, and already widely deployed in the market.
  During Rel-17 work, FR2 inter band UL CA with different frequency bands with 1CC in each band for PC1/2/3/5 was introduced(e.g., n257A+n259A).
  To enable higher peak rate, simultaneous operation of intra and inter-band CA is required.
Possible objectives
  Specify UE RF requirements to enable FR2 intra+inter band UL CA with different frequency bands with IBM
    Target power class: PC1/2/3/5
    Example band combination: n257I+n259M