## Slide 1
0
CMCC views on Rel-19 RAN4 RRM topics
3GPP TSG RAN Meeting #103 RP-240153
Maastricht, Netherlands, March 18-21, 2024
Agenda Item: 9.1.4.4
Source: CMCC
Document for: Discussion

## Slide 2
General consideration
Enhancement WIs for RRM and measurement gap have been conducted for 3 releases, only essential enhancements that has clear benefits and potential deployment demand should be prioritized in Rel-19
  Based on above consideration, following topic(s) are proposed for Rel-19 RAN4 RRM
    FR2 L3/L1 measurement delay reduction
For fast SCell activation with EMR, some issues are identified and suggestions are provided

## Slide 3
FR2 L3/L1 measurement delay reduction
Candidate solution 1
  FR2 L3/L1 measurement delay can be reduced by reducing RX beam sweeping factor based on AI/ML based beam prediction
    In Rel-18, for the use case of AI/ML based beam management, UE could predict beams in time/frequency domain. This approach is also helpful for UE to perform RX beam sweeping, the RX beam sweeping factor could be reduced or eliminated with AI/ML, the FR2 RRM long delay requirements could be reduced
Candidate solution 2
  FR2 L3/L1 measurement delay can be reduced by taking Rel-18 FR2 SCell activation delay reduction as baseline
    In Rel-18, reduced RX beam sweeping factor, e.g, X1 for cell detection and X2 for SSB based L1-RSRP measurement, is introduced for SCell activation delay reduction. Similar approach can be considered for FR2 L3/L1 measurement delay reduction
Candidate solutions to reduce FR2 measurement delay
It is observed that some of the FR2 L3/L1 measurement requirements allow excessively long delay with RX beam sweeping factor (e.g. for cell re-selection, the scaling factor (N1) could be up to 8 for FR2-1)
Up to Rel-18, the RX beam sweeping factor reduction is considered for some WIs, for example, multi-RX, FR2 SCell activation delay reduction, etc, which can be used as baseline to reduce RX beam sweeping factor for FR2 L3/L1 measurement delay
Motivation

## Slide 4
Consideration on fast SCell activation with EMR
Propasal 1
  It is proposed to delete “and enhanced measurement accuracy requirements” in the objective on fast SCell activation
Proposal 2
  It is proposed not to consider that UE can continue performing idle/inactive measurement after entering connected mode in the objective on fast SCell activation with EMR
Proposal
According to RP-240019, for the potential objective on fast SCell activation with EMR with both delay requirements for SCell activation and enhanced measurement accuracy requirements, the part highlighted in yellow is not clear:
  For SCell activation, there are no accuracy requirements
  If measurement accuracy requirements are not for SCell activation, it is not clear which scenario is considerd for accuracy enhancement
    if the scenario is EMR, the motivation to have accuray enhancement is not clear. In Rel-16 EMR, accuracy requirements are specified, the motivation to enhance existing EMR accuracy requirements need to be clarified.
    If the scenario is enhanced (additional) measurement discussed in Rel-18 SCell/SCG setup improvment, we do not see the necessity
      In Rel-18, there was tough discussion in RAN4 on the feasibility of enhanced (additional) measurement, but no consensus was reached. It is not necessary to spend effort to repeat the discussion in Rel-19
        For enhanced (additional) measurement, the issue on whether UE can continue performing idle/inactive measurement after entering connected mode was extensively discussed, no agreement was reached in Rel-18.
          From operator point of view, continue performing idle/inactive measurement after entering connected mode is not preferred, since it will have impact on the recommended sequence for measurement and reporting which is introduced in Rel-18.
Observation

## Slide 5
Annex

## Slide 6
Simulation results: RX beam sweeping factor reduction based on AI/ML solution
Observation
  With AI/ML, the Rx beam can be predicted by a subset of beams. For 8Tx/2Rx to predict 32Tx/8Rx, with top-3/1, the predict accuracy is above 90%. The RX beam sweeping factor (i.e. 8) could be reduced.
Set B is a subset of Set A
  Set A: 32Tx/8Rx
  Set B:
    case 1: 8Tx/4Rx
    case 2: 8Tx/2Rx
Top-K/1: the percentage of “the Top-1 strongest beam is one of the Top-K predicted beams”

## Slide 7
THANK YOU！