## Slide 1: BS RF topics for Rel-19
RP-240258
3GPP TSG RAN Meeting #103
Maastricht, The Netherlands, 18th – 21st March, 2024
Agenda Item 9.1.4.2
Source: Nokia

## Slide 2
BS RF – Mask of “Expected EIRP” above horizon in the 6425-7125 MHz band
Regulatory requirement for a single BS for protecting co-channel FSS space receivers from aggregate interference
Coexistence with Fixed Satellite Service (FSS) space receivers
Limits take into account that BSs within the satellite footprint have different:
  Orientations in azimuth
  Elevation angles range
  Beamforming directions
Technical conditions finalized at the ITU 2023 World Radiocommunication Conference (WRC-23)
Vertical angle measurement window (vertical angle above horizon) | Expected EIRP (dBm/MHz)
0 5 | P1
5 10 | P2
10 15 | P3
15 20 | P4
20 30 | P5
30 60 | P6
60 90 | P7
 | Expected EIRP (dBm/MHz)
 | P1
 | P2
 | P3
 | P4
 | P5
 | P6
 | P7
“Expected EIRP” for a vertical angle window is the averaging of EIRP over these 3 domains

## Slide 3
BS RF – Mask of “Expected EIRP” above horizon
Motivation:
  Need for reflecting the new metric and the resulting regulatory technical conditions in the BS RF core specifications as well as developing a methodology for measuring the expected EIRP for conformance test purposes.
Proposed objectives:
  Introduce the concept of “limits on expected EIRP for angles above horizon” into the RAN4 specifications and specify related requirement for 6425-7125 MHz based on the WRC-23 outcome.
  Specify manufacturer declarations, conformance test descriptions, test tolerances and test requirements.
Impacted specifications:
  38.104
  38.141-2
BS RF core requirements and conformance testing

## Slide 4
BS RF – OTA conformance testing enhancements
Motivation:
  Technical quality of 3GPP OTA conformance tests needs to be improved, address significant testing time for at least some of OTA requirements.
Proposed objectives:
  Identify excessive OTA test scope cases and reduce it for selected RF requirements, e.g., TX IM, RX out of band blocking.
  Re-evaluate and develop improved methods for co-location requirements and tests for AAS-based test specifications.
  Re-evaluate and simplify TRP test methods.
Impacted specifications:
  38.141-2
  37.145-2

## Slide 5
BS RF - BS specifications simplification
Motivation:
  Simplification of specifications below would significantly reduce number of CRs due to introduction of new band as well as reduce RAN4 workload overall.
Proposed objectives:
  Simplify structure of network nodes specifications, in cases where requirements are mirrored (e.g., co-location and co-existence) in order to minimize amount of CRs needed for new bands (both new WIDs and Maintenance).
Impacted specifications:
  36.104/141 (LTE)
  37.104/141 (MSR)
  37.105/145-1/145-2 (AAS)
  38.104/141-1/141-2 (NR)
  38.106/115-1/115-2 (Repeater)
  38.174/176-1/176-2 (IAB)