## Slide 1: Demodulation topics for Rel-19
RP-240261
3GPP TSG RAN Meeting #103
Maastricht, The Netherlands, 18th – 21st March, 2024
Agenda Item 9.1.4.5
Source: Nokia

## Slide 2
Contents
The three items proposed for demod requirement enhancement in Rel-19 in RP-240019 are:
Spatial Channel Modelling based requirements
UE performance requirements with inter cell and with intra-cell inter-use interference for 8Rx CPE/FWA/vehicle/industrial devices
MMSE-IRC receiver for uplink taking LTE interference profile as starting point
These are discussed in detail in the following slides.

## Slide 3
Spatial Channel Modelling
Motivation
Demodulation performance requirements in RAN4 are currently limited to the spatially-agnostic TDL channel model.
  Per-layer variability is not observed, unlike in real deployment scenarios. Hence the receiver’s ability to take advantage of spatial diversity provided by the channel/network is not subject to any requirements.
  In 8Rx SU-MIMO, where the 2 codewords are mapped to different sets of layers, no performance differentiation between the codewords is visible.
  MU-MIMO performance can only be tested when the UEs’ channels are spatially separable, which is not possible with the TDL channel model. Hence full benefits of operator investment in MU-MIMO cannot be verified.
Spatially realistic performance requirements are motivated for both 5G-Advanced and 6G:
  Help to underpin good performance for MIMO features in today’s 5G-Advanced networks, and
  Ensure that 6G uses spatially realistic methodology for performance requirements from day 1.
Widespread support for addressing this topic in Rel-19 was expressed on the RAN reflector in RAN#102.
  At RAN4#110 in February 2024, a multi-company proposal was submitted explaining the rationale [1], and extensive technical details were provided in [2].
Measured per-layer SINR | 
TDL | 
CDL 38.827 | 
[1] R4-2402774, “Channel Models with Spatial Features”, BT, Nokia, Nokia Shanghai Bell, Bell Mobility, CMCC, Deutsche Telekom, Ericsson, Intel, Orange, Telecom Italia, Telenor, Verizon, Vodafone, T-Mobile USA [2] R4-2402277, “Discussion on 8Rx general demodulation aspects and spatial channel models”, Nokia, Nokia Shanghai Bell, BT

## Slide 4
Spatial Channel Modelling
Proposal
CDL in TR 38.827 can provide a simple, testable, repeatable framework for spatial channel modelling requirements
  Previous discussions of spatial channel modelling in RAN4 revolved around the 38.901 spatial channel model, which had challenges with complexity and repeatability when used for testing. TR38.827 presents a tuned model that enables alignment between companies and straightforward repeatability.
Observation: RAN1 has developed advanced SU- and MU-MIMO features, and MNOs invest heavily in 5G NR MIMO systems, but performance requirements for MIMO features do not provide confidence in a minimum real-world performance.
Proposal: A spatial component is needed in the channel modelling used in RAN4 for MIMO performance requirements.
Proposal: Agree study Item to identify and define practical spatial channel modelling methodology for RAN4 demod and CSI requirements. When the study is complete, consider normative work to define performance requirements using the identified spatial channel modelling methodology for
8Rx (SU-MIMO) 2-codeword requirements for PDSCH demod, CQI and PMI.
CQI and PMI (eTypeII) for 4Rx MU-MIMO.
A Way Forward for a corresponding study item is provided in RP-240254.

## Slide 5
8Rx with inter-cell and with intra-cell inter-user interference
Observations and proposals
  The prior Rel-18 WI (8Rx with 8 layers) exists
    This is largely an extension with little commercial realization expectation.
    Having requirements with 5-7 layers was previously agreed to not be necessary.
  Inter-cell interference
    In the proposed CPE/FWA/vehicle/industrial devices use cases, cell planning will remove inter-cell interference.
  Setting requirements for an 8RX SDM/MIMO IRC receiver requires proper interference modeling (including UE positions, channel similarities, and transmit precoding) to exercise spatial interference rejection functionality. With current interference models, the performance requirements do not show gains above the increase of signal energy reception.
  Network assistance should be limited to configuration of CSI-RS IM for inter cell measurement. New signaling should not be introduced.
Observation: The value add over the Rel-18 8Rx/8layer requirements is unclear, and the interference model does not fit the use case.
Proposal: Introduce improved channel modelling before introducing further 8Rx requirements.

## Slide 6
MMSE-IRC receiver for uplink, starting from LTE interference profile
Observations and proposals
  LTE interference models in UL use the outdated DIP approach. LTE DL used INR, which seems more suitable.
  NW architecture and inter-gNB communication assumptions have a large performance impact when inter-cell interference is considered.
  Intra-cell interference performance impact is known since Rel-15 (using >1-layer cases).
The following points will need to be clarified in the objectives:
  Which LTE interference profile to use as starting point.
  Synchronous or asynchronous interference?
  Assumptions on NW architecture and inter-gNB communication.
Proposal: The choice of LTE interference profile, synchronous or asynchronous interference, and assumptions on NW architecture and inter-gNB communication need to be clarified in the objectives for this item.