## Slide 1: R19 NR Sidelink continuation and enhancements in RAN4 Agenda Item: 9.1.4.6 Source: OPPO Document for: Approval
3GPP TSG RAN#103
Maastricht, The Netherlands, March 18-21, 2024
RP-240310

## Slide 2: Background
In Rel-18, RAN4 has focused on the limited objectives of SL-unlicensed, SL CA, SL inter-band concurrent operation and the LTE/NR SL co-channel co-existence areas due to limited time. And some of the important SL targets have to be deprioritized and postponed to Rel-19.
During the RAN4#110 meeting, following parts has been identified and agreed
  If SL is agreed as Rel-19 RAN4-led package and the remaining NS values are included, specify them in Rel-19. If not, specify them in Rel-18 maintenance.
  If SL CA is agreed as Rel-19 RAN4-led package, specify the corresponding MPR in Rel-19. If not, specify it in Rel-18 maintenance. (non-contiguous RB allocation)
For SL-Unlicensed R18:
  Only power class 5 has been specified for SL-U
  Only 1Tx is supported for SL-U
  Only 5 NS values of 17 in unlicensed spectrum has been specified
For SL CA R18:
  Only intra-band contiguous CA is supported
  Only power class 3 is supported

## Slide 3: Proposal
  1. For SL CA enhancement
    Specify requirements for intra-band non-contiguous CA with power class 3
      Targeted band combination is SL_n47(2A)
      Bandwidth combinations are 10+10MHz and 10+20MHz
      UE with separate chains to support non-contiguous CA is prioritized
    Specify requirements for intra-band contiguous CA with non-contiguous RB allocation
      Targeted band combination is SL_n47B with power class 3
  2. For SL unlicensed
    Specify new NS values for SL unlicensed bands n46, n96 and n102 based on companies’ input
Considering RAN4 will continue on the SL-U R18 left works under either Rel-19 SL WID or Rel-18 maintenance, from project management perspective, put them in the WID will be much more visible and better control of the progress/load.
In light of this, below objectives are proposed for the Rel-19 SL WID contents.

## Slide 4: Annex: Example WID for Rel-19 SL enhancement in RAN4