## Slide 1: Views on IoT-NTN enhancements in Rel-19
3GPP TSG RAN Meeting #103 RP-240317
Maastricht, Netherlands, March 18-21, 2024
Agenda Item: | 9.3.2.2
Source: | Xiaomi
Document for: | Discussion

## Slide 2: Uplink Capacity Enhancement
The following objective was approved for IoT-NTN uplink capacity enhancement in RAN#102 plenary meeting[1].
  Support of Capacity enhancements for uplink
    Study then specify, if beneficial, enhancements to enable multiplexing of multiple UEs (e.g. up to the min of 4 and the maximum allowed by the existing UL and DL signalling) in a single 3.75 kHz or 15 kHz subcarrier via orthogonal cover codes (OCC) for NPUSCH format 1 and NPRACH [RAN1, RAN2]
      Multi-tone support for 15 kHz SCS should also be considered
  Note: Impact of impairment shall be taken into account
    Study and specify, if beneficial the following enhancements to reduce the necessary uplink and downlink signaling to complete an EDT transaction [RAN2]:
      Msg3 transmission without msg1/RAR
      Efficient delivery (reduced overhead) of msg4 / RRCEarlyDataComplete

## Slide 3: Uplink Capacity Enhancement
Motivation
  As noted in the WID[2], for NR-NTN PUSCH capacity enhancement, it is clear to us that OCC multiplexing is not applied to Msg3 PUSCH during initial access.
  For IoT-NTN uplink capacity enhancement, there is confusion regarding whether the OCC multiplexing should be applied to NPUSCH format 1 during idle or inactive states, as well as Msg3 NPUSCH format 1 during connected states.
  Given the limited TU and the complexity of specification efforts, it is better not to exclude these cases from the objective of IoT-NTN uplink capacity enhancements.
Proposal
  Clarify that OCC multiplexing is not applicable for NPUSCH format 1 during idle/inactive states, and Msg3 NPUSCH format 1 during connected states.

## Slide 4: Summary
According to the proposal in the contribution, we suggest to revise the objective of IoT-NTN uplink capacity enhancements in Rel-19 as follows.
  Support of Capacity enhancements for uplink
    Study then specify, if beneficial, enhancements to enable multiplexing of multiple UEs (e.g. up to the min of 4 and the maximum allowed by the existing UL and DL signalling) in a single 3.75 kHz or 15 kHz subcarrier via orthogonal cover codes (OCC) for NPUSCH format 1 and NPRACH [RAN1, RAN2]
      Multi-tone support for 15 kHz SCS should also be considered
  Note:
      Impact of impairment shall be taken into account
      Enhancements to Msg3 NPUSCH format 1, as well as NPUSCH format 1 in inactive/idle states are not in scope
    Study and specify, if beneficial the following enhancements to reduce the necessary uplink and downlink signaling to complete an EDT transaction [RAN2]:
      Msg3 transmission without msg1/RAR
      Efficient delivery (reduced overhead) of msg4 / RRCEarlyDataComplete

## Slide 5: Reference
[1] RP-234077, “New WID: Non-Terrestrial Networks (NTN) for Internet of Things (IoT) Phase 3”, Deutsche Telekom (moderator, RAN VC), 3GPP TSG RAN Meeting #102, Edinburgh, Scotland, December 11-15, 2023
[2] RP-234078, “New WID: Non-Terrestrial Networks (NTN) for NR Phase 3”, Huawei (Moderator, RAN1 Vice-Chair), 3GPP TSG RAN Meeting #102, Edinburgh, Scotland, December 11-15, 2023
Notes: For PRACH, some companies argues that if only format 2 is used, CE is unnecessary. Is it okay to only use PF2, any disadvantages?

## Slide 6
Thank you