## Slide 1: Views on candidate UE RF topics for RAN4 Rel-19
China Telecom
2024.03
3GPP TSG RAN #103
Maastricht, Netherlands, March 18-21, 2024
Agenda: 9.1.4.1
RP-240349

## Slide 2: Justification-power domain enhancement
To fully utilize the UE transmit power with higher efficiency, the two methods of reporting more power parameters and reducing MPR is intensely discussed in RAN4 release 18.
  MPR reduction is introduced in release 18 for both pi/2 BPSK and QPSK by allowing 1dB power boosting gain with PC3 and 0.5dB with PC2. However, however for 16QAM etc. higher order modulations, no power boosting capability applies. So power boosting or MPR reduction is still necessary to be further evaluated.
  Reporting the parameter is introduced for FR1 deployments, on a per cell basis. This mechanism allows network to know the UE power class information more precisely and to adjust the attainable transmitting and receiving power level timely. The parameter of depend on the dutycycle solution of which the evaluation period, start and end timing are up to UE implementation. Such information shall be also shared to BS for the timing of changes.
From rel-16 to rel-18 a series of SIs and WIs related to HPUE have been established to study and specify the requirements for EN-DC, LTE, NR, CA and SUL combinations, motivated by significant benefits in cell coverage and user throughput.
  This directly improves the cap of UE transmit power, however, the real transmit power of UE depends on many factors, of which MPR is a key parameter. As the MPR is derived based on ACLR, EVM, phase noise and IQ imbalance etc.,
  These conditional requirements may not always apply for all the scenarios, which means ACLR could be relaxed if no other operators in adjacent channel, or EVM could be relaxed if same receiving performance could be achieved. Thus power can be boosted or MRP can be further reduced based on relaxed ACLR or EVM requirements.
Hence, it is proposed to set a WI to work on the power boosting or MPR reduction for PC2/PC3 with conditional requirements relaxation, and also continue optimize the power class related reporting solution including duration, full-power transmission, P-MPR reporting.

## Slide 3: Objectives-power domain enhancement
Power boosting or MPR reduction for PC2/PC3 with conditional requirements relaxation
  Under condition of relaxed ACLR or EVM requirements, Specify Power boosting or MPR reduction requirement for specific power class
    Identify the bottleneck requirements within ACLR and EVM for Power boosting or MPR reduction for different modulation orders of QPSK, 16QAM, 64QAM and 256QAM
    Specify the Power boosting or MPR reduction requirements based on identified relaxed ACLR or EVM requirements
  Under condition of PAPR reduction, specify Power boosting or MPR reduction requirement for specific power class
    Study and confirm PAPR reduction methods that shows benefit for smoothing power across frequencies
    Specify the Power boosting or MPR reduction requirements based on identified PAPR reduction requirements
    Optimize the Power boosting or MPR requirements for 2Tx UE architecture according to different implementation of the CBW or PRB allocation for each Tx
Continue optimize the power class related reporting solution
  Introduce ‘duration’ information (e.g., a UE can sustain UL at a previously or concurrently reported PCmax) report for FR1
  Consider UE full-power transmission capability report method, and specify the corresponding configuration/indication method for full-power transmission mode
  Discuss to distinguish UE capabilities about SAR solution for single carrier /CA/DC and whether to introduce P-MPR report in FR1

## Slide 4: Views on 3Tx and 6Rx
3Tx
  Extend the capability for increasing power high limit to more power class use cases including, PC2 + PC3 for 3Tx architecture, PC1.5 + PC2/PC3 for 3Tx architecture
  An general framework e.g. removing the cap of CA power class is a straight forward way to simplify introducing the power class combinations
  PC1.5 supporting for inter-band CA (PC2+PC2) with 2Tx or 3Tx for handheld and FWA
  PC1.5 supporting for intra-band contiguous CA with or without MIMO with 2Tx
    PC1.5 is supported only for single UL in Rel-18, it's suggested to introduce PC1.5(PC2+PC2) inter-band and intra-band combs in Rel-19.
    If new PC1.5 objectives are captured, it is suggested to refine the existing WI title and objectives or coordinate with other high power UE basket WIs. The intention is to better categorize and trace them.
6Rx
  Investigate and enable 6Rx on higher frequency bands (>2.5GHz ) targeting at support of smartphone and FWA
    It is proposed to cover the example bands including n41, n77, n78 with smartphone
  Specify the requirements to support SRS antenna switching