## Slide 1: Views on candidate NTN topics for RAN4 Rel-19
China Telecom
2024.03
3GPP TSG RAN #103
Maastricht, Netherlands, March 18-21, 2024
Agenda: 9.1.4.6
RP-240351

## Slide 2: HPUE for NTN
Justification:
  The high power UE has been identified as a direct technology to solve the coverage issue in high and medium frequency range for both NR and LTE. From rel-16 to rel-18 a series of SIs and WIs related to HPUE have been established to study and specify the requirements for EN-DC, LTE, CA and SUL combinations, motivated by significant benefits in cell coverage and cell edge user throughput. In which, the duty cycle solution was raised as one of efficient mechanism to make UE comply with the SAR (specific absorption rate) limit, and now are still under optimization.
  Recently, for some of operators who can provide satellite service, the NTN system is also with high priority for their commercial deployment plan. Thus to make NTN UE support higher transmit power will benefit NTN applying for more scenarios especially supporting large channel bandwidth and accessing to higher orbit satellite.
  Referring to the design and implementation of UE in other non-3GPP satellite systems, it is feasible for the NTN handheld UE to support higher power to achieve better user experience.
  Hence, it is proposed to set a WI to work on the mechanism and requirements for NTN UE to support high power.

## Slide 3: HPUE for NTN-Objectives
Introduce PC2 for NR/IoT NTN UE in NTN FR1 bands for both handheld and non-handheld (need confirmation on the co-existence)
  Specify the RF requirements including: UE maximum output power, Tx power tolerance, MPR, A-MPR and reference sensitivity degradation requirements if needed. [RAN4]
  The example band include both IoT NTN Band and NR NTN Band of (n)256, (n)255, (n)254 [RAN4]
The duty cycle solution needs to be improved to comply with the SAR regulation.
  Delta power class method could be reused [RAN4, RAN2]
  Specify P-MPR reporting solution [RAN2]
Coexistence study for NTN UE support PC1.5 and PC1 [RAN4]
  The simulation assumptions and methodology are based on TR 38.863
Based on coexistence study outcome, introduce PC1.5 and PC1 for NR/IoT NTN UE in NTN FR1 bands for both handheld and non-handheld [RAN4]
  The handheld UE is suggested to support PC1 for only working in the non-proximity way(e.g. hands free mode)
Need further discussion on high power UE in NTN FR2 bands for non-handheld UE

## Slide 4: Views on NTN testing and small channel bandwidth
NTN performance requirements/testing for NGSO for UEs
  The GSO and NGSO are both intended to provide direct satellite to smartphone service, the typical scenarios include:
    GEO + L\S band + IoT NTN: Direct satellite-to-smartphone with low data rate and short message
    GEO + Ka\Ku\V band + NR NTN: Direct satellite to vehicle, ship and emergency terminals
    LEO + L\S\C band + NR NTN: Direct satellite-to-smartphone
    LEO + Ka\Ku\V band + NR NTN: Direct satellite-to-dedicated terminal
  Observation: The scenario of NGSO for LEO+L\S\C band shows larger potential market for smartphone directly accessing to satellite. The channel model for LEO changes all the times and is quite different from TN network, due to the satellite keeping moving fast relative to the UE.
  Proposal: Parameters as DL arrival timing and Doppler frequency needs to be optimized to facilitate LEO channel modeling and guarantee NTN UE performance by specifying both demod and RRM test requirements.
NR Channel BW less than 5 MHz (focusing on 3MHz)
  Observation: With one of the commercial satellite services as low date rate voice and short message, supporting less than 5MHz is necessary for NR NTN.
  Proposal: Specify requirements for channel BW less than 5 MHz for NR NTN