## Slide 1: Views on RAN4 Rel-19 demodulation requirement enhancement
China Telecom
3GPP TSG RAN #103
Maastricht, Netherlands, March 18-21, 2024
Agenda: 9.1.4.5
RP-240352

## Slide 2: Introduction
In RAN#102, companies have discussed the potential demodulation enhancement topics for Rel-19. As a result, a summary of the candidate demodulation topics is given in [1].
Prior to RAN#103 meeting, the summary on RAN4 part of RAN Rel-19 package is provided by RAN Chair and RAN4 Chair in [2], in which high-level objectives are proposed for Rel-19 RAN4 demodulation requirement enhancement topic:
In this contribution, our views on the detailed objectives in [2] are given.
Demod

## Slide 3: Proposed justifications and detailed objectives (1/2)
  UE performance requirements with inter cell and with intra-cell inter-user interference for 8Rx CPE/FWA/vehicle/industrial devices
  Proposed Justification:
    Performance requirements for 8Rx UE is introduced in Rel-18 with MMSE-IRC is the assumed receiver.
    The existing 8Rx performance requirements do not cover scenarios with co-channel inter cell and with intra-cell inter-user interference, which is mandatory for 2/4Rx UEs from Rel-17.
    Compared with 2/4Rx, larger gain of MMSE-IRC is expected for 8Rx UEs under interference scenarios, due to larger spatial domain freedom.
  Proposed Objectives:
    Define the following requirements for 8Rx CPE/FWA/vehicle/industrial devices:
      PDSCH demodulation requirements with inter cell and with intra-cell inter-user interference
      CQI reporting requirements with inter cell interference
      Specify release independence requirements in TS 38.307 if needed.

## Slide 4: Proposed justifications and detailed objectives (2/2)
  BS demodulation requirements with MMSE-IRC advanced receiver
  Proposed Justification:
    The UE MMSE-IRC requirements have been defined in Rel-17. There is necessity to introduce the BS MMSE-IRC requirements for FDD and TDD.
    For NR, the widely use of HPUE makes UL co-channel interference from the UE in neighboring cell severer than that of LTE.
    In field test with different TDD UL/DL configurations between neighboring cells, heavy gNB-to-gNB co-channel interference is observed, which can also be largely alleviated by BS MMSE-IRC receiver.
  Proposed Objectives:
    Define PUSCH demodulation requirements under inter-cell interference
      Receiver type: MMSE-IRC receiver
      Interference profile: LTE interference profile as a starting point. Other interference profiles are not precluded

## Slide 5: Impacted spec
Impacted existing TS | 
TS/TR No. | Description of change
38.101-4 | NR; User Equipment (UE) radio transmission and reception; Part 4: Performance requirements
38.104 | NR; Base Station (BS) radio transmission and reception
38.141-1 | NR; Base Station (BS) conformance testing Part 1: Conducted conformance testing
38.141-2 | NR; Base Station (BS) conformance testing Part 2: Radiated conformance testing
38.307 | NR; Requirements on User Equipments (UEs) supporting a release-independent frequency band

## Slide 6: Views on spatial channel modeling
  Channel model with spatial component for performance requirements was discussed in RAN #102, with the following alternatives for study the test feasibility
  Alternative 1: Extending TDL channel model
  Alternative 2: CDL channel model
  Our view:
  Spatial domain channel model is important for demodulation performance requirement definition, but it is more beneficial to consider it in Rel-20:
    By Rel-20, RAN4 can discuss channel model with spatial components based on the state-of-art test equipment implementation and other industrial progress, which can be better applied to both 5G-A and future 6G.
    For Rel-19, the spatial channel model (if defined) can be applied in few new test cases but cannot be applied to most of the existing demodulation test cases, thus the benefit for 5G deployment is limited. Instead, it is more preferable for us to focus on the other objectives that better reflect the current deployment status in Rel-19.
  If this objective will be included in Rel-19, to keep the same number of objectives for demod WI, we suggest to combine this objective with another Rel-19 demod objective for 8Rx UE, i.e.,
    Define PDSCH demodulation requirements for channel model with spatial component, under intra-cell inter-user interference for 8Rx CPE/FWA/vehicle/industrial devices

## Slide 7: Reference
  [1] RP-233951, Moderator's summary for RAN4 Candidate Demodulation/RRM Topics for Rel-19, Moderator (vivo), RAN#102, Dec 2023
  [2] RP-240019, Proposed Summary for RAN Rel-19 Package: RAN4 Part, RAN Chair, RAN4 Chair, RAN#103, March 2024

## Slide 8: Thanks!