## Slide 1: Proposals on Rel-19 spectrum related items
Source: ZTE, Sanechips
Agenda: 9.1.5
3GPP TSG RAN Meeting #103
Maastricht , NL, March 18 – 21, 2024
RP-240475

## Slide 2: NR based AeroMACS-Use case
Justification:
AeroMACS is the aeronautical mobile airport communication system (AeroMACS) which is used to provide the wireless communication system for airport to help airlines, airport authorities and airport ground service etc.
AeroMACS is still using the WiMAX standard (IEEE 802.16) at the aeronautical C-band (5 GHz) to provide the service till now.
Based on the latest decision from CAAC (Civil Aviation Administration of China), it's planned to provide the NR based AeroMACS system.

## Slide 3: NR based AeroMACS- Spectrum status
Spectrum status:
ITU-R WRC-07 decided to assign the 5091-5150MHz for the spectrum of AeroMACS system;
ITU-R WRC-12 decided to assign the 5030~5091MHz for the spectrum of AeroMACS system;
NASA consider the use of the 5000-5030 MHz band to extend the tuning range for the the AeroMACS.
Proposal 1: Specify the band 5091~5150MHz for regional deployment and 5000~5150MHz for global deployment.
Proposal 2: Define RF requirement for BS and UE requirement;
Proposal 3: Define the RRM requirement for AeroMacs UE if necessary;
Proposal 4: Define the Demod requirement for AeroMacs BS and UE if necessary;

## Slide 4: Thanks