## Slide 1: MSS Satellite operator RAN4-led non-spectrum priorities for NTN Evolution in Release 19
Source: Inmarsat, Viasat, Omnispace, Hughes/EchoStar, Terrestar Solutions, Ligado Networks
3GPP TSG RAN #103
March 18 - 22, 2024, Maastricht/The Netherlands
Agenda: 9.1.4.6 - Proposals led by RAN4 (not spectrum related), Other topics (e.g. covering multiple)
TDOC: RP-240506
For: discussion

## Slide 2: NR NTN Operator Priorities
NR less than 5 MHz – At least enabling support for 3 MHz channel BW and 12 PRB transmission, as already specified by NR_FR1_lessthan_5MHz_BW also for NTN bands. This is critical to enable NR NTN deployments within the context of existing non-3GPP services, as well as to support EIRP limited satellites and maximize frequency reuse efficiency.
HPUE for NR NTN – For all FR1 NTN bands, with support for PC2 (+26 dBm), PC 1.5 (+29 dBm) and PC1 (31 dBm), reusing existing TN assumptions for FDD HPUE
NTN-NTN intra-SAN Carrier aggregation (CA) - Focused on improving throughput per user and aggregating BW across different NTN frequency blocks within the same SAN (e.g. intra-band and inter-band L + S)
Better Support of Fragmented Spectrum - To accommodate situations where the existing legacy services may interrupt a 5G NR channel allocation, requiring 5G NR NTN services to be scheduled around, with a larger system bandwidth
4RX for NR NTN – To improve receive performance and align NR NTN UE with TN specification and requirements for devices that can fit up to four L and S-band antennas.

## Slide 3: IoT NTN Operator Priorities
HPUE for IoT NTN - For all FR1 IoT NTN bands including especially for NB-IoT NTN, with support for PC2 (+26 dBm) and PC1 (31 dBm).
In-Band NB-IoT NTN with NR NTN in same SAN – Currently, deployment of NB-IoT within 5G NR carriers is already supported for terrestrial networks as of Rel-16, helping greatly improve spectrum usage efficiency and deployment flexibility. This is a key missing feature and low hanging fruit for NTN.
  No change in NB-IoT vs NR coexistence assumptions (TR 37.824)
  Already discussed in Athens RAN4#110

## Slide 4: NR NTN less than 5 MHz
Background:
Initial NR NTN deployments will have to coexist with existing non-3GPP satellite services
Furthermore, satellites will still have limited power and will be largely EIRP-limited
Reduction of the minimum BW required can facilitate with:
  Early NR NTN deployment around existing services
  Support of EIRP-limited satellite assets
  Easier frequency resource management and reuse
Proposals:
Specify support for 12 and 15 PRB operation and new 3 MHz NR channel BW for NR NTN bands n255, n256 the n254 and upcoming Extended L-band [n253]
  Support of 12 PRB and 15 PRB should include deployment with a larger system/channel BW than 3 MHz
As a minimum, reuse existing TN assumption of support down to 12 PRB with no further impact to PSS/SSS and PBCH puncturing.
  Potentially up to 5 dB PBCH link budget loss has been identified due to puncturing
  Clarify link budget loss for NTN and consider techniques to recover PBCH performance loss
  Consider if further reduction could be achieved at least for certain physical layer channels (i.e. no impact to PSS/SSS)

## Slide 5: HPUE support for NR NTN
Background:
Current NTN systems in are both coverage and capacity challenged in UL due to the tight link budget, especially when taking realistic antenna gain assumptions (e.g. -5.5 dBi gain)
Current solutions to improve coverage are mostly based on repetitions, which severely affect system capacity.
This issue was raised during RAN#97 and later RAN#99 and was postponed to Rel-19.
Satellite UE transmission regulation allow UL transmission powers up to 15 dBW for hand-held type terminals (e.g. satellite phones) and far higher for non-handheld. 3GPP should better align with what is allowed within the current satellite regulatory framework.
The lack of this capability will be severely limiting for a number of use cases in upcoming NR NTN deployments
Objectives:
Taking reference NTN bands n255, n256 the n254 and upcoming Extended L-band [n253] into consideration:
  For NR NTN UEs: Specify support for PC2 (+26 dBm) for smartphone form factor; PC1.5 (+29 dBm) and PC1 (+31 dBm) at least for non-smartphone form factor.
  If necessary, consider aspects related to duty cycle to control Specific Absorption Rate (SAR) for smartphone applications.

## Slide 6: HPUE support for IoT NTN
Background:
Current NTN systems in are both coverage and capacity challenged in UL due to the tight link budget, especially when taking realistic antenna gain assumptions (e.g. -5.5 dBi gain)
Current solutions to improve coverage are mostly based on repetitions, which severely affect system capacity.
This issue was raised during RAN#97 and later RAN#99 and was postponed to Rel-19.
Satellite UE transmission regulation allow transmission powers up to 15 dBW for hand-held type terminals (e.g. satellite phones) and far higher for non-handheld. 3GPP should better align with what is allowed within the current satellite regulatory framework.
The lack of this capability is currently severely limiting ongoing NTN deployments and use cases, which are starting with NB-IoT.
Objectives:
Taking reference NTN bands 255, 256, 254 and 253 into consideration:
  For eMTC IoT NTN UEs (Cat M1): Specify support of UE Power class 2 (+26 dBm) for smartphone form factor; Power class 1.5 (+29 dBm) UE Power class 1 (+31 dBm) at least for non-smartphone form factor;
  For NB-IoT NTN UEs (Cat NB1, NB2): Specify support for a New UE Power Class with MOP of +26 dBm; and a New Power Class with MOP of +31 dBm;
  If necessary, consider aspects related to duty cycle to control Specific Absorption Rate (SAR) for smartphone applications (NB-IoT might be used for smartphones)

## Slide 7: In-Band NB-IoT NTN with NR same SAN
Background
Currently, deployment of NB-IoT within 5G NR carriers is already supported for terrestrial networks as of Rel-16, helping greatly improve spectrum usage efficiency and deployment flexibility. To support growth of NTN NB-IoT it is necessary to further improve and encourage its network deployment with NTN-NR operation.
This is a key missing feature and low hanging fruit for NTN.
Objectives
  For NB-IoT operation in NR guard band, baseline assumption is to re-use the conclusions from TR 37.824, where this is treated the same as in-band deployment. RF requirements will not be specified
  No change in NB-IoT vs NR coexistence assumptions (TR 37.824)
  Already discussed in Athens RAN4#110

## Slide 8: NTN-NTN Intra-SAN Carrier Aggregation (CA)
Background
Between L and S bands, it is expected that a relatively large amount of spectrum will be available for NR NTN, however, different blocks of spectrums might not necessarily be contiguous, at least in the initial part of the service lifetime.
NTN Operators may have access to both L and S band spectrum blocks (e.g. n256 and n255), deployable from the same SAN and combining spectrum bands could significantly increase User Experienced Throughput
NR NTN link budget is very challenged, especially in UL from handheld UE.  Allocation of UL CC to different PAs in the same UE (same or different band) could significantly improve the available BW and resulting UL user throughput.
Objectives
Identify and, if necessary, specify any missing requirements in order to support NTN-NTN intra-SAN Carrier Aggergation (CA), both intra-band and inter-band, with an initial focus on bands n255 and n256
Both DL and UL CA must be supported  UL leveraging 2 TX PAs independently on the UE
The following CA combinations should be considered in priority as a starting point (to be specified including UL CA combinations):
  Intra-band non-contiguous (DL and UL)
    CA_n255(2A)
    CA_n256(2A)
  Inter-band (DL and UL)
    CA_n255A-n256A
    CA_n256A-n255A

## Slide 9: Support for fragmented spectrum
Background:
Current NTN spectrum bands are in many cases already hosting some legacy services (to varying degrees)
The total potential available spectrum for NTN is quite significant, but it may be interrupted by some legacy services.
  Some chunks may be available that are just slightly smaller than a full NR channel BW, and would work best aggregated with a parent channel
An NTN operator may specify a wider NR system bandwidth and schedule signalling and user data around existing legacy services, but currently this is mostly left to implementation, and there are no explicit mechanisms to facilitate this mode of operation
Although the NTN scenarios for fragmented spectrum will be different from TN, there are a lot of commonalities and work that can benefit both TN and NTN
5 MHz CH
2 MHz block
SSB
1CC UE BW
1CC
Objectives:
Study the possible enhancements required to facilitate spectrum utilization of fragmented spectrum blocks across a wider frequency band through single wider Component Carriers, where frequency allocations might be interrupted by other allocations for NTN or other legacy services
  Include grouping of spectrum blocks that might be smaller than the minimum NR Channel BW with other allocated Channels
NTN scenarios for fragmented spectrum usage can be combined with any TN studies on improved usage of fragmented spectrum