## Slide 1: New L-band definitions and CA combinations for NR NTN
Viasat, Inmarsat
3GPP TSG RAN #103
March 18 - 22, 2024, Maastricht/The Netherlands
Agenda: 9.1.5 - Proposals led by RAN4 (spectrum related)
TDOC: RP-240551
For: discussion

## Slide 2: New NTN Operator Spectrum Candidate Proposals
Summary:
New NR NTN band [n253] to support the MSS Extended L-band (UL 1668-1675, DL 1518-1525), mirroring the current band 253 for IoT NTN covering the same range
New un-paired NR NTN DL and UL bands encompassing the contiguous DL range of L-band and Extended L-band (e.g. n255 + n253) and the non-contiguous UL blocks
  DL block 1518-1559 MHz
  UL block #1 1626.5-1660.5 MHz
  UL block #2 1668-1675 MHz
New DL and UL Intra-SAN Carrier Aggregation (CA) combinations for FR1 NR NTN bands.
  Intra-band (e.g. n255 + n255, n255 + n253, n256 + n256)
  Inter-band (e.g. n256 + n255, n255 + n253, etc)
New DL + UL inter-band pairings, to allow combining 1xDL and 1xUL from different NTN bands, e.g:
  n255 UL + n256 DL (and vice-versa)
  n255 DL + n253 UL (and vice-versa)
  etc

## Slide 3: New NTN Operator Spectrum Candidate Proposals
Background and Motivation:
Extended L-band (UL 1668-1675, DL 1518-1525) is being addressed in Release-18 for IoT NTN (LTE band) only as band 253 (IoT_NTN_extLband).
The need for a corresponding NR NTN band covering the Extended L-band range has been expressed since RAN#100, but has been postponed due to high RAN4 workload
The L-band and Extended L-band DL ranges are contiguous and are both available in the majority of global regions (Region 1, 3 and parts of Region 2), but separate band specifications would lead to lack of flexibility, making carrier allocations at the band edges (e.g. across the 1525 MHz edge for DL) unusable
The L-band and Extended L-band UL ranges are non-contiguous, so there is a need to identify how to best specify them. The simplest and most future-proof option would be to specify unpaired band segments (1x DL and 2x UL).
  A similar approach could be taken to allow L and S-band combinations
    n255 UL with n256 DL (and vice-versa)
    n255 DL with n253 UL (and vice-versa)
    etc
There is an urgent need to complete the FR1 NR NTN band plan to allow sufficient time for UE implementation in preparation for network roll-out

## Slide 4: New NR NTN Band and CA combos Candidate Proposals
Band(s) | Candidate Band Number | Downlink | Uplink | Channel Raster | Mode | TX-RX Separation
Extended L-band | [n253] | 1518-1525 MHz | 1668-1675 MHz | Enhanced (10 kHz) - Mandatory | FDD or Unpaired | Flexible or unspecified
Potential Combined L-band and Extended L-band | TBD | 1518-1559 MHz | Block #1 1626.5-1660.5 MHz Block #2 1668-1675 MHz | Enhanced (10 kHz) - Mandatory | Unpaired DL and UL | Flexible or unspecified
New or Modified Combination | Band combination configuration | UpLink configuration | Subclass | Power class of band X | Tx number of band X | Power class of band Y | Tx number of band Y | Total Power class
New | CA_n255(2A) | CA_n255(2A) | NR only | PC3 | 1Tx | - | - | PC3
New | CA_n256(2A) | CA_n256(2A) | NR only | PC3 | 1Tx | - | - | PC3
New | CA_n255A-n256A | CA_n255A-n256A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3
New | CA_n255A-n253A | CA_n255A-n253A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3
New | CA_n256A-n253A | CA_n256A-n253A | NR only | PC3 | 1Tx | PC3 | 1Tx | PC3

## Slide 5: Thank You!