## Slide 1
Way forward on Duplex Evolution in Rel-20
RP-250076
3GPP TSG RAN #107
Incheon, Korea, March 12-14, 2025
Agenda: 15.2.10
Source: Samsung, CMCC, InterDigital, MediaTek, Qualcomm, Spreadtrum, Xiaomi
Document for : Discussion and decision

## Slide 2: Discussion on duplex evolution
According to the endorsed RAN Chair’s Summary of 5G-Advanced in Rel-20 (RP-243292),
  As a baseline, RAN WG capacity is not expected to increase in Rel-20 due to the parallel tracks of 5G-Advanced and 6G
  RAN WG capacity has to be carefully shared between 5G-Advanced and 6G in Rel-20
  It is necessary to avoid duplicate scope in 5G-Advanced and 6G in Rel-20
  In 5G-Advanced Rel-20, SBFD was categorized into “Others” based on WS contributions
Also, study of SBFD and its enhancements has been proposed in 6G WS contributions

## Slide 3: Discussion on duplex evolution
From TR38.858 and the corresponding Duplex Evolution Study Item (Rel-18)
  RAN1 has studied the following four deployment cases and Case 1 was mostly evaluated. Also, RAN1 has studied dynamic SBFD but no conclusion on performance benefits has been drawn
    SBFD Deployment Case 1 (Non-coexistence case with single SBFD subband configuration)
    SBFD Deployment Case 2 (Non-coexistence case with multiple SBFD subband configurations)
    SBFD Deployment Case 3 (Co-channel co-existence case)
    SBFD Deployment Case 4 (Adjacent-channel co-existence case)
  RAN4 has only studied “the SBFD configuration is the same in all sectors and sites” – SBFD Deployment Cases 2 and 3 were out of the study. So, their implementation feasibilities are not confirmed.
    Throughout the study, it is assumed that all other sectors and other base stations belonging to the same operator do not transmit in the uplink sub-band during SBFD slots, that is, that SBFD is deployed in all sectors and sites and the SBFD configuration is the same in all sectors and sites. The case where SBFD is not deployed at all sites or SBFD configurations could differ has not been examined as part of the study.

## Slide 4: Proposal
Rel-20 should avoid duplicate scope in Duplex Evolution for 5G Advanced and 6G Study
  Instead, the focus should be on Duplex Evolution for 6G based on commercial needs, new spectrum availability, and deployment scenarios, etc.