## Slide 1
Support for NTN positioning for GNSS resilient IoT-NTN operations in 5G-Advanced Rel-20

## Slide 2
Drivers for RAT-dep. Positioning in IoT-NTN
02
03
IMS voice call over GEO (emergency calls require knowledge about UE location)
GNSS resilient operation
01
  IOT-NTN positioning for GNSS resilient operation: Drivers
01
Un-addressed stage 1 requirements
GNSS resilient operation
The initial access mechanism in 5G NTN remains unchanged and continues to rely on UE and satellite location for time and frequency pre-compensation.
The proposed IoT-NTN-native positioning acts as fallback to maintain operational continuity, without replacing GNSS.
IMS voice call over GEO
This feature is expected to also enable emergency call, where knowledge of the UE location is critical. Without support for basic IoT-NTN positioning, this capability would remain fully dependent on GNSS availability, increasing the risk of service unavailability during GNSS outages.
SA1 TS 22.261 req. for positioning aspects for satellite access
A 5G system with satellite access shall be able to provide positioning service to a UE using only satellite access and the information on positioning services. NOTE: UE can be with or without GNSS capabilities.
Few more requirements in 6.46.10
Current NTN systems are overly dependent on GNSS, leaving them vulnerable to service disruptions.
Notes: Continue to be very dependent on a non-3GPP system (GNSS) for important system aspects e.g., initial access, mobility, etc.

## Slide 3
  IoT-NTN positioning: high level concept description
02
Any satellite positioning system needs two main features: (1) a positioning reference signal and (2) system information (e.g., satellite ephemeris)
Starting from OTDOA in TN for NB-IOT (TS 37.355), NB-NTN positioning can be specified with little effort:
Narrowband Positioning Reference Signal, already specified in TS 36.211 for use in TN systems, can be adjusted to work also in IoT-NTN systems.
Satellite ephemeris are broadcast in SIB31-NB (IoT-NTN) are always available for initial access. Leveraging this feature and the potential availability of NPRS, UE can estimate its location based on measuring time of arrivals on signals from NTN satellites.
Putting together the elements from above, a positioning method derived from OTDOA in TN systems could become feasible in NB-NTN systems. Furthermore, it can work in UE-based mode and for UEs in IDLE mode.
OTDOA positioning in NB-NTN systems

## Slide 4
  IoT-NTN positioning: Specifications impact
03
Potential scope for RAT-dependent NB-NTN positioning in Rel20 5G-Advanced:
Leverage positioning reference signals ((N)PRS, etc.), methods (OTDOA, etc.), signalling (LPP) already specified for TN systems to enable positioning in IOT-NTN.
Group | Impact | Workload Estimate
RAN1 | Minimal impact: Narrowband Positioning Reference Signal (NPRS) is already specified in TS 36.211, respectively | 0.5 TU (to assess feasibility of using NPRS in IoT-NTN systems) Reference Signals: Reuse Narrowband PRS specified in TS 36.211 in IoT-NTN
RAN2 | Primary group affected | 0.5 TU (to adjust Stage 2 and LPP signalling (Stage 3) specs TS 36.305 and TS 37.355 to support OTDOA-NB in IoT-NTN) Methods: Adapt terrestrial OTDOA for NB-IOT to IoT-NTN case Protocols: LPP primarily
RAN3 | Minimal or no impact | 0 TU (no impact a-priori as satellite position is broadcast in SIB31-NB; any potential posSIB updates could be done via normal alignment CR process)

## Slide 5
Observation 1: IoT-NTN systems do no support RAT-dependent positioning despite stage 1 requirements (section 6.46.10 of TS 22.261)
Observation 2: Incorporating IoT-NTN positioning in Rel-20 for 5G-Advanced will not only fulfil unaddressed 3GPP requirements but also ensure service robustness in case of GNSS unavailability.
Proposal: Support for NB-NTN RAT-dependent positioning in Rel-20 for 5G-Advanced (RAN1/2/3).
  Conclusions
04

## Slide 6
Thank you for your attention!
Contact: stefano.cioni@esa.int; florin-catalin.grec@esa.int

## Slide 7
Introduction of OTDOA (Rel-9)
Introduction of NB OTDOA (Rel-14)
Introduction of A-GNSS (Rel-9)
Current 3GPP specifications for 4G and 5G include positioning capabilities based on terrestrial networks and GNSS
  Annex: Evolution of RAT-dependent positioning in LTE and 5G
Missing capability:
RAT-dependent positioning in IoT-NTN and NR-NTN