## Slide 1: Consideration on Ambient IoT for Rel-20
CMCC
3GPP TSG RAN Meeting #107 RP-250256
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.3
Source: CMCC
Document for: Discussion

## Slide 2: Background for Rel-20 A-IoT (RAN#106)
Workplan for Rel-20:
  Includes D2T2
  Includes Device 2
  A limited number of additional use cases, deployments, connectivity topologies, devices, traffic types in TR38.848 as a starting point
  Note: work on D2T2, device 2 shall follow the Rel-19 study conclusions, and further down-selection of architecture options for topology 2 may be needed. For indoor use cases, deviations from Rel-19 study conclusion shall be well justified and agreed.
  Details to be discussed at a later RAN plenary meeting, including the need for study phase.
For both Rel-19 and Rel-20, co-ordination with SA2/3 is expected

## Slide 3: High level timeline for R20 A-IoT
Ambient IoT is an important 5G-A technology covers both indoor and outdoor solutions
  Rel-19 WI mainly focus on indoor scenarios.
  Rel-20 WI mainly focus on indoor/outdoor(limited coverage) scenarios.
High-level timeline
  The step-by-step release of specifications for A-IoT effectively supports market utilization.
The Rel-19 AIOT SI is well on track and is expected to complete in December.
RAN1 5G-A Rel-19
RAN1 5G-A R20 (15 mon.)
2024
2025
2026
R19 AIOT SI
R19 AIOT WI
(6 mon.)
R20 AIOT WI (18 mon.)
RAN2/3 5G-A Rel-19
RAN2/3 5G-A R20 (15 mon.)

## Slide 4: High level scope of Rel-20 A-IoT WI
Scenarios
  Support of both topology 1 and 2.
  Device type 2b (IF/ZIF)
  In addition to inventory/command, support the following use cases,
    Sensor
    Positioning*
Rel-20 A-IoT device are not replacement of LPWA technologies,
  with limited coverage, limited power consumption and low cost.
Definition of device 2b are as in TR38.769.
* For positioning, if included, down-scope for positioning solutions is necessary in order to avoid multiple solutions being studied/specified.

## Slide 5: High level scope of Rel-20 A-IoT WI
Coverage target
  Alt 1: limited coverage
    Better coverage extension compared to Rel-19. May not be able to continuous coverage of the cell.
    Physical layer should target for simple technical enhancement based on Rel-19 design.
  Alt 2: almost MCL 140dB (i.e., full coverage of the cell)
    Initial access procedure for sync
    CFO calibrate for better UL Tx/Rx
    More repetitions in D2R to support large coverage compared to Rel-19 A-IoT.
  Remark: need to discuss whether Alt 1 or Alt 2 for Rel-20 WI.
Necessary enhancements
  Support of active transmission in D2R for device 2b
  DoA RACH procedure/configuration and data transmission procedure for device 2b
  Necessary solutions to extend device’s sustainable operation time
  Support device 1 and device 2b in topology 2, including,
    Down-selection or support both of RRC/UP based solutions for topo 2.
      Note: NAS based solution is not recommended by SA2
    Specify the Uu and NG interface procedures and signallings for topo 2.
      Note: A-IoT interface for topo 1 should be reused as much as possible
  Co-existence
    Outdoor ambient IoT and NR/LTE co-existence is required if it target for outdoor.