## Slide 1: Support of GEO satellite voice call
3GPP TSG RAN Meeting #107 RP-250258
Incheon, Korea, March 12-14, 2025
Agenda: 15.2.5
Source: CMCC

## Slide 2: Voice over IoT-NTN
Motivation
GEO provides a unique advantage in terms of global coverage:
  In some cases (e.g. without TN coverage or the conventional TN communication infrastructure is destroyed), it is urgent to establish real-time interaction in a short time period
  Therefore to support real-time voice communication over NTN is essential.
SA1 has agreed a new WID (S1-244772 Satellite access - Phase 4) in Rel-20 including support IMS voice calls using GEO satellite access and discussed new potential service requirements.
Low data rate:The current IoT-NTN data rate can reach 1-2 kbps, however, to support voice call, a minimum of 4.75 kbps is required according to the 3GPP standards.
Long Propagation delay: Regarding the VoLTE voice, one cycle of transmission and reception is within 20ms, but due to the limited bandwidth and half-duplex scheduling of IoT-NTN, it is challenging to complete one transmission and reception within 20ms.
Lack of IMS voice function: Exisiting IoT-NTN does not support IMS voice services.
Current RoHC for voice cannot be supported in NB IoT device.

## Slide 3: Voice over IoT-NTN
Solutions
eNB
SBC
I/S/E-CSCF/BGCF
voicce AS
IP-SM-GW
Rx
Mw
ISC
ISC
UE
IoT-NTN
GW
MME
SAE GW
HSS
S6a
S11
SGi(Gm)
EPC
PCRF
SMSC
Gx
PSAP
GEO
VoLTE
SGs
MSC
S1-MME
S1-U
LRF
Architecture
SA2: Enable the connection with IMS and SIP signaling
SA4: Low data rate codec, e.g.,1.2kbps

## Slide 4: Voice over IoT-NTN
Solutions
  Support of UP solution for signaling and data transmission of voice respectively(4G QCI 5 for SIP, QCI 1 for voice traffic).
Table 1 Standardized QCI characteristics of VoLTE |  |  |  |  | 
QCI | Resource Type | Priority Level | Packet Delay Budget | Packet Error Loss Rate | Example Services
1 | GBR | 2 | 100ms | 10-2 | Conversational Voice
2 |  | 4 | 150ms | 10-3 | Conversational Video (Live Streaming)
5 | Non-GBR | 1 | 100ms | 10-6 | IMS Signalling
Support SPS
  For voice service, the packet size is fixed and the arrival interval meets certain rules of real-time services (e.g. a typical voice service cycle is 20ms). To address this feature, SPS is introduced in LTE, which transmits new data according to the pre-configured resources on the specified subframe, but in order to reduce the latency, dynamic scheduling is still utilized during retransmission.
  For voice over IoT-NTN, SPS could be supported.

## Slide 5: Voice over IoT-NTN
Solution
Support ROHC
  For NB-IoT, to improve bandwidth utilization is important, therefore, to support ROHC for voice packets could be discussed. And the existing ROHC mechanism for VoLTE could be considered.
Figure 1. An example ROHC for VoLTE
Objective
RAN
  Support of UP solution for signaling and data transmission of voice respectively(4G QCI 5 for SIP, QCI 1 for voice traffic)
  Introduce of SPS in IoT-NTN for voice service
  Support of RoHC Profile0x0001 for PDCP header compression (RTP+UDP+IP for VOLTE packet)

## Slide 6: Thanks!