## Slide 1: Views on Rel-20 AI/ML for NG-RAN CMCC
3GPP TSG RAN Meeting#107 RP-250259
Incheon, KR, Mar. 12-14, 2025
Agenda: 15.2.6
Document for: Discussion

## Slide 2: Motivation
RAN3 has already worked on the benefits, solutions, and potential standard impacts of AI/ML-based Energy Saving, Load Balancing, Mobility Optimization, Network Slicing, Coverage and Capacity Optimization (CCO) and NR-DC in Rel-17/18/19
In RAN#106, RAN Chair’s Summary of 5G-Advanced in Rel-20 has the following recommendation:
Based on the RAN Chair’s Summary, the Rel-19 leftovers will be treated with high priority, and the new use cases studied in Rel-20 will be limited.
For the additional new use cases, considering that some new use cases were proposed in Rel-19, but were not included in the Rel-19 WI scope due to the limited time, including QoE optimization and multi-hop UE trajectory prediction, the study/normative work of Rel-20 can take these use cases into account

## Slide 3: Study on Potential New Use Cases
New use cases need to be studied first for AI/ML-based solutions in Rel-20, with 6 months SI same as Rel-19
Potential Objectives:
  Study the AI/ML-based solutions for new use cases (including non-split architecture and split architecture), e.g. QoE optimization, Multi-hop UE trajectory prediction, etc.:
    Study standardization impacts for the new use cases including: the data that may be needed by an AI model as input, data that may be produced by an AI model as output, and feedback data, which is interpretable for multi-vendor support
    Study standardization impacts on the node/interface in current NG-RAN architecture to convey the input/output/feedback data among nodes
Proposal 1: The QoE optimization and multi-hop UE trajectory prediction are proposed to be studied in Rel-20

## Slide 4: Proposal for AI/ML for NG-RAN WI
The normative work of Rel-20 new use cases and Rel-19 leftovers will be discussed in the follow-up WI after Rel-20 SI finished
Potential Objectives
  Specify data collection enhancements and signaling support within the existing NG-RAN interfaces and architecture (including non-split architecture and split architecture) for new use cases, including:
    QoE Optimization
    Multi-hops UE trajectory across gNBs
  Support of Rel-19 leftovers, if any
Proposal 2: It’s proposed RAN to take the above as baseline to discuss potential objectives for Rel-20 WI

## Slide 5: Potential New Use Case - QoE Optimization
AI-based QoE performance guarantee during mobility: (focus on RVQoE)
  QoE prediction for resource allocation, e.g. whether more resources are needed to guarantee enough buffer and prepare in advance
  Maintain user experience during handover
QoE measurements collection for prediction validation
  Collect QoE related measurements/metrics after handover to evaluate AI/ML model
  Resource reallocation after handver
  Analyze whether more RVQoE metrics need to be introduced and collected for AI, if needed
RAN-visible QoE information reporting
Example: Signalling procedure for AI-based QoE Optimization

## Slide 6: Potential New Use Case - Multi-hop UE trajectory Prediction
UE trajectory prediction transmission:
  UE Trajectory prediction (including prediction of multi-hops) transmission across gNBs, e.g. from one node to the next hop node in order
  UE trajectory prediction validity information, to avoid confusion caused by outdated prediction information
Measured UE trajectory collection
  Node/Cell level measured UE trajectory
  Measured UE Trajectory collection mechanism, e.g. from one node to the previous hop node in order
Multi-hop UE trajectory across gNBs
Example: Signalling procedure for multi-hop UE trajectory

## Slide 7: Thank you