## Slide 1
CMCC
Views on ISAC for Rel-20
3GPP TSG RAN Meeting #107
Incheon, Korea, March 12-14, 2025
Agenda item: 15.2.9.1
RP-250261

## Slide 2
ISAC scenario in Rel-19
The study on ISAC in Rel-19 (RP-234069) is to define channel modelling aspects to support object detection and/or tracking the following sensing targets:
UAVs
Humans indoors and outdoors
Automotive vehicles
Automated guided vehicles
Objects creating hazards on roads/railways

## Slide 3
Requirement and capability of sensing for UAV
Requirement
  Sensing
    RCS: 0.01m2
    Coverage: 10m~1000m
    Velocity range: 5~100km/h
    Latency: ≤1000ms
  Reliability
    Missed detection: 5%
    False alarm: 5%
  Accuracy
    Positioning: ≤10m
    Range resolution: 10m
    Angular accuracy: 1o
Test of protype
  Sensing
    RCS: 0.01m2
    Coverage: 1000m
  Accuracy
    Positioning: meters level
Target-1
Taget-2
Sensing coverage
Positioning accuracy
Range resolution
False alarm
Communication
Sensing

## Slide 4
Requirement and capability of sensing for V2X
Requirement of objects creating hazards on roads
  Sensing
    Coverage: 10m~1000m
    Latency: ≤1000ms
  Reliability
    Missed detection: 5%
    False alarm: 5%
  Accuracy
    Positioning: 1m~2m
    Range resolution: 1.5m
Test of protype
  Sensing
    Lane level sensing
  Accuracy
    Positioning: meters level
Requirement of sensing vehicles and humans
  Sensing
    Coverage: 10m~1000m
    Latency: ≤100ms
  Reliability
    Missed detection: 5%
    False alarm: 5%
  Accuracy
    Positioning: 0.5m~1m
    Range resolution: 0.5m~1.5m
    Angular accuracy: 0.2o
    Velocity accuracy: 1m/s
  Observation 1: Low latency is a critical and challenging requirement for sensing.

## Slide 5
The study of ISAC should firstly consider the data type for evaluation. The data type is highly related to the interface and architecture. Three kinds of sensing architecture can be considered.
Option 1: Core network-side sensing architecture
  SF (sensing function) is located at core network.
  Sensing measurement (such as delay, Doppler, angle) is transmitted from gNB to core network, and sensing result (such as position and velocity of sensing target) is calculated at SF in core network.
  Sensing evaluation is based on sensing measurement.
Transmission overhead: The transmission overhead from gNB to core network is high.
Low latency requirement: Core network-side sensing architecture may not satisfy the low latency requirement, such as ≤100ms for V2X.
  Observation 2: High transmission overhead and sensing latency are identified for core network-side sensing architecture.
Core network-side sensing architecture

## Slide 6
Option 2: BBU-side sensing architecture
  SF is located at BBU side.
  Sensing raw data is transmitted from AAU to BBU, sensing measurement (such as delay, Doppler, angle) is transmitted from BBU to SF, and sensing result (such as position and velocity of sensing target) is calculated at SF.
  Sensing evaluation is based on sensing measurement.
  Data consistency and integrity: The sensing result calculated in SF is based on the sensing measurement, we may further consider the sensing data non-consistency and non-integrity caused by measurement error.
  Observation 3: The sensing data non-consistency and non-integrity caused by measurement error should be considered for BBU-side sensing architecture.
BBU-side sensing architecture

## Slide 7
Option 3: AAU-to-BBU interface for sensing data collection
  Define the interface from AAU to BBU (backward fronthaul only).
  Sensing data is collected at the interface from AAU to BBU.
  Whether/how to quantize the raw data may need further discussion, and sensing evaluation is based on the quantization value.
  Less transmission nodes to satisfy the low latency requirement.
  The sensing data consistency and integrity could be ensured to improve sensing reliability.
  Proposal 1: Study AAU-to-BBU interface for sensing data collection.
AAU-to-BBU interface for sensing data collection

## Slide 8
Overall consideration for ISAC
In RAN Chair’s Summary of 5G-Advanced in last meeting, it points out a study needs to be avoided duplicate scope in 5G-Advanced and 6G in Rel-20. Thus, the study of ISAC for 5G-Advanced should avoid overlap with the corresponding 6G study. Furthermore, considering the deployment requirements of ISAC in both 5G-A and 6G, the study of ISAC should be designed to be compatible for both 5G-A and 6G.
  E.g., the specifications of 5G-A are 38 series, while the specifications for 6G are 40 series, so, we may consider to use the specification of 39 series for Rel-20 ISAC, which could be compatible for both 5G-A and 6G.
Now, companies have not anticipated the negative impacts of 5G-A ISAC, and proponents believe the RAN1 evaluation results are generally positive. In fact, the RAN3-led ISAC should be based on validated RAN1 evaluations, the information exchanged via RAN3 interfaces would neither represents an urgent issue requiring immediate resolution nor pose a bottleneck for commercial deployment.
  E.g., In operator’s live network testing, the sensing result calculated by the SF deployed inside BBU can meet commercial requirements, so the ISAC currently can be supported by gNB implementation.
In addition to the study of physical layer aspects of ISAC, the study of ISAC should additionally consider the data type for evaluation. The data type is highly related to the interface and architecture. Therefore, a comprehensive study that addresses the physical layer aspects, data consistency, interface and architecture of ISAC should be considered in Rel-20.
  Proposal 2: The study of ISAC for 5G-Advanced should avoid overlap with the corresponding 6G study, e.g., consider to use the specification of 39 series for Rel-20 ISAC, which could be compatible for both 5G-A and 6G.
  Proposal 3: The RAN3-led ISAC should be based on validated RAN1 evaluations, the information exchanged via RAN3 interfaces would neither represents an urgent issue requiring immediate resolution nor pose a bottleneck for commercial deployment.
  Proposal 4: Comprehensive study that addresses the physical layer aspects, data consistency, interface and architecture of ISAC should be considered in Rel-20.

## Slide 9
THANK YOU !