## Slide 1: Abandon or Maintain 5G CU–DU interface? L3 measurement based LTM handovers and RAN 3
3GPP RAN Plenary#107
Vodafone
RP-250278

## Slide 2: Background on L1/L2 Triggered Mobility (LTM)
Intra-CU LTM is one of the main features of Release 18. It provides the possibility to significantly reduce interruption time during handover.
Release 19 extends it to inter-CU case.
To achieve the improvements, the UE does an early synchronization of the DL and UL with the target cell, and the switch to the target cell is commanded by a MAC CE Switch command.
LTM functionality is based on measurements sent in L3 and/or L1 signalling for FR1:
  Agreement from R4#111 RRM session chairman nodes: “For FR1, the cell switch delay requirement is applicable for the case without L1 measurement and report, under certain conditions.”
Interruption time requirements are described in section 6.3.1 of 38.133 and are valid for both L3 and L1 measurement based LTM

## Slide 3: RAN 3 issue related to L1/L2 Triggered Mobility (LTM)
  “L3 measurements” are sent in RRC signaling that terminates in the CU.
  “L1 measurements” are sent in UCI signaling that terminates in the DU.
  The DU is responsible for sending the Early Sync Instruction and MAC CE Switch Command to the UE.
  With “L3 measurements”, the unresolved problem in Release 18 is whether the CU or the DU is in control of the LTM execution.
  The same issue applies to Release 19 inter-CU LTM
  RAN 3 has discussed this issue over several meetings, analyzing multiple options, but has not reached consensus.
      The consequence of this is that one of 3GPP’s open interfaces will become CLOSED.
      We believe that the closing of an open interface is an issue for RAN plenary to discuss.
Proposal:
  As there has not been any discussion on closing the 5G CU-DU interface in RAN plenary, it is proposed that RAN plenary requests RAN 3 to find a solution for multi-vendor operation.

## Slide 4: Technical options in RAN WG 3

## Slide 5: RAN 3 options related to L1/L2 Triggered Mobility (LTM)
Based on LS (R2-2407606, R2-2409373), RAN WG3 discussed several alternatives:
  Option1: CU based solution (L3 measurements are sent to CU and CU instruct DU to initiate DL and/or UL Early Synchronization and/or Switch command to the UE)
  Option2: DU based solution (CU provides L3 measurements to DU and DU initiates DL/UL Early Synchronization and Switch command)
  Option3: Hybrid Solution (i.e., support F1-AP signaling enhancements for both CU and DU based solutions and it is up to implementation to choose CU or DU based solution as way forward)
  Option4: No Solution (i.e., it is left up to implementation of F1-AP)
RAN3 decided to go with option 4: LS in R3-250879 was sent to RAN2, CC: RAN4, RAN
  RAN WG3 has discussed the solutions, however does not reach a consensus to specify the support for L3 measurement based LTM for CU/DU distributed architecture. As a result, F1 support for L3 measurement based LTM will not be specified in Release 18.