## Slide 1: 3GPP NTN roll-out status
Sources: Thales, Hispasat, Iridium, Sateliot, EchoStar, Omnispace, Eutelsat Group, Thuraya, SES, Viasat, Terrestar, Ligado, Intelsat, Skylo, JSAT, Novamint
3GPP TSG RAN Meeting #107 RP-250302
Incheon, Korea, March 12-14th, 2025
Agenda: 15.2.8.4 5G-Advanced in Rel-20 – NR-NTN
For: Discussion

## Slide 2: NTN targeted market segments
Enterprise market:
  Need for services in rural areas or less developed areas and moving platforms;
  Unique UE for both NTN/TN;
  Similar use cases to today (e.g. office, media & entertainment);
  As the technology becomes cheaper and compact and easier to access, the adoption is expected to rise.
Vertical markets:
  Transportation (aeronautic, maritime, railway, land), Utilities, agriculture (e.g. sensors), governmental users (e.g. broadband communication);
  Specific requirements: e.g. sensor data collection over a wide area, autonomy, security, resilience and mobility;
  Several millions of users are expected to require satellite connectivity.
Consumer market:
  Includes connectivity to smartphones or wearable devices & cars;
  Need for guaranteed coverage;
  By 2030, at least:
    7.5% of the total number of mobile subscribers (5.2Bn) expected to be NTN;
    5% of the new cars (~75 million per year) are expected to be NTN capable.

## Slide 3: 3GPP NTN technology roll-out
A
2024
2025
2026
2027
2028
2029
2030
D
B
E
C
Scenarios | A | B | C | D | E | F
Service | IoT-NTN, Messaging & voice |  |  | Broadband |  | 
3GPP NTN RAT | IoT-NTN | IoT-NTN | IoT-NTN | NR-NTN | NR-NTN | NR-NTN
Orbit | GSO | NGSO | NGSO | NGSO | GSO | NGSO
Duplex mode | FDD | FDD | TDD | FDD | FDD | FDD
Payload | Transparent | Transparent/Regenerative |  |  | Transparent/Regenerative | Transparent/Regenerative
Bands | Below 7.125 GHz (e.g. L/S bands) |  |  |  | Above 10 GHz (e.g. Ku/Ka band) | 
Targeted devices | IoT & Smartphones (D2D) |  |  | Smartphones | Fixed and Mobile VSAT | 
Potential SNOs | EchoStar Viasat/Inmarsat Ligado TerreStar Solutions Thuraya Skylo | Sateliot EchoStar OmniSpace | Iridium | EchoStar, Viasat, Ligado, Thuraya | Eutelsat Group Hispasat Intelsat, Ovzon, SES, Intelsat, JSAT | SpaceRISE Eutelsat Group, Intelsat
F
Earliest service opening for each scenario (and related 3GPP releases)
Deployment scenarios
Rel-17
Rel-18/19
Rel-19
Rel-17/18
Rel-17/18/19
Rel-18/19

## Slide 4: Proposed way forward
Observation:
  3GPP NTN technology is being rolled out for all the targeted deployment scenarios
Proposal:
  TSG-RAN to consider enhancements for both IoT-NTN and NR-NTN as part of the Rel-20 5G advanced track

## Slide 5: Questions ?