## Slide 1: AI/ML MU MIMO use case for R20
T-Mobile USA
RAN#107
March 5-7, 2025 Incheon Korea
RP-250325, Agenda Item 15.2.1

## Slide 2: Need to study/specify MU MIMO use case
Approved RAN Chair’s Summary of 5G-Advanced in Rel-20 (RP-2503292) allows for new AI/ML use cases to included in R20.
  Strong need to explore new use cases in Rel-20 for 5G-Advanced or not?
    If so, these new use cases should be very limited.
    Study of these new cases is expected to convert to normative work in Rel-20.
    How to avoid overlapping with 6G study?
MU MIMO dramatically improves cell spectral efficiency

## Slide 3
Overview
CONFIDENTIAL
Uplink channel sounding
  Sounding Reference Signals (SRS)
Downlink common reference signals (CSI-RS)
  Type 1 CSI codebook
    Standard resolution CSI feedback
    Suitable for SU-MIMO
    Extensions: Single/ multiple panel, precoded CSI-RS
  Type 2 CSI codebook
    High resolution CSI feedback targeting MU-MIMO
    Extensions: Port selection, precoded CSI-RS
SRS
Type 2 CSI
Type 1 CSI
MU-MIMO
SU-MIMO
Coverage Area, Mobility,UE Support
Combine AI/ML with CSI-RS Type 1 to get the same, or better, performance than type 2 for MU MIMO.
  It is very difficult to get MU-MIMO with CSI-RS type 1 codebook
    CSI-RS type 1 has been widely deployed
    While high resolution feedback CSI-RS type 2 is suitable for MU-MIMO it has not been deployed and has higher overhead.
  Using AI/ML technique to guide UE in estimating MU-MIMO channel based on the transmitted CSI-RS; then feed RI and PMI back to gNB
Extend similar AI/ML technique(s) to guide gNB on selecting SRS beam-based MU-MIMO as well

## Slide 4
Overview

## Slide 5
Overview
CSI-RS calculation is shown below, the codebook type II is made up of multiple codebook type I formula and amplitude scaler which are linearly combined.
Each components of the equation can be further described as below.

## Slide 6
Add objective the SID/WID
Study/specify AI/ML methods that combine AI/ML with CSI-RS Type 1 to get the same, or better, performance than type 2 for MU MIMO.
Proposal