## Slide 1: Ambient IoT objectives for R20
T-Mobile USA
RAN#107
March 5-7, 2025 Incheon Korea
RP-250331, Agenda Item 15.2.7

## Slide 2: Ambient IoT
Per the endorsed WG chair summary of the 5GA workshop (RP-243292)
  A WG-level work item is expected in Rel-20, with details depending on the progress of Rel-19
Need to differentiate between a UE that is not present, out of coverage and doesn’t have enough battery to respond to a page
  The detailed signaling procedures for battery-less A-IoT devices (Type 1 and Type 2a) should be defined.
    Paging procedure:
      Rel. 19: A-IoT paging message contains an identifier or group ID mapped to multiple A-IoT devices to trigger the communication. It is assumed that the corresponding A-IoT devices can receive the paging message and give response.
      Rel 20: Type 1 or Type 2a A-IoT devices need to be energized before they can respond to the paging message. The paging messages would not be responded if the devices are out of energy or outside the range. There should be an initialization procedure for the reader to identify which devices are reachable before sending out paging messages.
      Paging every device multiple times is ineffective in networks with millions of devices and in networks were devices change locations.

## Slide 3: Ambient IoT
Need to Improve Random Access Procedure:
  Detailed signaling procedure should be defined for FDMA access of A-IoT devices for collision avoidance.
  Rel. 19 is mainly focused on contention-based random-access process for TDMA, FDMA access was briefly mentioned, but not much studies have been done.
  Rel. 20: FDMA random access can be much more efficient to avoid collision when there are a large amount of A-IoT devices communicating with readers simultaneously in indoor inventory use cases

## Slide 4: Positioning Solution for Ambient IoT Devices
Based on Rel. 18 TR 22.848, most of ambient IoT indoor use cases require positioning accuracy to be 3m – 5m.
In Rel. 19, the position of ambient IoT devices can be only identified based on the proximity of the devices to the locations of A-IoT readers.
  Current communication range of indoor use cases is 15 m, which mean the position accuracy is only 15 m.
To meet the positioning accuracy requirements, it is important to study the feasible positioning solutions of ambient IoT devices to enable less than 1 meter accuracy.

## Slide 5
Include the following objectives in the R20 WID
  Develop FDMA based contention based random access and contention free random access.
  To meet the positioning accuracy requirements, it is important to study the feasible positioning solutions of ambient IoT devices to enable less than 1 meter accuracy.
  Develop Methods/procedure to improve network paging success by having the UE inform the network when there is sufficient energy to respond to a page.
Proposal