## Slide 1: Views on Rel-20 5G-A AI/ML for air interface enhancements
NTT DOCOMO, INC.
RP-250359
3GPP TSG RAN Meeting #107
Incheon, Korea, March 12-14, 2025
Agenda item: 15.2.1
Document for: Discussion

## Slide 2: Overview
Background
  In Rel-19, CSI compression is studied without normative work
  Rel-20 UE side data collection SA2 SID is expected to be approved in SA
Our view to Rel-20 5G-A AI/ML for air interface
  New AI/ML use cases should be included in 6G study
  CSI compression can be potentially considered as Rel-20 item, although its feasibility and performance gain in the actual field are still questionable
  UE side data collection discussion in RAN should be delayed until SA2 makes progress in Rel-20

## Slide 3: CSI compression
Background
  UPT gain is observed for temporal domain aspects of AI/ML CSI compression
    Case 2 and 3 are prioritized among Case 1-5 in Rel-19
  Each inter-vendor collaboration direction is still under the Rel-19 discussion
    Direction A can provide high performance, although overhead/proprietary/user privacy issue may exist
    Direction B has more feasibility issues than Direction A
    Direction C can eliminate the inter-vendor collaboration complexity and ensure a minimum performance requirement
View
  There is little real/urgent commercial needs of supporting CSI compression, considering the feasibility and performance in each inter-vender collaboration
  If CSI compression is specified in Rel-20,
    Case 3 should be supported, because the large UPT gain is observed
      If the workload is not an issue, Case 2 also can be specified
    Direction A/C should be supported for high performance and testability, respectively
      Supported direction A solution(s) should take user privacy into account
    Related WIs should be RAN1 (leading WG), RAN2, RAN4, SA2 and/or SA5