## Slide 1: Views on UL Coverage Enhancements in Rel-20 5G-A
NTT DOCOMO, INC.
3GPP TSG RAN#107
Incheon, Korea, March 12-14, 2025
Source: NTT DOCOMO, INC.
Agenda item: 15.2.7.1
Document for : Discussion
RP-250363

## Slide 2: “Msg5” Coverage Enhancement
Motivation:
  Until Rel-18, repetition-based coverage enhancements are (to be) specified
    PUSCH after RRC connection
    Msg3 PUSCH
    PUCCH
    PRACH
  Meanwhile, “Msg5 PUSCH” doesn’t support repetition
    “Msg5 PUSCH” is a PUSCH after Msg3 PUSCH and before reception of dedicated PUSCH config
    From specification perspective, “Msg5 PUSCH” is included in “PUSCH scheduled by DCI format 0_0 with CRC scrambled by C-RNTI”
  Without repetition, Msg5 PUSCH can be a significant bottleneck, especially for NTN operation
View:
  Specify repetition for PUSCH scheduled by DCI format 0_0 with CRC scrambled by C-RNTI
Leading WGs: RAN1

## Slide 3: Views on other proposals
PRACH repetition with different beams
  View: Fine to support
    It can be useful for FR2 operation, which is important for 5G-A and 6G from our point of view
    Specifications for Rel-18 PRACH repetition can be almost reused
Improvement of PUSCH coverage for high UL data rate, including extending pi/2-BPSK to more MCS entries in MCS tables
  View: Fine to support
    It is true that the commercial requirement for UL is getting higher
    Specification impacts for supporting this solution seems to be very small and involving a fewer number of WGs (RAN1 only)