## Slide 1: Views on Rel-20 5G-A Mobility enhancements
NTT DOCOMO, INC.
3GPP TSG RAN meeting #107
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.8.1
Document for: Discussion
RP-250364

## Slide 2: Overview on proposed enhancements
L1-SINR measurement quantity for LTM
Enhancements on SCell handling during LTM cell switch
Inter-CU conditional LTM
NG based inter-CU LTM

## Slide 3: L1-SINR measurement quantity for LTM
Motivation
  Rel-18/19 LTM supports cell switch between inter-frequency cells in addition to intra-frequency cells. Also, inter-frequency L1 measurement is supported. Considering cell switch between inter-frequency cells, noise and interference levels would be necessary to select proper target cell. On the other hand, only L1-RSRP measurement quantity is supported. Hence, L1-SINR should be supported in addition to L1-RSRP.
  In Rel-19, support of L1-SINR was discussed but it was not agreed due to concerns on high workload.
Proposal
  Specify support for L1-SINR measurement quantity for L1 measurement and reporting for LTM candidate cells.
    Support both intra-frequency and inter-frequency measurements.

## Slide 4: Enhancements on SCell handling during LTM cell switch
Motivation
  Rel-18/19 LTM supports CA scenario. SCells can be included in an LTM candidate configuration and be part of the target cell group configuration indicated by cell switch command at LTM cell switch.
  However, the SCells would be configured as deactivated, and NW needs to activate them in the target cell after completion of the LTM cell switch.
  Current SCell handling in LTM causes a delay before CA can be used in the target cell, which decreases data throughput and user experience.
Proposal
  Specify support for activation/deactivation of SCells of the target LTM candidate cell configuration during LTM cell switch.

## Slide 5: Inter-CU conditional LTM
Motivation
  In Rel-19, we support intra-CU conditional LTM and also inter-CU NW triggered LTM including non-DC scenario and DC scenarios. We think it is straight forward approach to extend the support of conditional LTM for inter-CU cases.
  Support of inter-CU conditional LTM can be considered in R20. On the other hand, SN change is also an important scenario for dense and small cell deployments. We see benefits on both non-DC and DC scenarios. Therefore, we propose to support inter-CU conditional LTM for non-DC scenario and DC scenario.
  Considering the time limitation, we can down select the scenarios, if needed.
Proposal
  Specify support for inter-CU conditional LTM in following scenarios (arranged in order of priority): [RAN2/RAN3]
    CU is acting as MN when DC is not configured
    CU is acting as SN when DC is configured, and MN is not changed
    CU is acting as MN when DC is configured, and SN is not changed
    CU is acting as MN when DC is not configured, and SN is added

## Slide 6: NG based inter-CU LTM
Motivation
  In Rel-19, we support inter-CU LTM, however, it relies on Xn interface and NG based LTM is not supported.
  Interaction between gNBs over NG interface has longer round trip time than Xn interface based one. On the other hand, LTM can achieve fast triggering and low interruption based on DU decision and early synchronization even if it is NG based. Hence, it is beneficial to support NG based inter-CU LTM for the case there is no Xn connection.
  Considering the time limitation, we can down select this scenario, if needed.
Proposal
  Specify support for NG based LTM [RAN2/RAN3]