## Slide 1
RP-250366
3GPP TSG RAN Meeting #107
Incheon, Korea, 12th to 14th March, 2025
Views on Scope for R20 “AI-ML for Mobility Enhancement in 5G-NR”
Agenda Item: 15.2.4
Source: Tejas Networks
Document for: Discussion

## Slide 2
The existing mobility relies on the present and historical measurements
  The methods based on these measurements suffer from following phenomenon resulting in throughput-loss:
    Ping-pong
    Radio link failure (RLF)
    Hand-over failure (HOF)
    high RS overhead due to RRM measurements
In Rel-19, RAN2 studied the potential of AI-ML for enhancing the mobility. The following use-cases are identified for the study:
  RRM measurement prediction : 6 sub-cases has been identified for the study.
  Measurement event prediction: 2 sub-cases has been identified.
  RLF prediction
Companies studied and submitted promising results for RRM measurements prediction and Measurement event.
Motivation
The measurement event prediction and the RRM measurement prediction should be considered for normative work and the RLF prediction should be studied further in Rel-20 of 5G-NR.

## Slide 3
Predict the beam-specific and cell-specific measurements related to mobility management using AI-ML techniques.
These predicted (future) RRM measurements are used to mobility related decisions with an objective to:
  reduce the number of ping-pong,
  reduce RRM measurement overhead.
Measurement event predictions helps in enhancing the HO execution to
  reduce the throughput-loss due to early HO and,
  reduce HO failure rates.
RLF prediction based on AI-ML offers improved continuity of service by reducing the interruption time.
Consider combining results from different domains, such as temporal, spatial, and inter frequency prediction models for enhanced mobility management.
Proactive Mobility Management based on AI/ML

## Slide 4
The measurement event prediction and the RRM measurement prediction should be considered for normative work and the RLF prediction should be studied further in Rel-20 of 5G-NR.
Proposal 1: AI/ML for Mobility Enhancement Phase 2 [RAN-2 led] to include:
  Enhancements based on event measurement predictions
  Enhancements based on RRM measurement predictions
  Enhancements based on combination of temporal, spatial and inter frequency domains
[RAN-2] AI-ML for Mobility Enhancement Phase 2
Proposal
AI-ML can be used in context of mobility management to
  reduce the number of ping-pong,
  reduce RRM measurement overhead.
  reduce the throughput-loss due to early HO and,
  reduce HO failure rates.
Observation