## Slide 1: Discussion on Rel-20 AI/ML air-interface

## Slide 2: Status on AI/ML for air-interface
AI/ML for air interface
  R19 is expected to support the following
    The following one-sided model use cases
      Spatial and/or temporal domain beam prediction
      Direct AI/ML positioning and AI/ML-assisted positioning
      Temporal domain CSI prediction (UE-sided model only)
    Functionality based LCM framework
      Applicability report
      NW-side data collection
  Study objectives in R19
    The following two-sided model use case
      CSI compression
    Model identification and model transfer
    CN/OAM/OTT collection of UE-sided model training data
    Testability and interoperability

## Slide 3: Discussion on Rel-20 AI/ML air-interface
High level principles
  Duplicated discussion between 5G-A and 6G should be avoided.
  Non-urgent topics from real deployment perspective should be deprioritized.
  Scope/TU of Rel-20 AIML work item (if supported) should be reduced and maintained in a reasonable level(e.g. ~1TU for RAN1) compared to AIML SIs/WIs in previous releases considering that 6G SI is likely to take more than half of the overall TU budget.
Discussion
  Among the considered use cases in previous releases, two-sided model based CSI compression use-case has more practical challenges (e.g. compatibility across different vendors, testability) compared to other one-side model based use cases.
  Two-sided model based CSI compression use-case would require much larger specification impact including model identification and model-based LCM which would fit better to 6G.

## Slide 4: Potential candidates for Rel-20 AI/ML for air-interface
.
#1. Left-over for Positioning
  Motivation:
    AI/ML based positioning has high potential to improve NR based positioning accuracy.
    For 2nd priority Case 2a/2b, they were not discussed during Q4 of 2024 and there was no further progress on these use cases in RAN1#120. Therefore, considering that only two meetings left for Rel-19, these use cases seem difficult to be completed in Rel-19.
      Direct AI/ML positioning:
        (1st priority) Case 1: UE-based positioning with UE-side model, direct AI/ML positioning
        (2nd priority) Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
        (1st priority) Case 3b: NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning
      AI/ML assisted positioning
        (2nd priority) Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
        (1st priority) Case 3a: NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning
    Assuming that 1st priority cases are well supported in Rel-19, the additional work for Rel-20 seems small.
    No overlap with 6G SI is expected.
#2. CSI prediction with NW-sided model
  Motivation:
    CSI prediction is beneficial to mitigate CSI aging problem and/or to reduce CSI-RS and CSI reporting overhead.
    The inference operation for CSI prediction can be done at either UE-side or NW-side. However, only UE-side model has been considered in 3GPP mainly due to lack of time.
    CSI prediction using NW side model is an attractive option for operators and NW vendors, and expected specification impact is small compared to UE sided model, e.g. NW-side data collection.

## Slide 5: Proposals
Proposal for Rel-20 AI/ML for air-interface
  Rel-20 5G-A focus on the following use cases
    Positioning left-over (i.e. Case 2a/2b)
    CSI prediction with NW-sided model
  The following topics are discussed in Rel-20 6G SI
    Two-sided model based use cases including CSI compression and new use-cases (e.g. RS overhead reduction)
    AIML framework that may support model identification/LCM and model transfer.
.