## Slide 1: Discussion on Rel-20 AI/ML mobility

## Slide 2: Status on AI/ML for mobility
AI/ML for mobility
  R19 is expected to complete the study of the following
    RRM prediction, focusing on sub-use case 2 for measurement event prediction
      3 sub-use cases are considered for cell-level RRM measurement prediction:
        Sub-use case 1: L1 beam-level measurement result(s) is predicted based on actual L1 beam-level measurement result(s) and then L3 cell-level measurement result is generated
        Sub-use case 2: L3 Cell-level measurement result(s) is predicted based on actual L3 cell-level measurement result(s)
        Sub-use case 3: L3 Cell-level measurement result(s) is predicted based on actual L1 beam-level measurement result(s)
      3 sub-use cases are considered for beam-level RRM measurement prediction:
        Sub-use case 4: L1 filtered beam-level measurement result(s) is predicted based on actual L1 beam-level measurement result(s) and then L3 beam-level measurement result is generated
        Sub-use case 5: L3 beam-level measurement result(s) is predicted based on actual L3 beam-level measurement result(s)
        Sub-use case 6: L3 beam-level measurement result(s) is predicted based on actual L1 beam-level measurement result(s)
    Measurement event prediction
      Prediction of event satisfaction for event A1-A5(A3 as starting point)
      The RRM prediction results are used for measurement event prediction, i.e., indirect prediction is baseline.
      Output:
        Probability of event occurrence within a time window (direct)
        Expected occurrence time of a measurement event satisfaction (indirect)
  RAN2 has agreed that RLF prediction will not be studied in Rel-19

## Slide 3: Discussion on Rel-20 AI/ML for mobility
High level principles
  Duplicated discussion between 5G-A and 6G should be avoided.
  Non-urgent topics from real deployment perspective should be deprioritized.
  Scope/TU of Rel-20 AIML work item (if supported) should be reduced and maintained in a reasonable level(e.g. ~1TU for RAN2) considering that 6G SI is likely to take more than half of the overall TU budget.
Discussion
  Use cases for normative work
    Work scope should be strictly limited to use cases well studied in Rel-19 AIML Mobility SI, in order to mange the normative work with minimal uncertainty.
    That is, normative work should only address the use cases of RRM prediction and Measurement report event prediction, as specified in TR 38.744.
  Procedures for AIML mobility
    Modification/extension of existing procedures should be the prioritized, whenever possible, instead of specifying entirely new procedures.
    For RRM prediction and event prediction, existing measurement and measurement reporting procedures in TS 38.331 can be extended.
  For LCM, Rel-19 LCM framework can be reused as much as possible.

## Slide 4: Potential candidates for Rel-20 AI/ML for mobility
.
#1. RRM prediction
  Motivation:
    Observations from the simulation:
      Reliable Prediction Accuracy: AIML-based RRM prediction achieves acceptable accuracy in time, spatial, and frequency domains.
      Improved Inter-frequency Prediction: Cluster-based approaches enhance accuracy over single-cell and pathloss offset methods.
      Outperformance Over Non-AI Methods : In time domain prediction, AIML outperforms sample-and-hold, with larger gains for longer PW
      Measurement Reduction Gains : Measurement reduction is observed in intra-frequency intra-cell and inter-frequency predictions
      Generalization : AIML models generalize well across UE speeds and frequencies, with GC#2 showing superior performance.
    AIML-based RRM prediction can enhance accuracy, reduce overhead, and demonstrate strong generalization, making it well-suited for a normative work
      #2. Measurement event prediction
  Motivation:
    Observations from the simulation:
      Reusability of RRM model : RRM measurement prediction model can be reused, ensuring consistency and efficiency
      Indirect Prediction Performance: Indirect prediction for intra-frequency temporal domain case B offers strong results with minimal overhead
      High Accuracy: AI/ML-based prediction shows high F1-score, improving precision and recall, outperforming baseline methods
      Handover Improvement: AI/ML-based prediction reduces handover failure rates, enhancing network performance
    The improvements in prediction accuracy and efficiency make measurement event prediction a strong candidate for a normative work.

## Slide 5: Proposal
Proposal for Rel-20 AI/ML for mobility
  Rel-20 5G-A focus on the following use cases
    Cell-level RRM prediction
    Measurement event prediction
  The following topics are discussed in Rel-20 6G SI
    RLF prediction and other Mobility enhancement (e.g., AI-assistant LTM/CHO)
.