## Slide 1: Conditional LTM for DC case
3GPP TSG RAN Meeting #107 RP-250416
Incheon, Korea, March 12-14, 2025
Agenda Item: 9.3.2.1
Source: Lenovo
Document for: Discussion

## Slide 2: Mobility Enhancement
  Progress for Rel-19 Objectives:
  Three objectives (i.e., Inter-CU MCG/SCG LTM, Measurements related enhancements, Intra-CU MCG conditional LTM) are included in current Rel-19 mobility. Most of main issues have been addressed already on top of Rel-18 Intra-CU MCG/SCG LTM. Therefore, the work goes on smoothly in RAN1, RAN2 and RAN3.
  Intra-CU MCG conditional LTM supporting subsequent LTM and RACHless have been supported. The main issues of LTM condition and early TA delivery have been addressed already.
  Checkpoint:
  According to WID, whether Intra-CU conditional LTM can be specified to DC scenarios should be checked at RAN#107.
Observation 1: The work for Rel-19 Mobility goes on smoothly in RAN Groups.
Observation 2: Whether Intra-CU conditional SCG LTM can be specified should be checked at RAN#107 according to WID.

## Slide 3: Mobility Enhancement
  Intra-CU SCG conditional LTM:
  In Rel-18 Intra-SN SCG LTM, only intra-SN SCG LTM without MN involvement is supported. Therefore, only SN initiated Intra-SN SCG LTM conditional LTM without MN involvement can be supported for Rel-19.
  L1/L3 condition for Intra-CU MCG CLTM can be reused for Intra-CU SCG CLTM .
  Subsequent LTM:
    For both cases w/o SRB3, the signaling flow for SN initiated SCG LTM without MN involvement in 37.340 can be reused.
    The enhanced F1 interface for Intra-CU MCG CLTM can be reused for Intra-SN SCG CLTM e.g., to generate L1/L3 condition for initial LTM and subsequent LTM.
  RACH-less based Intra-CU MCG CLTM can be reused for Intra-CU SCG CLTM. Namely, the mechanism for early sync and TA based measurement can be reused.
  Based on the above analysis, there are no big issue for supporting Intra-SN SCG CLTM on top of Rel-18 Intra-SN SCG LTM and Rel-19 MCG CLTM. If additional issues are observed, Intra-SN SCG CLTM can be skipped in Rel-19.
Proposal 1: Conditional Intra-CU SCG LTM can be supported in Rel-19 only if the current mechanisms for Rel-18 Intra-SN SCG LTM and Rel-19 MCG CLTM can be reused without additional enhancement.

## Slide 4: Thanks
thanks