## Slide 1
Huawei, HiSilicon
Rel-20 Mobile AI/XR (XR-like) use cases and work scope
3GPP TSG RAN#107 RP-250454
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.8.2

## Slide 2
Status Quo of XR Enhancements in 3GPP
Rel-18 XR
XR awareness:
  CN/UE provide XR-specific information to NG-RAN to make it aware of PDU sets or data bursts. NG-RAN provide congestion information to CN for congestion mitigation.
Power saving enhancements:
  NG-RAN provide rational number for DRX short and long cycle.
  The HARQ RTT timer can be disabled per CG configuration to get power saving gain.
Capacity enhancements:
  To help the network be aware of the UL PDU sets/data burst information, the DSR procedure is introduced.
  To support PDU set based handling for UL, the PDCP discard procedure is enhanced.
R18 - XR awareness
Rel-19 XR
Support for multimodality in RAN for UL and DL
  Multi-modality awareness
Enhancements to enable transmission/reception in gaps/restrictions that are caused by RRM measurements
  DCI indicate the RRM measurement can be skipped
Enhancements for uplink scheduling
RLC re-transmission related enhancements
Uplink rate control based on MAC CE
R19 – Multi-Modality XR
RAN chair summary of Rel-20 5G-A workshop in RP-243292
Additional RAN2-led Candidate Topics

## Slide 3
Fast Growth of mobile AI traffic requires 5G-A solution
Emerging mobile AI Services and AI devices
Driverless taxi is already in operation in 11 major cities in Mainland China, including 1000+ Robotaxi in Wuhan by 2024.
① AI wearables (e.g. AI glasses) with large AI model at cloud
AI phone | HUAWEI Mate 70 | Apple iPhone 16 | Magic 7 | Galaxy S24
Large Model | PanGu | GPT-4o | DeepSeek | Gemini
③ Automated Driving vehicle (e.g. driverless taxi) with local AI model
Observation 1: Mobile AI related traffic has already emerged in operators' networks and is experiencing exponential growth. Mobile AI applications have been integrated with various devices including mobile phones, glasses, vehicles, etc.
② AI smartphones with LLM at cloud
In addition to generative AI embedded in smartphones and other devices, there are numerous AI applications available on app stores, many of which are highly popular.
AI applications are experiencing explosive growth. AI applications are already widely integrated into current 5G devices, and it is highly likely that AI applications will be widely used by 2027
  According to a June 2024 report, there are approximately 20,000 AI-related applications available on Google and Apple app stores.
  Global AI chat app downloads in 2023 grew more than 14 times compared to the previous year, reaching nearly 1.6 billion downloads.
  According to a research report by Quest Mobile [1], by September 2024, the monthly active users of AIGC apps increased by 393.9% year-over-year.
  In October 2024, Waymo One is providing over 150,000 paid trips, marking a 200% growth over just five months.
AI Glass | Meta Ray-Ban | Rokid Glasses | Brilliant Labs Frame
Large Model | Meta Llama3 | Tongyi Qianwen | ChatGPT
Reference | Link | Link | Link

## Slide 4
Mobile AI Traffic and Requirements
Non-video(Voice/image/text) traffic in mobile AI services
Video traffic in mobile AI Services
Intelligent voice/Image/text interaction: Large Language Models (e.g. ChatGPT/Doubao, etc) have become personal AI assistants
Cloud-based photography: post-processing for photos
Intelligent real-time video interaction: Chat GPT supports Real-time video interaction
Autonomous driving: Driverless taxi needs to upload real-time video for on-vehicle AI model performance monitoring and remote take-over when needed
Stringent latency requirement
Burst data triggered by AI tasks
Stringent latency requirement
Constant high data rate video transmission
AI services generate a substantial amount of traffic in networks, including various forms such as video, voice, images, text and etc.
To enable AI to respond in a human-like manner, the total delay for an AI process needs to be limited to, e.g. 300 ms. However, AI inference typically consumes the majority of this time (e.g., more than 200 ms), leaving only a small latency budget for network communication.
Observation 2: Mobile AI services cover real-time video traffic and non-video traffic, such as voice, image, and text.
Observation 3: The existing R18/R19 XR enhancements, which are defined based on real-time video traffic characteristics, can be reused for mobile AI video traffic.
Observation 4: Mobile AI non-video traffic, including voice, image, and text, also demands strict latency control, yet there have been no relevant enhancements for this type of traffic so far.

## Slide 5
Mobile AI Non-video (voice/image/text) transmission
Key Difference between mobile AI non-video transmission and Real-time video transmission
To ensure the latency of the entire AI application layer data, it is straightforward to reuse “PDU set” concept and DSR mechanism for RAN delay awareness:
  All IP packets of the application layer UL mobile AI data are considered to be within a single PDU set,
However, existing PDU set and DSR mechanisms are defined based on real-time video traffic characteristics. Due to different transport layers and different traffic characteristics, there are problems in reusing PDU set and DSR mechanisms for mobile AI non-video data:
  Mobile AI non-video data relies on a reliable transport layer, so the PDCP discard timer should be disabled (i.e., set to infinite) as a standard configuration.
  Mobile AI non-video packets are scattered and arrive at the UE AS buffer at different times.
XR/Mobile AI
Real-time video data
Mobile AI Non-video data
To achieve round-trip interactive latency that is close to human reaction, it is crucial to minimize the uplink transmission delay of AI metadata.
For uplink transmission, the key difference between XR real-time video and mobile AI non-video traffic is at transport layer:
  Mobile AI non-video transmission is based on reliable transport protocol with congestion control (e.g., TCP/QUIC)
  Existing XR enhancements are for Real-time video, which is based on protocol without congestion control (e.g. UDP)
Observation 5: Existing XR enhancements (such as PDU set, DSR) are defined based on Real-time video traffic characteristics. It is problematic to directly apply existing XR enhancements to mobile AI non-video traffic. Adaptation enhancements should be considered.

## Slide 6
Enhancements for Mobile AI Non-video traffic
Uplink AI Data Awareness
Extend PDU set concept to support AI uplink data, and make RAN aware of uplink AI PDU set.
Options to make RAN aware of uplink AI PDU set:
  Option 1: Enhance DSR by considering disabled PDCP discard timers and scattered packets of a PDU set.
  Option 2: Extend DL “PDU Set Size”/“End of PDU set” indicators to uplink. In downlink R19 XR enhancement, it has been supported to send the identified “PDU Set Size”/“End of PDU set” to gNB by UPF to enable PDU Set based QoS handling by gNB.
Proposal: Extend PDU set concept to support AI service uplink data.
Proposal: RAN to specify the solution to make RAN aware of uplink AI PDU set information.
0
1
2
T
…
0
1
2
T
…
Scheduling
based on PDU set info
By being aware of the uplink AI PDU set, gNB can schedule the packets based on the whole uplink AI PDU set size and the arrival time of the first packet in the PDU set.
Scheduling
without AI PDU set info

## Slide 7
Mobile AI/XR Real-time Video traffic
Existing video traffic in mobile AI/XR services
Mobile AI real-time video
  Chat GPT Video interaction: Real-time video is uploaded to cloud and AI provides responses per users’ requests.
Autonomous vehicle
  Driverless taxi (e.g. Robotaxi): Real time video (~20Mbps) needs to be uploaded to operation center for on-vehicle AI model performance monitoring and remote take-over when needed.
Advanced XR devices
  XR devices are upgraded to higher resolution (e.g. 8K) and higher data rate (up to 100Mbps).
AI traffic
（real-time video uploading）
Chart: 
| 3 | 4 | 5 | 6 | 7
用户SLA满足率 | 0.901 | 0.823 | 0.793 | 0.752 | 0.7
# of UEs per cell
Traffic @ 20Mbps,15ms
UL User Satisfaction Ratio
DL User Satisfaction Ratio
XR 8K
(Cloud Gaming)
Chart: 
| 3 | 4 | 5 | 6 | 7
用户SLA满足率 | 0.9593 | 0.9356 | 0.897 | 0.8546 | 0.7941
# of UEs per cell
Traffic @ 100Mbps,10ms
Observation 6: The number of satisfied users for Mobile AI/XR real-time video services that can be supported within a cell is extremely limited. Improvements are required to increase this number.
Remote Take Over
(real-time video uploading)
Chart: 
| 2 | 3 | 4 | 5 | 6 | 7
用户SLA满足率 | 0.923 | 0.869 | 0.795 | 0.759 | 0.723 | 0.669
# of UEs per cell
Traffic @ 20Mbps,15ms
UL User Satisfaction Ratio

## Slide 8
Potential enhancements for Mobile AI/XR video traffic
N3 delay measurement
Motivation: For XR services, all PDU sets are buffered on the same RLC bearer with a single L2 queue
Same configuration (e.g., RLC mode) for all PDU sets even with different PSIs
Inefficient scheduling due to difficulty of identify the exact importance of data in the L2 buffer
The data with different level of importance have to be treated in a equal way in congestion scenario
Separate L2 queue
Configuration restriction
Scheduling restriction
Enhancement: PDU set level differentiation of L2 queue management
Motivation: There may be variable N3-jitter for cloud XR frames in real deployment.
The CN-PDB (based on the maximum N3-delay) may result in an overly tight AN-PDB for the majority of data that arrived earlier at the RAN, resulting in a smaller number of satisfied UEs.
E.g. configure different RLC bearers per DRB for XR service, with each bearer associated with a specific PSI
Proposal: RAN to define higher layer enhancements to better support mobile AI/XR video traffic, e.g. N3 delay measurement, separate L2 queue handing per different PSIs, etc.
Min: 5.5ms，max: 17ms
Average Delay: 7.6ms
Packet
Latency(ms)
N3 delay
UPF
Network Test Data of Hangzhou city
Max
Enhancement: The awareness of real-time N3 transmission delay in RAN can help relax RAN scheduling by increasing AN-PDB, thereby increasing the number of satisfied UEs.
Timestamp
PDU set 1
PDU set 2
Without N3 delay awareness PDB = 10ms
N3 Jitter 4ms
With N3 delay awareness PDB = [10, 14] ms
Additional Assumptions:
AN PDB: 10ms
Jitter at RAN: ±4ms

## Slide 9
Issue 1: Limited overall transmission opportunities within tight PDB, where new Tx and reTX will have to compete for every single Tx opportunity.
Motivations
Potential enhancements for Mobile AI/XR video traffic
TX suffers channel fluctuation (peak difference > 10dB) across entire 100MHz bandwidth.
  Note scheduling flexibility may handle similar situation for smaller TX bandwidth (e.g. 20MHz), but for ~100MHz TX, it can hardly avoid fluctuation
Chart: RB
30kHz SCS, 100MHz, CDL-c n=100ns
Issue 2: Single MCS across large bandwidth (at level of ~100MHz allocated bandwidth) cannot match channel fluctuation.
Multiple Concurrent HARQ (MC-HARQ)
Potential spec impact:
Single PDCCH schedules initial transmission(s) and re-transmission(s) with different HARQ process numbers in one transmission opportunity.
Single PDCCH schedules multiple PDSCHs/PUSCHs in frequency domain on the same cell with independent indication of MCS
To address issue 1 and issue 2, potential enhancements:
For A UE in a given transmission opportunity (slot/mini-slot)
Support concurrent transmission of initial transmission and retransmission with different HARQ processes on a single carrier
Support concurrent transmission of multiple PDSCHs/PUSCHs with independent MCS on a single carrier
Current spec, only one HARQ process (either new or retransmitted) per UE on a given slot/mini-slot in a carrier, for both single and two codewords (TX layer > 4)
Proposal: Support single DCI scheduling the followings in a given transmission opportunity on a single carrier
Initial transmission(s) and re-transmission(s) with different HARQ process numbers
Multiple PDSCHs/PUSCHs in frequency domain with independent indication of MCS
Performance evaluation:
Chart: 
| 3 | 4 | 5 | 6 | 7 | 8
Single HARQ | 0.9593 | 0.9356 | 0.897 | 0.8546 | 0.7941
MC-HARQ | 0.9878 | 0.9562 | 0.939 | 0.928 | 0.9098 | 0.89726
User satisfaction ratio (8K XR)
4.9
7.8
Notes: 1. 加一个32 HARQ 进程的增益柱子；

## Slide 10
Summary
The Rel-20 XR and Mobile AI objectives are as follows:
Specify support for mobile AI awareness [RAN2]:
  Extend PDU set concept to support AI service uplink data
  Specify enhancements to make RAN aware of uplink AI PDU set information
Specify enhancements for video transmission to ensure low latency and higher data rate [RAN2, RAN1, RAN3]:
  N3 delay measurement
  separate L2 queue handing per different PSIs
  Single DCI scheduling the following in a given transmission opportunity on a single carrier
  Initial transmission(s) and re-transmission(s) with different HARQ process numbers
  Multiple PDSCHs/PUSCHs in frequency domain with independent indication of MCS
TU Estimation
RAN2 | 1 TU
RAN1 | 0.5 TU
RAN3 | 0.5 TU

## Slide 11
Copyright©2018 Huawei Technologies Co., Ltd. All Rights Reserved. The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
Bring digital to every person, home, and organization for a fully connected, intelligent world.

## Slide 12
Appendix – Simulation Assumption for XR-like traffics
Carrier Frequency | 3.5GHz
Bandwidth | 200MHz
Antennas | BS：64T64R (192AE)
 | UE：2T4R (4AE)
Transmit Power | BS: 56dBm
 | UE: 23dBm
ISD | 200m; 500m(for vehicular scenario)
TDD configuration | 4:01
Noise Figure | BS: 5dB
 | UE: 9dB
Topology | Randomly distributed UEs per cell; 3 cells in total
SRS | 20ms
Channel estimation | RCE
Channel Model | 38.901 UMa
 | O2I (20% outdoor)
 | O2O (100% outdoor, for vehicular scenario)
Speed | 3km/h;
 | 60km/h (for vehicular scenario)
RAN jitter | [-4, 4] ms
Carrier Frequency | 2.1GHz (SUL)
Bandwidth | 50MHz
Antennas | BS: 32T32R (128AE)
 | UE: 2T4R (4AE)
Transmit Power | UE: 23dBm
ISD | 200m; 500m (for vehicular scenario)
Noise Figure | UE: 9dB
Topology | Randomly distributed UEs per cell; 3 cells in total
SRS | 20ms
Channel estimation | RCE
Channel Model | 38.901 UMa
 | O2I (20% outdoor)
 | O2O (100% outdoor, for vehicular scenario)
Speed | 3km/h;
 | 60km/h (for vehicular scenario)
RAN jitter | [-4, 4] ms