## Slide 1: 3GPP TSG RAN Meeting #107 RP-250468 Incheon, Korea, March 12-14, 2025 Agenda Item: 9.4.1.6 Source: Intelsat, Gilat, JSAT Sky Perfect, MITRE, Tejas Networks, Lockheed Martin, Kratos, CHTTL Title: Motivation of Including 15 kHz Sub-Carrier Spacing for FR1 in the Ku Band Document for: Discussion and Decision

## Slide 2: Introduction
The purpose of this contribution is to highlight the benefits of 15 kHz Sub-Carrier Spacing (SCS) for narrow band services in the Ku Band.
Currently several Satellite operators are providing services to various customers using narrowband beams.
The network involves terminals with a substantial number of devices in a wider coverage area. Majority of these mass devices are low-cost entry level devices designed with simple technology for the consumer market. Specifically, these low-cost devices are power limited and low form-factor antenna aperture resulting in narrowband carrier services.

## Slide 3: Narrow Band Services
As part of our service offering to customers, Narrow Band Services' make up the bulk of the low-throughput services These services and application involve providing capacity for Narrow Band applications such as:
  Telemetry
  VoIP
  IoT
  Firmware updates
The above services are currently deployed over proprietary technology. Currently these narrow band services are offered over 5-10 MHz bandwidths
With the future deployment of 5G-NTN Technologies, it is vital to continue to provide like services to our customers.

## Slide 4: Narrow Band Broadcast Services- Use Cases
The following figure illustrates the application of narrow-band broadcast from a GEO Satellites using a narrow 0.5 Degree beam
Figure 1 illustrates a typical deployment scenario where IoT, Telemeter and VSAT devices are served by a 5-10 MHz narrow broadcast beam from a GEO Satellite. This example is using a proprietary technology.
In a typical deployment the beam covers approximately 500km radius and serves approximately 1500 devices in the coverage area.
Some of these devices are fixed on the ground and some devices are mobile.

## Slide 5: Advantages of 15 kHz SCS for FR1
In previous contributions [1-3] we have demonstrated that for a narrow 10 MHz band, 15 kHz SCS allows for greater utilisation of the radio channel and consequently greater data rates, see following Table 1:
The increased data rates in the UL and DL directions has significant effect on narrow band services.
The increased data rates are independent whether the terminal is a low-cost device or high-end terminal.
Table 1: FR1 10MHz Channel: Resource Block, Signal Bandwidth, and Data Rate |  |  |  | 
10 MHz Channel Bandwidth |  |  |  | 
SCS (kHz) | Resource Block | Signal Bandwidth (MHz) | Downlink Data Rate (Mbps) | Uplink Data Rate (Mbps)
15 | 52 | 9.375 | 15.5 | 16.2
30 | 24 | 8.670 | 14.3 | 15.0

## Slide 6: Advantages of 15 kHz SCS for FR1
And for narrow band services such as VoIP, we can increase the number of service users with 15 kHz SCS see following Table 2:
* CODEC data from satellite network includes network and IP overheads etc.
15 kHz SCS allows for *more efficient utilisation of the 10 MHz bandwidth
With 15 kHz SCS, we are able to provide greater number of VoIP Services than 30 kHz SCS
Table 2 Number of Additional VoIP Calls Supported by 15kHz |  |  |  |  | 
VoIP CODEC Type | Throughput per CODEC (kbps)* | SCS (kHz) | Number of Downlink VoIP calls | Number of Uplink VoIP calls | Number of additional VoIP calls supported by 15 kHz total
G.729 | 24 | 15 | 645 | 675 | 100
 | 24 | 30 | 595 | 625 | 
Opus | 48 | 15 | 322 | 337 | 50
 | 48 | 30 | 297 | 312 | 

## Slide 7: Business Critical
Satellite operators, like mobile terrestrial operators, need to have options in their operational portfolio to be able to cope with various radio environments and to be able to offer a variety of services.
Currently for FR1 Numerology, we only have 30 kHz SCS option: although this allows us to provide basic services, nevertheless without the 15 kHz SCS option, there will be service gaps, leading to inefficient use of the network and radio resources.
Moreover, the 15 kHz SCS is already part of the terrestrial network 3GPP 5G protocol standard and including it to the 5G NTN standard should ease and accelerate implementation which is critical for commercialization and interoperability.

## Slide 8: Conclusion and Proposal
In the past contributions [1-3] we have demonstrated the overall benefits of the 15 kHz SCS for FR1 Numerology.
In addition to the technical benefits, the 15 SCS is business critical for GEO Satellite operators who wish to deploy narrow band services.
To enable service continuity, from proprietary technologies to 5G-NTN technologies, satellites operators would require additional options in their toolbox to cope with varying radio conditions and terminal capability.
We propose to include the 15 kHz SCS option in the FR1 Numerology of the Ku Band.

## Slide 9: References
[1] R4-2500210, Ku Band: Narrow Band Services with 15 kHz Sub-Carrier Spacing
[2] RP-2418029, Ku Band Link Budget Analysis, Intelsat, RAN#113, Orlando, US, 18th-22nd November 2024.
[3] RP-2418030, Ku Band: Analysis of the Timing Alignment and Cyclic Prefix, Intelsat, RAN#113, Orlando, US, 18th-22nd November 2024.