## Slide 1: NR SBFD Phase II in Rel-20
KT Corp., China Unicom, Turkcell, Vodafone, Huawei, Hisilicon, NEC, Wilus, CEWiT, Korea Testing Laboratory, Google, ETRI, TCL, IIT Kanpur, Fraunhofer HHI, Fraunhofer IIS, Kookmin University, Tejas Networks, Yonsei University, Sharp
3GPP TSG RAN Meeting #107
Incheon, Korea, March 12-14, 2025
RP-250486
Agenda Item: 15.2.10

## Slide 2: Background and Motivation
Rel-18 SBFD (Study Item)
  Four different SBFD Deployment Cases were defined and studied as in TR 38.858
  Dynamic SBFD was studied and documented in TR 38.858
Rel-19 SBFD (Work Item)
  Deployment case 1 were prioritized
  Deployment case 2 and Deployment case 3 were not prioritized
  Dynamic SBFD was not included
  Intra-subband CLI handling was not optimized
D
D
D
U
U
U
U
D
D
D
D
D
U
D
D
D
U
U
U
U
D
D
D
D
D
U
Deployment case 1: Single operator with same SBFD subband configuration
D
D
D
U
U
U
U
D
U
D
D
D
U
U
U
U
D
D
D
D
D
U
Deployment case 2: Single operator with different SBFD subband configurations
D
D
D
U
D
D
D
D
U
U
U
U
D
D
D
D
D
U
Deployment case 4: Adjacent channel co-existence between TDD and SBFD
Operator A
Operator B
Deployment case 3: Single operator co-channel co-existence between TDD and SBFD
TDD Cell
D
D
D
U
U
U
U
D
D
D
D
D
U
D
D
D
U
D
SBFD Cell(s)
Motivation for Rel-20 SBFD Phase II
  Facilitate practical SBFD deployments (deployment case 3) and accommodate varying DL/UL traffic demands (dynamic SBFD and deployment case 2) via support of dynamic SBFD and intra-subband CLI enhancement

## Slide 3: Proposal
Proposal 1: to support a new Rel-20 work item for NR SBFD Phase II
Proposal 2: NR SBFD Phase II includes:
  Specify signaling support of dynamic transition between SBFD symbols and non-SBFD symbols [RAN1, RAN2]
    Note: the detailed schemes are to be down-selected from those in TR38.858
  Specify subband-level downlink power back off including corresponding enhancements in CSI measurement and report [RAN1, RAN4]
    Support frequency-dependent PDSCH EPRE to CSI-RS EPRE ratio for CSI derivation
    Extend gNB RE power control dynamic range as needed