## Slide 1: PUSCH coverage enhancement for 5G-Advanced in Rel-20
Huawei, HiSilicon, China Telecom, SK Telecom, TIM, Deutsche Telekom, NTT DOCOMO, Vodafone, KDDI, CEWiT, FutureWei, TCL, CAICT, Google
3GPP TSG RAN#107 RP-250492
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.7.1

## Slide 2
Coverage is one of the key factors that an operator considers when commercializing cellular communication networks due to its direct impact on service quality as well as CAPEX and OPEX [1].
Based on RP-243292 Chair’s summary endorsed in RAN#106 meeting, coverage enhancement is listed as an additional RAN1-led candidate topic for Rel-20 5G-A with details copied as below:
[1] RP-221858 Revised WID on Further NR coverage enhancements
[2] RP-242881 Rel-20 Coverage enhancement scope
UL performance is usually the bottleneck in most of scenarios in real deployment, while there are emerging commercial use cases that have UL heavy traffic, e.g., video uploading and mobile AI [2], which require higher UL data rate, e.g. higher than 5 Mbps. In the current commercial network, there are still a large amount of UEs which cannot reach UL data rate of 5 Mbps.
Therefore, the contribution proposes to support PUSCH coverage enhancement for 5G-A in Rel-20, targeting for higher UL data rate.
pi/2-BPSK is beneficial for PUSCH coverage performance, since it can enable higher transmission power due to low PAPR characteristics. However, pi/2-BPSK is only supported for MCS 0 and MCS 1 in the current specification. PUSCH with high UL data rate usually requires higher MCS, instead of MCS 0 or MCS 1.
Background

## Slide 3
  Proposal 1: Support a 5G-A Rel-20 item on coverage enhancements.
  Proposal 2: Take the following as one of the objectives for 5G-A Rel-20 coverage enhancements:
    Specify enhancements to improve PUSCH coverage for high uplink data rate, including extending pi/2-BPSK to more MCS entries in MCS tables
Proposal