## Slide 1: Network energy saving enhancements for 5G-Advanced in Rel-20
Huawei, HiSilicon, KT Corp., CEWiT, TIM, Orange, FutureWei, TCL, CAICT, Google, Fraunhofer IIS, Fraunhofer HHI
3GPP TSG RAN#107 RP-250494
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.7.2

## Slide 2
Background
Energy consumption is a key part of the operators’ OPEX, and thus it is worthwhile to apply network energy saving techniques to as many scenarios and cases as possible.
The techniques developed in Rel-18/19 can only apply to part of the cases and/or deployment scenarios. Therefore, there is still strong need to continue the enhancements on network energy saving for 5G-Advanced in Rel-20.
Based on RP-243292 Chair’s summary endorsed in RAN#106 meeting, network energy saving is listed as an additional RAN1-led candidate topic for Rel-20 5G-A.
The contribution provides a way forward on network energy saving enhancements for 5G-Advanced in Rel-20.

## Slide 3
  Proposal 1: Support a 5G-A Rel-20 item on enhancements of network energy saving.
  Proposal 2: Take the following as the candidate enhancements for further discussion:
    On-demand SSB for UEs in idle/inactive mode
    SSB periodicity extension
    On-demand SIB1 for case 1 and/or case 3
    Cell DTX/DRX enhancements for RRC CONNECTED UEs, including UE recommended Cell DTX/DRX
    Cell DTX/DRX enhancements for RRC IDLE/INACTIVE UEs
    On-demand CSI-RS/TRS
Proposals