## Slide 1
Huawei, HiSilicon
Rel-20 Efficient utilization of operating band larger than 100MHz
3GPP TSG RAN#107 RP-250498
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.10

## Slide 2
Motivation for efficient utilization of operating band larger than 100MHz
Many operators obtain operating band(s) larger than 100 MHz
n41[1] (2496 MHz – 2690 MHz) | China | China Mobile – 160M
n78[1] (3300 MHz – 3800 MHz) | China | China Telecom + China Unicom – 200M
 | UAE | DU – 200M ; Etisalat – 200M
 | Denmark | TT Network – 140M ; TDC Netco – 130M ; Hi3G – 120M
 | Estonia | Elisa – 130M ; Tele2 – 130M ; Telia – 130M
 | Finland | Elisa – 130M ; DNA – 130M ; Telia – 130M
 | Greece | Cosmote – 150M
 | Hungary | Yettel – 140M ; Telekom – 120M ; Vodafone – 110M
 | Norway | Telenor – 120M
 | Romania | Orange – 160M
 | Spain | Orange – 110M
 | Sweden | Telia – 120M
 | Switzerland | Swisscom – 120M
n79[1] (4400 MHz – 5000 MHz) | China | China Mobile + CBN – 160M
[1] www.spectrum-tracker.com
[2] World Radiocommunication Conference 2023 (WRC-23) Provisional Final Acts
[3] https://www.gov.cn/lianbo/bumen/202306/content_6888759.htm
6425-7125MHz are identified for IMT for certain countries in WRC-23[2]
6425
7125
700MHz
The frequency band of 6425-7125MHz is identified for IMT services in China[3]

## Slide 3
Potential enhancements for efficient utilization of operating band >100MHz
Carrier aggregation (CA) is a usual way to utilize the contiguous wide spectrum resources, and the bandwidth of each carrier does not exceed 100 MHz in FR1.
2*100M CA
CC1
CC2
Key Challenge
①CA features from Rel-15 to Rel-19 are all optional. UE penetration rate affects network performance.
① Single DCI
② Intra-band SSB-less
③ Fast SCell activation
CC1
CC2
SSB/SIB1
CC1
CC2
DCI
PDSCH
PDSCH
CC1
CC2
~20ms
Overhead reducation
Overhead reducation and energy saving
User experience improvement and energy saving
MAC CE & HARQ
CSI
~5ms
~15ms
Activation
Activation
Data
transmission
Activation
Deactivation
CC1
CC2
~20ms activation delay [38.133]
Low traffic
High traffic
[Note: Assume that the UE supports intra-band SSB-less]
②Long SCell activation delay to aggregate multiple carriers, leading to bad user experience.
Motivation for efficient utilization of operating band larger than 100MHz
Challenges of carrier aggregation
CC1
200 MHz Single Carrier
Single carrier with channel bandwidth up to 200 MHz

## Slide 4
Single carrier with channel bandwidth up to 200 MHz
Preliminary simulation results
Enable BWP switching in one single carrier for efficient resource utilization to achieve good user experience.
One SSB/SIB1 and one PDCCH are naturally enabled, which brings lower system overhead to achieve good network capacity.
CC1 200MHz
SSB/SIB1
DCI
PDSCH
BWP 1
(100MHz)
BWP 2
(200MHz)
CC1 200 MHz
1~2ms
DCI
Low traffic
High traffic
CC1
200 MHz Single Carrier
Advantages
Single carrier with channel bandwidth up to 200 MHz shall support 30 kHz SCS, since 30 kHz is the typical SCS for FR1 TDD bands.
Limited standard efforts (Detailed analysis as shown in the Appendix)
Extend the configurations and parameters for channels and signals to support channel bandwidth up to 200MHz (RAN1, RAN2, RAN3, RAN4)
Specify the corresponding RF requirements (RAN4)
Single carrier with channel bandwidth up to 200 MHz
Chart: Average UPT
| Case 1 | Case 2 | Case 3
R19 CA | 1 | 1 | 1
Rel-20 | 1.25 | 1.24 | 1.15
Parameters | Values
Frequency & Bandwidth & Resource Utilization | Case 1: 6.7GHz; 100MHz(PCC)+100MHz(SCC); RU=10% Case 2: 3.5GHz; 50MHz(PCC)+ 100MHz(SCC); RU=10% Case 3: 3.5GHz; 50MHz(PCC)+ 100MHz(SCC); RU=50%
gNB/UE antenna | Case 1: 256T4R; Case 2/3: 64T4R
Traffic model | FTP3
Packet size and arrival rate | 5MB @
R19 CA | CA with 20ms SCell activation delay
Rel-20 | Single carrier with bandwidth > 100 MHz with 1ms BWP switching delay
Parameters | Values
Frequency & Bandwidth & Resource Utilization | Case 1: 6.7GHz; 100MHz(PCC)+100MHz(SCC); RU=10% Case 2: 3.5GHz; 50MHz(PCC)+ 100MHz(SCC); RU=10% Case 3: 3.5GHz; 50MHz(PCC)+ 100MHz(SCC); RU=50%
gNB/UE antenna | Case 1: 256T4R; Case 2/3: 64T4R
Traffic model | FTP3
Packet size and arrival rate | 
R19 CA | CA with 20ms SCell activation delay
Rel-20 | Single carrier with bandwidth > 100 MHz with 1ms BWP switching delay
15%~25% average UPT gain compared with legacy CA
25%
15%
24%

## Slide 5
Summary
  Observations from the above analysis and evaluations:
    Single carrier with channel bandwidth up to 200 MHz can enable efficient utilization of operating band larger than 100 MHz
    Single carrier with channel bandwidth up to 200 MHz can also enable simpler carrier management
  Proposal: Specify a single carrier with channel bandwidth up to 200 MHz for FR1 in Rel-20, at least for 30 kHz SCS
    Specify the corresponding RF requirements for BS and UE (RAN4)
    Extend the configurations and parameters for channels and signals to support channel bandwidth up to 200 MHz (RAN1, RAN2, RAN3, RAN4)

## Slide 6
Appendix
Potential specification impact for single carrier with channel bandwidth larger than 100MHz
  For single carrier with 30 kHz SCS and channel bandwidth up to 200 MHz for FR1, the potential specification impacts are as below:
    Extension of the existing configurations and parameters [RAN1, RAN2, RAN3, RAN4]
    To extend the existing configurations and parameters as shown in the table in the next slide
    Other corresponding modification for frequency resource configuration if needed
    Specify the corresponding RF requirements [RAN4]
  Note:
    The table in the next slide shows that all are just simple/straightforward extensions
    For the RF requirements, some discussions may be needed but at least gNB RF requirements would be simple extensions also

## Slide 7
 | Configurations or Parameters | Definition in the current specs | Extended values or definitions
Maximum FFT size [RAN1] | Nf | 4096 | 8192
Range of DC subcarrier indices [RAN1/2] | txDirectCurrentLocation in the SCS-SpecificCarrier | txDirectCurrentLocation INTEGER (0..4095) | txDirectCurrentLocation INTEGER (0..7395)
 | txDirectCurrentLocation in the UplinkTxDirectCurrentBWP | txDirectCurrentLocation INTEGER (0.. 3301) | txDirectCurrentLocation INTEGER (0..6601)
Maximum number of PRBs [RAN2, RAN3] | maxNrofPhysicalResourceBlocks | maxNrofPhysicalResourceBlocks INTEGER ::= 275 | maxNrofPhysicalResourceBlocks INTEGER ::= 550
 | maxnoofPhysicalResourceBlocks | 275 | 550
Maximum indication value of BWP BW [RAN2] | locationAndBandwidth in the BWP | locationAndBandwidth INTEGER (0..37949) | locationAndBandwidth INTEGER (0.. 151524)
Maximum CORESET resource indication (in bits) [RAN2] | frequencyDomainResources in the ControlResourceSet | frequencyDomainResources BIT STRING (SIZE (45)) | frequencyDomainResources BIT STRING (SIZE (90))
Number of PRBs configured for rate matching pattern (in bits) [RAN2] | resourceBlocks in the RateMatchPattern | resourceBlocks BIT STRING (SIZE (275)) | resourceBlocks BIT STRING (SIZE (550))
Frequency density threshold for CP-OFDM [RAN1/2] | frequencyDensity in PTRS-UplinkConfig and PTRS-DownlinkConfig | SEQUENCE (SIZE (2)) OF INTEGER (1..276) | SEQUENCE (SIZE (2)) OF INTEGER (1..551)
Frequency density threshold for DFT-s-OFDM [RAN1/2] | sampleDensity in PTRS-UplinkConfig | SEQUENCE (SIZE (5)) OF INTEGER (1..276) | SEQUENCE (SIZE (5)) OF INTEGER (1..551)
Definition of nominal RBG size [RAN1/2] | Table 5/6.1.2.2.1-1 in TS 38.214 | Table 5/6.1.2.2.1-1 in TS 38.214 | Add new RBG size 32 for PRB number 276~550
Maximum number of PRBs configured for SRS [RAN1/2] | Table 6.4.1.4.3-1 in TS 38.211 | 272 | 548
Subband size for CSI reporting [RAN1/2] | Table 5.2.1.4-2 in TS 38.214 | Table 5.2.1.4-2 in TS 38.214 | Add new subband size 32&64 for PRB number 276~550
Maximum transmission bandwidth configuration [RAN4] | TS 38104/38101-1 Table 5.3.2-1 | TS 38104/38101-1 Table 5.3.2-1 | Add one column for 200 MHz with value 540 for 30 kHz SCS
Minimum guardband for each UE channel bandwidth and SCS [RAN4] | TS 38104/38101-1 Table 5.3.3-1 | TS 38104/38101-1 Table 5.3.3-1 | Add one column for 200 MHz with value 2785 for 30 kHz SCS