## Slide 1: Views on Ambient IoT work in 5G-A Rel-20
Agenda item: 15.2.3
Source: CATT
3GPP TSG RAN Meeting #107 RP-250507
Incheon, South Korea, 12th -14th March, 2025

## Slide 2: Ambient IoT Normative works after RAN study
RAN working group complete the study of solution for Ambient IoT in Rel-19
The outcome of A-IoT study
  Target to have the common air interface design for different deployment scenarios and topologies for all types of devices.
  Evaluation methodology and evaluation results of coverage and latency for inventory use case
  The frame structure and timing for A-IoT operation
  The A-IoT device architecture – devices 1/2a/2b
  The device availability/unavailability associated with energy harvesting,
  The physical layer design -
    Modulation and waveform – including CP handling for OFDM waveform
    Channel coding – Line code, FEC, CRC, bit/chip/block-level repetition
  Physical channels/signals –
    DL PRDCH
    UL PDRCH
    Preamble
  Carrier wave –
    Single tone and dual single tone
    Operation spectrums and transmission node
    Interference cancellation
  Multiple Access – TDMA/FDMA/CDMA
  Random Access procedures
    Paging
    3-step/2-step/unified
  Topology 2 resource allocation for UE reader

## Slide 3: Normative work in Rel-20
The NR system design framework in support of A-IoT operation would have a common air interface for devices 1/2a/2b and high power device 3 in all deployment scenarios and topologies for all use cases
  Rel-19 A-IoT work needs to finalize several aspects with different alternatives which has impact to the A-IoT system design framework
    The frame structure and the end of PRDCH/PDRCH
    The CP handling of PRDCH and the associated chip duration for PRDCH
    The timing determination between DL R2D transmission and UL D2R transmission
    The random access procedures
  The selection of options would be critical for the A-IoT operation in different scenarios, topologies, and use cases in the first release and subsequent release
The A-IoT normative work in Rel-19
  The target deployment scenarios would be indoor
  The UE reader is not included in Rel-19 and is the critical element in extending the network coverage of A-IoT devices and
  The Rel-19 A-IoT frame work needs to specify the common interface and functions with forward compatibility to support the outdoor deployment scenarios and use cases with additional Topologies in addition to Topologies 1 and 2 as well as Topologies 3 and 4.
Rel-20 A-IoT normative works is based on the assumption of Rel-19 A-IoT to support A-IoT system design framework for both Indoor and outdoor use cases

## Slide 4: Outdoor Coverage with A-IoT device Mobility
Motivation:
  Tracking outdoor/indoor A-IoT device with device mobility
  The target coverage distance of 50-1000 m for A-IoT device with mobility
  Outdoor use cases:
    Outdoor inventory: airport port terminal/shipping port
    Outdoor positioning: personal belonging finding, cargo tracking, luggage tracking
      Autonomous A-IoT device triggering focuses on device 2A/2B
Objective:
  Specify mechanism in extension of the A-IoT coverage to maximum distance of 50-1000m with device mobility for outdoor scenarios
  Specify autonomous A-IoT device triggering for device initiated use case for outdoor inventory and positioning
  Specify the control mechanism for Topologies 3 and 4 in addition to Topologies 1 and 2.
Outdoor sensor: ultra-high voltage substation
Outdoor inventory airport terminal/shipping port and cargo tracking
Outdoor Positioning: personal belonging finding

## Slide 5: A-IoT Positioning for Positioning Use Cases
Motivation:
  A-IoT positioning use cases of locating and tracking A-IoT devices could not get the required positioning accuracy from Proximity determination in Rel-19 A-IoT study
  Support the positioning method for tracking A-IoT device with device mobility.
  Low hearability in signals backscattered/transmitted from the A-IoT device
Objective:
  Specify the positioning method for the reader to enable the A-IoT device positioning estimation for positioning use cases
Smart Parking
Tracking and locating A-IoT devices indoors and outdoors
Inventory management and positioning base payment

## Slide 6: Autonomous/network trigger Report Sensing
Motivation:
  Sensor service: periodic/aperiodic A-IoT device triggering device triggering reporting or network-initiated reporting for sensing and tracking
  Support of use case for A-IoT device triggering reporting/alarming e.g., cargo monitoring, fire monitoring, room monitoring with alarming
Objective:
  Specify DO-DTT and Do-A traffic for triggering periodic/aperiodic reporting in indoor/outdoor scenarios
Fire monitor sensor
Room Environmental Supervision
Smart grid

## Slide 7: TU for Rel-20 A-IoT WID
Proposed TU for Rel-20 A-IoT：
WG | Q3’2025 | Q4’2025 |  | Q1’2026 | Q2’2026 |  | Q3’2026 | Q4’2026 |  | Q1’2027
 | 2025.8 | 2024.10 | 2024.11 | 2026.2 | 2026.4 | 2026.5 | 2026.8 | 2025.10 | 2025.11 | 2027.2
RAN1 | 2 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 
RAN2 |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
RAN3 |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
RAN4RF |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
RAN4RD |  |  |  | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5