## Slide 1: Views on 5G-A Rel-20 ISAC
CATT
3GPP TSG RAN Meeting #107
Incheon, Korean, March 12-14, 2025
Agenda item: 15.2.9.1
RP-250516

## Slide 2: Background
In Rel-19, channel modeling for Integrated Sensing And Communication (ISAC) is studied (RP-242348). The study aims to support object detection & tracking for the following sensing targets:
  UAVs
  Humans indoors and outdoors
  Automotive vehicles (at least outdoors)
  Automated guided vehicles (e.g. in indoor factories)
  Objects creating hazards on roads/railways, with a minimum size dependent on frequency
In RAN#105 checkpoint , there was no consensus to extend the scope in Rel-19
  Progress at RAN#105 was premature to pursue performance evaluation
It is expected that the study on ISAC channel modeling will be finished in time in Rel-19
  Progress after RAN#105 is smooth and good
In SA2#167,Rel-20 5G-A Integrated Sensing and Communication SID was approved

## Slide 3: Motivation
It is desired to support sensing feature in 5G-A Rel-20
  To seize the urgent commercial need (e.g. low altitude economy) in 1~4 years from vertical industry, which can’t wait for the first version of 6G
  To extend 5G-A capability and life cycle, and accumulate experience for 6G standardization
Proposal 1: Support gNB-based sensing feature in 5G-A Rel-20.
UAV detection & tracking
Sensing pedestrian/vehicle/obstacle
migrates
+
sensing

## Slide 4: Objectives
High level consideration for gNB-based sensing
  gNB mono-static can be supported
  How to perform sensing by a gNB can be up to vendor’s implementation
  gNB-based sensing should be transparent to UE
Higher layer aspects for gNB-based sensing
  Architecture, Signalling and Procedure for sensing data transmission between RAN and sensing function
  Sensing capability report related procedure
  Note: Coordination with SA2/RAN1 maybe needed.
Proposal 2: The following higher layer aspects are specified for gNB-based sensing(RAN3)
  Architecture, Signalling and procedure for sensing data transmission between RAN and sensing function;
  Sensing capability report related procedure

## Slide 5: Potential RAN1 work
As only gNB-based mono-static sensing is considered in Rel-20 5G-A, physical layer design should be up to vendor’s implementation.
For now, we do not consider RAN1 work as a prerequisite for the success of this RAN3-led 5G-A Rel-20 ISAC. However, RAN1 work may be triggered based on the request from RAN3, potentially include:
  Performance evaluation
  Definition of sensing measurement
  Note 1: As a starting point, 0 TU is assumed for RAN1.
  Note 2: Whether to trigger RAN1 work can be discussed during RAN3 study/normative phase.
Proposal 3: For 5G-A Rel-20 ISAC, RAN1 work may be triggered based on the request from RAN3, if any.

## Slide 6: Conclusion
Proposal 1: Support gNB-based sensing feature in 5G-A Rel-20.
Proposal 2: The following higher layer aspects are specified for gNB-based sensing：
  Architecture, Signalling and procedure for sensing data transmission between RAN and sensing function（RAN3）
  Sensing capability report related procedure（RAN3）
  Note：1 TU each meeting in RAN3 is expected
Proposal 3: For 5G-A Rel-20 ISAC, RAN1 work may be triggered based on the request from RAN3, if any.

## Slide 7
Notes: 万物互联，无限沟通
Universal Connectivity, Infinite Communication.