## Slide 1
Huawei, HiSilicon
Rel-20 Ambient IoT scope
3GPP TSG RAN#107 RP-250522
Incheon, South Korea, March 12-14, 2025
Agenda Item: 15.2.3

## Slide 2
Background
In RAN#106, the workplans for Rel-19 and Rel-20 are endorsed in RP-243280.
Workplan for Rel-19:
  No impact to Rel-19 ASN.1 freeze, no impact to the timeline of Rel-20. Rel-20 Ambient IoT starts after the completion of the Rel-19 Ambient IoT WI.
  Completion of the Rel-19 work (Core Part) is targeted at the stage-3 functional freeze for Rel-19 in Sept. 2025, with 3 quarters for RAN2/3/4 and 2 quarters for RAN1.
Workplan for Rel-20:
  Includes D2T2
  Includes Device 2
  A limited number of additional use cases, deployments, connectivity topologies, devices, traffic types in TR38.848 as a starting point
  Note: work on D2T2, device 2 shall follow the Rel-19 study conclusions, and further down-selection of architecture options for topology 2 may be needed. For indoor use cases, deviations from Rel-19 study conclusion shall be well justified and agreed.
  Details to be discussed at a later RAN plenary meeting, including the need for study phase.
For both Rel-19 and Rel-20, co-ordination with SA2/3 is expected

## Slide 3
Outdoor use cases supported, indoor use cases enhanced
Higher-power ‘Device C’ (1 – 10 milliwatt) for outdoor environment
Topology requirements for reaching Rel-20 devices
Design targets: Rel-20 A-IoT BSs co-deployed with NR, and A-IoT still a segment well below LPWA
RAN WGs workload management
Outline

## Slide 4
Outdoor use cases are essential in Rel-20
In Rel-20, Ambient IoT should additionally support outdoor use cases to meet urgent market demand.
Outdoor inventory and command are clear use cases, and sensor use cases also have ready market demand.
Indoor enhancements to Rel-19 inventory & command
There is interest in positioning, hence applicable scenarios, requirements, type of solution, etc. need further discussions
Proposal 1: Rel-20 Ambient IoT supports outdoor inventory, outdoor sensor, and outdoor command use cases. Applicable scenarios, extent, and requirements of positioning use case support in Rel-20 should be further discussed until June.
Representative use case (rUC) | Analysis
rUC5: Outdoor inventory | Example use case recyclable logistics crate management has inventory requirement Inventory functionality has been studied in Rel-19, it can be easily extended from indoor to outdoor
rUC6: Outdoor sensor | Example use case smart grid and infrastructure health monitoring has DO-A traffic type sensor report requirement In Rel-19, the air interface for DO-DTT and DT traffic types is not sufficient for the DO-A traffic type The functionality for sensor with DO-A traffic types should be specified in Rel-20
rUC7: Outdoor positioning | rUC7 includes use cases with cell level positioning, and higher positioning accuracy requirements Cell level positioning, e.g. recyclable logistics crate management, can be achieved via an inventory procedure For higher accuracy requirements, the scenarios, solutions, and market demand should be further discussed towards Rel-20.
rUC8: Outdoor command | Example use cases may also need device management, command procedure could also be supported Command functionality has been studied in Rel-19 bundled with inventory procedure, it can be easily extended from indoor to outdoor

## Slide 5
Device C is needed to support outdoor use cases
  Device 2 studied in Rel-19 targets indoor use case and cannot support outdoor use case.
  Based on indoor pathloss model InF-DH NLOS, the maximum distance of device 2 is 62.86m
  If outdoor pathloss model UMA NLOS is assumed, the maximum distance of device 2 is only 33.23m
  The maximum distance of NR macro site is 500m or 1732m based on TR 38.830.
    Proposal 2: For outdoor use cases, ‘Device C’ defined in TR 38.848 should be supported.
  Active transmitter
  1 mW to 10 mW power consumption
 | MPL(dB) | InF-DH NLOS Max distance(m) | UMA NLOS Max distance(m)
Device 2 | 72.1 | 62.86 | 33.23

## Slide 6
Rel-20 Device C needs to be reachable after moving indoors
  Rel-20 Device C should provide an overall solution for a customer whose devices transition from outdoor use to indoor use, and vice-versa. E.g., re-use of a recycling crate inside a site, after transportation
    Indoor BS deployed for Rel-19 may not be upgraded quickly to Rel-20, or may not be deployed by this customer
    Topology 1 is the baseline of cellular network, for high service availability and reliability in large/wide areas.
    Deploying new intermediate UEs in T2 to support this indoor-outdoor transition is not a realistic cost burden for the end customer who is paying an operator, nor the network operator who has built and upgraded their outdoor network already
  Hence, Rel-20 Device C, when indoors, should connect directly to an outdoor macro-cell BS, i.e. Topology 1
  For outdoor base station readers, two deployment scenarios D4 and D2 are defined in TR 38.848.
    Deployment scenario 4: Device outdoors, base station outdoors
    Deployment scenario 2: Device indoors, base station outdoors
Proposal 3: With BS reader outdoors, D4T1 and D2T1 should also be supported in Rel-20 to ensure continuous coverage and benefit from an upgraded outdoor cellular network with continuous coverage

## Slide 7
Design targets
Outdoor use cases should be supported assuming existing outdoor NR BS sites, i.e. no new BS sites are needed
The principle that Ambient IoT will not aim to replace existing 3GPP LPWA technologies has worked well in Releases 18 & 19 to constrain the design parameters. It should be continued by the distinguishing facets:
  Device power consumption and complexity is still designed to be far lower than NB-IoT/LTE-MTC/RedCap
  User experienced data rate target: minimum not less than 0.1 kbps.
These characteristics allow development of physical devices which can be used in commercial and environmental cases where existing 3GPP technology cannot penetrate. E.g. high-voltage environments cannot allow battery-powered devices, and high-density monitoring of infrastructure is highly intolerant of cost
Proposal 4: Rel-20 Ambient IoT targets an IoT segment well below the existing 3GPP LPWA technologies, e.g. NB-IoT, eMTC, RedCap, etc.
Proposal 5: Rel-20 Ambient IoT design includes Device C for outdoor use and:
  A-IoT BSs are deployed co-located with existing outdoor NR BS sites
  User experienced data rate minimum not less than 0.1 kbps.

## Slide 8
Workplan management
  Apart from power consumption, Device 2b is fundamentally the same as Device C: active signal generation, and receiver filtering ability. Hence same air-interface changes would be expected in Rel-20 for these two devices.
  There is no need for a specialized air interface for every conceivable Device 1/2/C!
  Proposal 6: Device 2b and Device C have a unified air interface design in Rel-20.
  RAN needs to carefully consider the workload introduced by Topology 2, based on the Rel-19 SI, to ensure that commercial demand for other use cases, etc. (as per the agreed WF) are given sufficient time and scope
  Proposal 7: For D2T2 in Rel-20:
  One architecture solution should be down-selected in WID.
  RAN should scope for the minimum necessary workload to enable Topology 2 commercialization

## Slide 9
Summary of proposals
  Proposal 1: Rel-20 Ambient IoT supports outdoor inventory, outdoor sensor, and outdoor command use cases. Applicable scenarios, extent, and requirements of positioning use case support in Rel-20 should be further discussed until June.
  Proposal 2: For outdoor use cases, ‘Device C’ defined in TR 38.848 should be supported.
  Active transmitter
  1 mW to 10 mW power consumption
  Proposal 3: With BS reader outdoors, D4T1 and D2T1 should also be supported in Rel-20 to ensure continuous coverage and benefit from an upgraded outdoor cellular network with continuous coverage
Proposal 4: Rel-20 Ambient IoT targets an IoT segment well below the existing 3GPP LPWA technologies, e.g. NB-IoT, eMTC, RedCap, etc.
Proposal 5: Rel-20 Ambient IoT design includes Device C for outdoor use and:
  A-IoT BSs are deployed co-located with existing outdoor NR BS sites
  User experienced data rate minimum not less than 0.1 kbps.
  Proposal 6: Device 2b and Device C have a unified air interface design in Rel-20.
  Proposal 7: For D2T2 in Rel-20:
  One architecture solution should be down-selected in WID.
  RAN should scope for the minimum necessary workload to enable Topology 2 commercialization

## Slide 11
Example use case #1: Recyclable logistics crate management
China has announced policies and plan to support modern logistics with green, digitalization, networking, and intelligence since 2022 [1].
Recyclable logistics crate is the trend to replace disposable plastic foam boxes to avoid environment pollution. Add electronic labels on the crate for inventory, stock in/out, path tracing, temperature monitoring. And enable end-to-end visibility and management.
Packaging
Farm
Transport
Processing
Re-load
Shelves
Disposal
Recyclable crates
tag attached
Enabled by Ambient IoT
Recycling crates E2E management
UC1: Stock in/out
Inventory
UC2: Status tracking during Transport
UC3: Checkpoint
Stock in/out, automatic inventory accuracy 99.99%
Automatic reading of crates in check point, accuracy 99.99%
Continuous monitoring and update of crates’ temperature, location etc.
[1]: https://www.gov.cn/zhengce/content/2022-12/15/content_5732092.htm
Existing solutions issues cannot ensure continuous coverage and the cost is not acceptable.
Consumer requirements:
  Wide area continuous coverage
  Device ultra low power consumption and maintenance-free, device cost ~ 0.5$
  Cell level positioning
Market space forecast: ~3.7 billion recyclable logistics crates in fresh/automotive/electronics industries in 2027
Consumers expressed the desire to support recyclable logistics crate management since 2023

## Slide 12
Example use case #2: Infrastructure condition monitoring
Bridges are parts of outdoor public infrastructure and smart bridge condition monitoring is important for safety and maintenance.
In 2022, China published national specification GB/T 39339.2 that highlights bridges safety monitoring as part of transit facilities in cities.
Types of sensor used for monitoring status of bridge: displacement, strain, deflection, tilt, cable tension, temperature, acceleration, wind direction and speed, corrosion, crack etc.
Consumer requirements:
  Outdoor wide area coverage
  Device ultra low power consumption and maintenance-free, device cost ~ 0.5$
various sensors
Disadvantages of other solutions
Machine vision: conditions such as rain or night monitoring result low accuracy which is not enough to meet the demands
Wired sensor: reliable, but the layout cost is high and complex, and the cost of monitoring equipment is too high
Market space forecast: hundreds to thousands of sensors per bridge
In April 2024, the Ministry of Transport of China further promoted the structural monitoring of highway bridges [1]. Local Transportation Departments begin to carry out bridge monitoring pilot in 2024-2025.
[1] https://www.mot.gov.cn/2024zhengcejd/202410/t20241016_4157868.html

## Slide 13
Example use case #3: Smart grid
In electronic power industry, temperature monitoring is required to monitor the running status of equipment. In this high voltage environment, the battery has safety risks.
AC current transformer
AC switch
AC breaker
Solution 1:
Manual inspection + wired connection
High maintenance costs: About 1200 devices need to be monitored at a time, and the manual inspection is at high labor cost.
Complex networking: Wired devices are deployed at multiple sites, resulting in high deployment costs.
Low accuracy: The measurement accuracy is affected by factors such as magnetic field, load, and reflection.
Poor timeliness: The infrared thermogram used for temperature measurement cannot directly locate the point. Therefore, manual fault locating is required.
Solution 2:
infrared thermometric graph
Disadvantages of existing solutions
Consumer requirements: battery-less for environment safety in extreme condition
Market space forecast: ~ 0.6 billion sensors in power transmission connections, transformer cables and power distribution lines, etc.
There are research projects to study battery-less sensor solution: laboratory stage from 2024, field test in 2025-2026 and expected to be commercial in 2027.

## Slide 14
NB-IoT clearly a segment above Ambient IoT
Tx Power: 792 mW@23dBm
Tx Power: 252 mW@0dBm
Rx power: 216 mW
NB-IoT power consumption is hundreds mW
  NB-IoT reception power consumption is hundreds mW.
  NB-IoT transmission power consumption is hundreds mW with 0dBm transmission power.
To support long battery life, NB-IoT usually equipped with large dedicated battery
  The cost of NB-IoT dedicated battery is 6~8$
[2] https://www.alibaba.com/product-detail/1S2P-3-6V-38Ah-ER34615-Lithium_1600481471404.html?spm=a2700.galleryofferlist.normal_offer.d_title.354513a0XfFr4C
[3] https://www.alibaba.com/product-detail/EVE-Lithium-Batteries-ER34615-Li-SOCl2_62383204848.html?spm=a2700.details.you_may_like.4.c03636e2sxp9kZ
[2]
[3]
[1] https://docs.rs-online.com/dc48/0900766b816cd1ec.pdf
[1]
[1]
[1]