## Slide 1
Views on further mobility
enhancement in 5G-A Rel-20
3GPP TSG RAN Meeting #107
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.8.1
TDoc number: RP-250556
Source: ZTE Corporation, Sanechips

## Slide 2: Motivations
Progress of Rel-19 Mobility enhancements on LTM
  Inter-CU LTM is supported to increase the applicable scenarios (not limited to cells within the same gNB);
  Conditional LTM is supported to improve the mobility robustness;
Consideration on Conditional LTM
  Conditional handover can improve HO robustness, especially for FR2, or FR1 with rapid signal degradation case; L1/L2 based mobility(LTM) is beneficial for handover latency reduction, thus conditional LTM can reduce latency and improve robustness at the same time.
  Rel-19 conditional LTM is only supported for limited scenario, i.e. conditional intra-CU LTM in NR SA and possibly for NR-DC as well (with a check for this at RAN#107). But Inter-CU case is not supported and this is expected to limit the usage scenarios in real deployment.
Proposed enhancements for Rel-20 Conditional LTM:
  Support inter-CU conditional LTM, including:
    Inter-CU MCG CLTM with SCG release/reconfiguration;
    Inter-CU SCG CLTM without MN change;
    Note: ask SA3 to study the provision of security key.
  Note: additional objectives might be needed also for intra-CU conditional LTM, if some of the useful NR-DC cases will finally not be supported in Rel-19

## Slide 3: Motivations
Progress of Rel-19 Mobility enhancements on L1 measurements
  L1 based measurement event reporting is supported to reduce the signalling overhead, and to facilitate the execution of conditional LTM;
  CSI-RS based L1 measurement is supported, and CSI acquisition is supported for reducing handover interruption.
Consideration on L1 measurements
  Currently, a common CSI resource configuration is used for LTM L1 measurement. Based on Rel-18 design, the UE starts L1 measurements on all configured RS resources once configured by RRC. To enable subsequent LTM, the network can configure multiple candidate cells and each candidate cell has multiple beams that to be measured by the UE. However, only part of the beams need to be measured at any given time (or UE location). While measuring all RS resources at once increases the UE power assumption and also the reporting signaling overhead.
  In addition, based on Rel-18 design, many UE capabilities are defined to indicate the limitation regarding the supported measured beams, and for all the configured measurement resources. If dynamic activation/deactivation of L1 measurement and reporting can be supported, then the network would be able to configure more LTM candidate cells and further improve the benefit of subsequent LTM.
  Proposed enhancements for Rel-20 L1 measurements:
  Support dynamic activation/deactivation of L1 measurement resource and reporting
    Using MAC CE to dynamic activate/deactivate L1 measurement resources and reporting configuration;
    Support LTM-1 event reporting, used to deactivate L1 measurement resources.

## Slide 4: Summary
Proposals for Rel-20 mobility enhancements objectives:
  Specify support for inter-CU conditional LTM [RAN2, RAN3]:
    Prioritize the following cases:
      Inter-CU MCG CLTM with SCG release/reconfiguration;
      Inter-CU SCG CLTM without MN change;
    Note: ask SA3 to study the provision of security key.
  Note: additional objectives might be needed also for intra-CU conditional LTM, if some of the useful NR-DC cases will finally not be supported in Rel-19
  Support dynamic activation/deactivation of L1 measurement resource and reporting [RAN2]
    Using MAC CE to dynamic activate/deactivate L1 measurement resources and reporting configuration;
    Support LTM-1 event reporting, used to deactivate L1 measurement resources.

## Slide 5: Thank You！