## Slide 1: Views on Rel-20 Ambient IoT
RP-250651
3GPP TSG RAN #107
Incheon, Korea, March 12-14, 2025
Agenda Item: 15.2.3

## Slide 2
Background
Scope of A-IoT in Rel. 19 and Rel. 20 was discussed together in RAN#106 [1]
WI for A-IoT with minimum scope was agreed in Rel. 19 [2]
  To ensure timely completion of WI during Rel. 19 time frame
Based on discussions in RAN#106 [1], the scope of A-IoT in Rel. 20
  Includes D2T2
  Includes Device 2
  A limited number of additional use cases, deployments, connectivity topologies, devices, traffic types in TR38.848 as a starting point
  Note: work on D2T2, device 2 shall follow the Rel-19 study conclusions, and further down-selection of architecture options for topology 2 may be needed. For indoor use cases, deviations from Rel-19 study conclusion shall be well justified and agreed.
  Details to be discussed at a later RAN plenary meeting, including the need for study phase.

## Slide 3
Discussion on Rel-20 Ambient IoT
Topology D2T2 offers distinct coverage benefits depending on the use case
  D2T2 is more suitable when the reader is outdoor and enables reuse of the existing infrastructure
  Intermediate UE must be under the control of serving gNB for serving the Ambient IoT devices and for multiplexing NR and Ambient IoT operations
    L1 and higher-layer based control signaling (Option 2) provides higher flexibility and better resource utilization and is inline with the configurations in NR
Device 2a has additional capabilities and meet the minimum coverage requirements in case of D1T1 and D2T2
RRC based A-IoT architecture must be supported for D2T2
  gNB can do a better job in selection and controlling of UE reader compared to CORE network
  D1T1 scenario in Rel. 19 is based on control plane option

## Slide 4
Discussion on Rel-20 Ambient IoT
For device unavailability, Direction 2 offers low communication delay, efficient resource allocation and optimum use of device capabilities
For Carrier wave, external CW outside scenario (i.e., D1T1-B and D2T2-B) is simple, provide maximum coverage and avoids self interference issue
Control of CWN is essential
  Always ON CWN Generates significant interference and affects D2R reception [3]
  Demands higher interference suppression at reader, which increases reader complexity and cost
    E.g., During study phase, different companies have reported interference suppression value ~ 150dB
  Increase in reader complexity is not desirable, especially in D2T2 where UE act as reader

## Slide 5
Proposal:
Specify D1T1 and D2T2 for Device 2a
  For inventory and command use cases
  L1 and higher layer (i.e., Option 2) based control of intermediate UE
  At least RRC based A-IoT architecture for D2T2
  Device unavailability direction 2 and energy status report
  Control of carrier wave node
Discussion on Rel-20 Ambient IoT

## Slide 6
Discussion on Rel-20 Ambient IoT
Rel. 19 A-IoT studied only a limited set of use cases (focused on indoor inventory and command) and deployment scenarios (Indoor and outdoor to indoor) mentioned in TR 38.848.
Rel 20 should extend the study to other use cases and scenarios
  A-IoT for deployment scenario D4 (device outdoor, BS outdoor)
  A-IoT for sensor use cases
  Support Topology 1 and Topology 2 (with NCR as intermediate node)
  Enhancements to device architecture and procedure to improve coverage for outdoor use cases
  Enhancements to extend device operational time

## Slide 7
Proposal
Study the following aspects in Rel. 20 A-IoT
  D1T1 and D2T2 for sensor use cases
  A-IoT in deployment scenario D4 (device outdoor, BS outdoor) for sensor use case
    Support both Topology 1 and Topology 2 (with NCR as intermediate node)
    Enhancements to device architecture and procedure to improve coverage for outdoor use cases
    Enhancements to extend device operational time
Discussion on Rel-20 Ambient IoT

## Slide 8
Conclusion
Proposal 1
Specify D1T1 and D2T2 for Device 2a
  For inventory and command use cases
  L1 and higher layer (i.e., Option 2) based control of intermediate UE
  At least RRC based A-IoT architecture for D2T2
  Device unavailability direction 2 and energy status report
  Control of carrier wave node
Proposal 2
Study the following aspects in Rel. 20 A-IoT
  D1T1 and D2T2 for sensor use cases
  A-IoT in deployment scenario D4 (device outdoor, BS outdoor) for sensor use case
    Support both Topology 1 and Topology 2 (with NCR as intermediate node)
    Enhancements to device architecture and procedure to improve coverage for outdoor use cases
    Enhancements to extend device operational time

## Slide 9
References
[1]. RP-243280, “Way forward for Ambient IoT for REL-19 and REL-20”, RAN# 106, Madrid, Spain, December 9-12, 2024.
[2] RP-243326. “New Work Item: Solutions for Ambient IoT (Internet of Things) in NR”, RAN# 106, Madrid, Spain, December 9-12, 2024.
[3] Sec. 6.7.5, “Carrier wave interference cancellation study”, TR 38.769 TS study on solutions for A-IoT in NR, REL-19.

## Slide 10: Thank You