## Slide 1
RP- 250664
3GPP TSG RAN Meeting #107
Incheon, Korea, 12th to 14th March, 2025
Views on Scope for 5G-A R20 Ambient IoT
Agenda Item: 15.2.3
Source: Tejas Networks
Document for: Discussion

## Slide 2
Motivation
  Existing UHF RFID technology has various implementation issues in the mMTC scenario such as, limited reading range of a few meters, lack of interference management in case of dense deployment, etc.
  NB-IoT Technology provides massive connectivity but having high power consumption, high complexity, and high cost.
  Rel-19 Ambient IoT technology is low power consuming and cost effective indoor IoT technology, which supports massive connectivity with better interference management then RFID. However, Rel-19 work item for A-IoT specifies the protocols for Device 1 with topology 1 and the coverage is limited to 15 meters.
Observations from R19 Ambient IoT
  Rel-19 Ambient IoT (A-IoT) work item includes the following:
    Topology 1 for Device 1 only
    External carrier wave transmitter (CWT) for backscatter communication
  Physical layer uplink and downlink message signals are defined for handling multiple devices by one reader.
  Coverage is limited to 15 meters only for Device 1 with topology 1.
  Due to limited power budget of Device 1, the clock accuracy is low, which increases the R2D signaling overhead for clock calibration.
Topology 1: BS ↔ Ambient IoT device

## Slide 3
Proposal 1: CW inside topology is more practical than CW outside topology, as the on-demand availability of external CW transmitter is not always feasible (for device type 1/2a).
Proposal 2: Higher complexity and power budget of Device 2 provides higher coverage and clock accuracy compared to Deice 1. Thus, the specification requirement of Pre/mid/post-ambles for Device 2 should be defined for both Topologies 1 and 2.
Proposal 3: Charging cycle for energy harvesting of A-IoT devices should be defined for both Topologies 1 and 2 for all device types.
Proposal 4: Coverage enhancement between base station and intermediate node, intermediate node and A-IoT device in Topology 2 should be investigated for all device types.
[RAN1-led]: Ambient IoT Proposal
Topology 2: BS ↔ intermediate node ↔ Ambient IoT device

## Slide 4
Proposal 1: Unified message structure for both 2-step/4-step CBRA for both topologies 1 and 2
Proposal 2: A-IoT message signal design including sleep mode to optimize the energy consumption for Device 2
Proposal 3: A-IoT paging and random access for Topology 2
[RAN2-led]: Ambient IoT Proposals

## Slide 5
sushmitag@tejasnetworks.com